## Slide 1
FORTIGATE
Administrator Course
Foundations + Advanced • v1.5
Four days • 16 instructor-led blocks • theory with practical handoffs
Lab baseline: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
09:00–16:00 daily | Four 90-minute blocks per day
Editable theory deck • illustrative addressing • observable packet and protocol behavior
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Four-day instructor-led theory course; Days 1–2 Foundations; Days 3–4 Advanced
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.

## Slide 2
2
Four days build from packet behavior to integrated operations
Every 90-minute block reserves time for practice and discussion
DAY 1
09:00–10:30
Network Foundations & FortiGate Packet Flow
10:30–12:00
FortiGate Introduction & Initial Configuration
13:00–14:30
Segmentation, Zones & Firewall Policy Design
14:30–16:00
NAT, Logging & CLI Troubleshooting
DAY 2
09:00–10:30
Routing Fundamentals & Route Selection
10:30–12:00
Object Management & Policy Design Best Practices
13:00–14:30
Security Services & SSL Inspection
14:30–16:00
FortiGate Hardware Architecture, Monitoring & Operations
DAY 3
09:00–10:30
Route Selection, PBR & OSPF
10:30–12:00
BGP Fundamentals & Practical Use
13:00–14:30
IPsec VPN Architecture & ADVPN
14:30–16:00
VPN Troubleshooting & Operational Validation
DAY 4
09:00–10:30
FortiClient Architecture & EMS Awareness
10:30–12:00
FortiGate High Availability Fundamentals
13:00–14:30
Fortinet SD-WAN & Design Considerations
14:30–16:00
Performance Optimization, Advanced Troubleshooting & Capstone
COURSE MAP
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Four 90-minute blocks each day; Days 1–2 Foundations; Days 3–4 Advanced; Practice and debrief are protected within every block
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.

## Slide 3
003
Validated training lab: Azure underlay and Student N pods
FortiOS 7.6.7 • October 2026 validated endpoint and routed-path baseline
3
INSTRUCTOR FGT
port1 10.0.0.4
transit
LINUX ROUTER NVA
10.0.40.4
INSTR. SERVICES
p2 10.0.30.4 • p3 10.0.10.4
underlay
AZURE UNDERLAY
Shared Internet breakout / NAT
routed
STUDENT N FGT
p1/WAN 10.N.0.4
p2/LAN .10.4 • p3/DMZ .20.4
LAN / DMZ
LINUX ENDPOINTS
client 10.N.10.10
DMZ 10.N.20.10
FUTURE PROTECTED OVERLAY
Student LAN/DMZ ↔ instructor services through IPsec/ADVPN
EXAMPLES
S01: 10.1.0/24 | 10.1.10/24 | 10.1.20/24 • S02: 10.2.0/24 | 10.2.10/24 | 10.2.20/24 • Student N substitutes N.
Notes: Current lab source of truth: Architecture.md, Deployment.md and Instructor-Guide.md. Validated baseline: Student N FortiGate p1 10.N.0.4, p2 10.N.10.4, p3 10.N.20.4; client 10.N.10.10; DMZ 10.N.20.10; Transit NVA 10.0.40.4; Instructor FortiGate p1 10.0.0.4, p2 10.0.30.4, p3 10.0.10.4. Student-to-Internet routed path is validated. The IPsec/ADVPN overlay remains future work. Guacamole access is TBD.

## Slide 4
DAY 1 • 09:00–10:30
Network Foundations & FortiGate Packet Flow
Foundations • Day 1 of 2
LEARNING OBJECTIVES
• Explain packet fields, DNS, TCP/UDP and forwarding decisions
• Trace a new session through FortiGate decision stages
• Distinguish flow/proxy inspection and locate implicit deny
PREREQUISITES + PRACTICE RESERVE
• Basic IPv4 subnetting
• Illustrative topology on slide 3
• GUI/CLI access is demonstrated in the next block
Teach ~54 min • reserve ~36 min for guided activity, discussion and debrief
004
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain packet fields, DNS, TCP/UDP and forwarding decisions; Trace a new session through FortiGate decision stages; Distinguish flow/proxy inspection and locate implicit deny
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.

## Slide 5
5
The five-tuple is the identity of a unidirectional flow
FortiGate session matching begins with concrete packet fields, not application names
FIELD | EXAMPLE | WHY IT MATTERS
Source IP | 10.10.10.25 | Which host originated the packet
Destination IP | 203.0.113.80 | Which host the packet targets
Source port | 51514 | Ephemeral client-side transport port
Destination port | 443 | Service endpoint; not proof of the application
Protocol | TCP (6) | Separates TCP from UDP/ICMP flows
SESSION CONSEQUENCE
The return packet reverses source and destination. FortiGate associates it with the existing session and applies the stored policy, NAT and security state.
Worked packet
10.1.10.10:51514 → 203.0.113.80:443 / TCP Return: 203.0.113.80:443 → translated client tuple
Validate: diagnose sys session filter src 10.1.10.10; diagnose sys session list
005 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Source and destination IP locate endpoints; Source and destination ports identify transport sockets; Protocol distinguishes TCP, UDP, ICMP and others; Reverse traffic is associated with the created session
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.

## Slide 6
6
DNS turns names into routable destinations
01
Client query
02
Resolver cache
03
Authority lookup
04
Answer + TTL
What to observe
• Recursive resolution follows cache, root, TLD and authoritative data as needed
• A/AAAA answers provide addresses; TTL controls cache lifetime
• DNS success does not prove policy or route success to the returned address
INSTRUCTOR DEMONSTRATION
Use a filtered packet capture on UDP/TCP 53 and compare query, response and TTL.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
006 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Client asks a resolver, not the authoritative server directly in most enterprise designs; Recursive resolution follows cache, root, TLD and authoritative data as needed; A/AAAA answers provide addresses; TTL controls cache lifetime; DNS success does not prove policy or route success to the returned address
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.

## Slide 7
007
TCP handshake creates state that return traffic can reuse
New connection: client 10.1.10.10:51514 → server 203.0.113.80:443
7
CLIENT
10.1.10.10:51514
FORTIGATE
policy 12 • session 0042
SERVER
203.0.113.80:443
1 SYN →
1 SYN →
2 ← SYN-ACK
2 ← SYN-ACK
3 ACK →
3 ACK →
SESSION CREATED
The entry stores policy, route, NAT and TCP state. Return packets match the reverse tuple.
LESSON
Stateful inspection does not “trust replies”; it associates the reverse five-tuple with an existing allowed session.
Notes: Expected result: after the SYN is accepted, diagnose sys session list shows the original and reply tuples; reply packet/byte counters increase after SYN-ACK. Source: FortiOS 7.6.7 Administration Guide — Sessions and TCP session handling.

## Slide 8
008
New sessions take the full path; established sessions reuse state
Simplified teaching view—feature/platform exceptions exist
8
NEW SESSION
Ingress
packet + interface
Route/PBR
candidate egress
Policy
first matching rule
NAT
original ↔ translated
Inspection
profiles as configured
Create session
store decisions
ESTABLISHED SESSION
Reverse tuple
reply packet
Session lookup
policy/NAT/egress state
Forward + inspect
according to stored state
Update counters
bytes / timeout / TCP
Local-in traffic, proxy behavior, tunnels, hardware offload and special features can add or change stages.
LESSON
Use this as a troubleshooting map, not as a universal implementation pipeline.
Notes: Technical question for instructor review: compare this simplified teaching order with the exact FortiOS 7.6.7 “Life of a packet” documentation and features enabled in the Azure lab. Source: FortiOS 7.6.7 Administration Guide — Life of a packet, policy routes, firewall policy, NAT and security profiles.

## Slide 9
009
First HTTPS session
9
01
SYN enters LAN
02
Route selects WAN
03
Policy 12 accepts
04
SNAT creates reply tuple
05
SYN-ACK matches session
EXPECTED RESULT
A session entry shows the original tuple and the return packets increment the reply counters.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Packet arrives on LAN; source/destination and ingress interface are known; Route lookup identifies WAN and next hop; First-match policy permits traffic and applies SNAT; Session records original and translated tuples; security profiles inspect as configured
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.

## Slide 10
010
Common mistakes—and how to correct them
10
MISTAKE
CORRECTION — AND WHY IT HELPS
DNS success proves the application path
Test the returned IP and TCP handshake; DNS only proves name resolution.
Port 443 proves HTTPS
Inspect the handshake/application state; a port number identifies a socket, not the application.
Policy is the only forwarding decision
Check route and return path first; policy cannot repair an absent route.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.

## Slide 11
11
Troubleshooting workflow: narrow the failed decision
01
Reproduce one flow and record its five-tuple
02
Check route and neighbor reachability
03
Identify the matched policy and NAT decision
04
Confirm session creation and reverse traffic
05
Use filtered sniffer/debug only if route, session and logs are inconclusive
What to observe
• Identify the matched policy and NAT decision
• Confirm session creation and reverse traffic
• Use filtered sniffer/debug only if route, session and logs are inconclusive
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
011 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Reproduce one flow and record its five-tuple; Check route and neighbor reachability; Identify the matched policy and NAT decision; Confirm session creation and reverse traffic; Use filtered sniffer/debug only if earlier state/output is inconclusive
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.

## Slide 12
12
Practical handoff: Packet Flow and Session Visibility
• START / PREREQUISITES: Student N pod reachable; Student N addressing from slide 3; read-only diagnostics enabled.
• CHANGE / INVESTIGATE: Predict and trace one LAN-to-DMZ TCP flow: route, policy ID, five-tuple, session and both packet directions.
• EXPECTED RESULT: The predicted policy and route match; original/reply counters increase and the capture shows both directions.
• CLEANUP / RESET: Stop filters/debug and clear only the named test session; do not alter shared management access.
• DELIVERY: Hands-on with the validated Linux client and DMZ server; instructor capture fallback if a pod is unavailable.
PLANNED EXERCISE
Predict and trace one LAN-to-DMZ TCP flow: route, policy ID, five-tuple, session and both packet directions.
EXPECTED RESULT
The predicted policy and route match; original/reply counters increase and the capture shows both directions.
DELIVERY MODE
Hands-on; capture fallback
012 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: Exercise: Packet Flow and Session Visibility (hands-on; instructor capture fallback).
Preparation: assign Student N endpoint host IPs only after the Linux endpoints exist; preserve management access.
Core steps: predict five-tuple and path; generate one LAN-to-DMZ TCP flow; inspect route, policy ID, session original/reply tuples, packet capture and log.
Answer key: the chosen route and policy must match the actual ingress/egress interfaces; both session directions and counters increase. A one-way counter points to return-path, policy, endpoint or asymmetric-flow investigation.
Reset: stop debug/capture, clear filters, remove only the test session.

## Slide 13
13
Knowledge check — explain the result
QUESTION 1
• Which five values identify a TCP/UDP flow?
QUESTION 2
• Why can a return packet bypass a second full policy decision?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
013 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Which five values identify a TCP/UDP flow?; Why can a return packet bypass a second full policy decision?
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: Which five values identify a TCP/UDP flow?
A: Source IP, destination IP, source port, destination port and IP protocol.
Q: Why can a return packet bypass a second full policy decision?
A: It matches established session state containing the stored forwarding, policy and NAT decisions.

## Slide 14
DAY 1 • 10:30–12:00
FortiGate Introduction & Initial Configuration
Foundations • Day 1 of 2
LEARNING OBJECTIVES
• Navigate the FortiOS GUI and CLI safely
• Read and change configuration with contextual help
• Back up, restore and verify a disposable student FortiGate
PREREQUISITES + PRACTICE RESERVE
• Assigned Student N appliance and credentials
• Access URL/SSH target supplied as <TBD>
• Backup destination or browser download location prepared
Teach ~55 min • reserve ~35 min for guided CLI activity and debrief
014
Notes: Block 2 orientation. Guacamole deployment/access is not established in the current architecture documents; use <access-url>, <username> and <credential-source> placeholders. Keep management interfaces, routes and shared instructor infrastructure unchanged. Official references: FortiOS 7.6.7 Administration Guide—Using the CLI, configuration backups/restores and firmware; FortiOS 7.6.7 CLI Reference.

## Slide 15
FORTIGATE ADMINISTRATOR COURSE
015 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Reach the assigned FortiGate—and verify where you landed
15
ACCESS
• GUI: https://<student-N-access-url>
• CLI: ssh <username>@<student-N-target>
• Guacamole: TBD—not yet documented
IDENTIFY
get system status
• Confirm FortiOS v7.6.7
• Confirm hostname, serial/model and mode
• Use only your assigned Student N appliance
LAB IDENTITY
port1 10.N.0.4
port2 10.N.10.4
port3 10.N.20.4
client 10.N.10.10 • DMZ 10.N.20.10
Stop if the prompt, hostname or addresses do not match the assigned pod.
Notes: Starting access details remain instructor placeholders because the current sources do not establish final URLs, credentials or Guacamole deployment. Demonstrate both GUI and SSH/console only after the instructor confirms the supported access route. `get system status` is inspection, but its output may reveal serial/licensing details; do not share screenshots externally.

## Slide 16
FORTIGATE ADMINISTRATOR COURSE
016 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
The FortiGate CLI is not the Linux shell
16
FORTIOS CLI
• Prompt identifies the FortiGate context
• Commands include config, show, get, execute and diagnose
• Configuration is hierarchical—not files under /etc
• Use ? and context-aware completion
LINUX CLIENT / DMZ SHELL
• Prompt belongs to 10.N.10.10 or 10.N.20.10
• Commands include ip, ping, curl, dig and traceroute
• Generates traffic through the FortiGate
• Does not configure FortiOS
A successful FortiGate-local ping or telnet tests local-out traffic—not the student client’s forward policy.
Notes: Use a live prompt comparison. FortiOS commands are not Cisco IOS or Linux commands. Avoid teaching shell concepts such as cd, ls, sudo or editing files. The Linux client at 10.N.10.10 is the authoritative source for forwarded-client tests.

## Slide 17
FORTIGATE ADMINISTRATOR COURSE
017 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Command families signal intent—but not safety
17
FAMILY | PRIMARY USE | 7.6.7 EXAMPLE | CLASS
config | Enter configuration context | config firewall address | CONFIG CHANGE
show | Inspect configuration | show system interface port2 | INSPECTION
get | Settings or runtime, by path | get system status | INSPECTION
execute | Perform an operational action | execute ping 10.0.40.4 | MAY CHANGE / DISRUPT
diagnose | Inspect/debug internal operation | diagnose sys session list | INSPECT OR DISRUPT
Read the complete command and parameters; family name alone never proves “read-only.”
Notes: Official FortiOS CLI documentation groups configuration, display, operational and diagnostic commands, but risk depends on the exact subcommand and parameters. `execute` includes harmless tests and disruptive actions; `diagnose` includes read-only inspection and debug/session operations that can affect performance or state.

## Slide 18
FORTIGATE ADMINISTRATOR COURSE
018 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Context transitions turn a safe object into configuration
18
ANNOTATED CLI • replace N with your pod number
config firewall address
edit "student0N-temp-cli"
set subnet 10.N.10.10 255.255.255.255
set comment "temporary CLI exercise"
next
end
show firewall address "student0N-temp-cli"
CONTEXT
• config → enter the address table
• edit → select/create an object identifier
• set → assign a value
• next → commit this table entry
• end → leave configuration context
• show → inspect the resulting object
[CHANGE] Create only the dedicated temporary object; do not edit interfaces, routes or policies.
Notes: Use a student-specific name such as student01-temp-cli. In a table, `edit <identifier>` selects or creates an entry; `next` finishes the entry and returns to the table; `end` exits configuration mode. The subnet command uses the documented client IP /32. Cleanup is `config firewall address`, `delete "student0N-temp-cli"`, `end`. Confirm no policy references the object before deletion.

## Slide 19
FORTIGATE ADMINISTRATOR COURSE
019 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Tables have entries; singleton sections have settings
19
TABLE
config firewall address
• Contains named objects
• edit "name" selects one entry
• next returns to the table
• delete "name" removes an entry
SINGLETON
config system global
• One section—not a list of objects
• set and unset change settings
• No object identifier required
• end returns to the top prompt
NESTED CONTEXT
config ... edit ... config ...
• Prompt/help changes at every level
• Commands available here may not exist at top level
• Use end to leave the configuration tree
unset restores a setting to its default behavior; it is still a configuration change.
Notes: FortiOS CLI Reference identifies which branches are tables and the syntax for each setting. Avoid assuming that every `config` branch supports `edit`. Nested contexts exist in policies and profiles; use contextual help instead of memorizing paths from another release.

## Slide 20
FORTIGATE ADMINISTRATOR COURSE
020 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Discover commands from the current context
20
AT THE TOP PROMPT
? config ? get ? diagnose ?
INSIDE config firewall address
? edit ? set ? show ?
• Question-mark help lists valid commands/options at that point.
• Tab completion expands an unambiguous keyword.
• Model, build, feature state and admin permissions affect availability.
• Do not assume Cisco or Linux abbreviations and behavior.
[INSPECTION] Read help before entering a parameter that may change state.
Notes: Official CLI Reference: use `?` to verify available commands and options; commands can vary by FortiGate model, build, feature state and permissions. Demonstrate help at top level and within `config firewall address`. Completion behavior should be shown live on the 7.6.7 lab rather than described as Cisco-style shorthand.

## Slide 21
FORTIGATE ADMINISTRATOR COURSE
021 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Use one interface to separate configuration from runtime
21
SHOW
SHOW FULL-CONFIGURATION
GET
show system interface port2
show full-configuration system interface port2
get system interface physical
• Configured values that differ from defaults
• Best concise configuration review
• All configured fields plus default values
• Useful when absence from show is ambiguous
• Operational interface state across the system
• Link/runtime output—not a restorable config
A show text dump is useful for review, but it is not automatically a complete, encrypted, restorable backup.
Notes: FortiOS `show` presents configured values, generally omitting defaults; `show full-configuration` includes default-valued settings. `get` meaning depends on command/context and is commonly used for operational state. Demonstrate output on port2 (10.N.10.4) without changing it. Do not paste `show` output as a substitute for a supported configuration backup.

## Slide 22
FORTIGATE ADMINISTRATOR COURSE
022 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Applying, persisting and exporting are different actions
22
1
EDIT
set / unset / next / end
2
ACTIVE STATE
Accepted changes can affect traffic
3
PERSISTENCE
cfg-save mode controls storage
4
BACKUP FILE
Export creates a separate recovery file
INSPECT—DO NOT CHANGE IN CLASS
show full-configuration system global | grep cfg-save
Manual mode uses execute cfg save; there is no universal “copy running-config startup-config” workflow.
Notes: FortiOS supports configuration save modes under `config system global` (`cfg-save`). Do not change the cohort setting during class. In automatic mode, accepted configuration is persisted automatically. In manual mode, `execute cfg save` is required to save persistent state. Revert mode has additional timeout behavior and should remain an instructor topic. Exporting a backup is separate from persistence.

## Slide 23
FORTIGATE ADMINISTRATOR COURSE
023 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Back up from FortiGate to controlled storage
23
STUDENT N FGT
configuration scope: global or VDOM-aware
BACKUP FILE
student0N-20261004.conf optional encryption/password
DESTINATION
browser download or provisioned SFTP storage
CLI TRANSFER—ONLY AFTER THE INSTRUCTOR PROVISIONS SFTP
execute backup config sftp <file.conf> <sftp-server> <username> <password>
• GUI: use the configuration Backup action and record where the browser saved the file.
• Protect credentials and backup files; configs can contain sensitive data.
• A show text dump is not automatically a complete restorable backup.
Notes: Official 7.6.7 CLI workflow shown: `execute backup config sftp <backup_file> <sftp_server> <username> <password>`. The current lab documents do not define an SFTP service, hostname, account or storage path, so use placeholders and provision/test the service before delivery. If SFTP is not available, use the supported GUI configuration Backup action and a controlled browser download. Confirm whether global/VDOM scope and encrypted backup options are appropriate. Do not display real passwords during projection.

## Slide 24
FORTIGATE ADMINISTRATOR COURSE
024 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Restore moves a reviewed file back to a disposable appliance
24
CONTROLLED STORAGE
review filename, source pod, encryption and integrity
COMPATIBILITY GATE
platform/model • build/upgrade path • VDOM • pod addresses
STUDENT N FGT
upload/transfer → restore → interruption/reboot → verify
POTENTIALLY DISRUPTIVE • INSTRUCTOR-SUPERVISED
execute restore config sftp <file.conf> <sftp-server> <username> <password>
• GUI alternative: select the reviewed backup file with the configuration Restore action.
• Expect management interruption or reboot; verify build, interfaces, routes, DNS and client forwarding afterward.
• Never restore another pod’s export before reviewing Student N addresses and dependencies.
Notes: Live restoration is restricted to a disposable student FortiGate with a tested recovery path and instructor supervision. The current documents do not provision SFTP; the CLI syntax is a template until a reachable server is tested. Before restore, compare model/platform, FortiOS build/upgrade path, VDOM scope and pod-specific addresses. Preserve out-of-band/emergency access. After reboot/interruption, verify `get system status`, interfaces, routes, DNS, management reachability and a forwarded client test. Store exact recovery steps in the instructor runbook.

## Slide 25
FORTIGATE ADMINISTRATOR COURSE
025 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Firmware maintenance is a controlled reboot—not a file copy
25
1
PREPARE
Release notes • supported upgrade path • config backup
2
SELECT IMAGE
Correct FortiGate-VM platform image from Fortinet
3
INSTALL / REBOOT
Upload alone is not installation; confirm upgrade triggers reboot
4
POST-CHECK
Build • interfaces • routes • logs • client traffic
LAB RULE
The lab already runs FortiOS 7.6.7. Use a demonstration/walkthrough unless the instructor supplies a tested alternate image and recovery procedure.
Upgrading an existing FGVM is different from replacing the Azure Marketplace VM image.
Notes: Instructor-only procedure: obtain the exact image from the authorized Fortinet support channel; read 7.6.7 release notes and the supported upgrade-path guidance; verify platform/model and licensing; export configuration; preserve recovery access; use the supported GUI firmware upload/upgrade workflow; confirm installation/reboot; verify the running build and data path. Do not run a cohort-wide upgrade/downgrade. Uploading/selecting an image is distinct from confirming installation. Replacing an Azure Marketplace VM image is an infrastructure lifecycle operation, not the same FortiOS firmware workflow.

## Slide 26
FORTIGATE ADMINISTRATOR COURSE
026 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
First checks move from appliance state to forwarded traffic
26
01
BUILD / UPTIME
get system status get system performance status
02
INTERFACES
get system interface physical
03
ROUTING / DNS
get router info routing-table all get system dns
04
LOCAL TEST
execute ping 10.0.40.4
05
CLIENT TEST
from 10.N.10.10: ping / dig / curl / traceroute
Known Student01 path: 10.1.10.10 → 10.1.10.4 → 10.0.40.4 → 10.0.0.4 → Internet
Local FortiGate success does not prove that forwarded client traffic matches a policy.
Notes: Use Student01 for the worked path and Student N for reuse. The current architecture validates client 10.1.10.10 → Student FG 10.1.10.4 → Transit NVA 10.0.40.4 → Instructor FG 10.0.0.4 → Internet. `execute ping` is local-out traffic. A Linux client ping/dig/curl/traceroute is the required forwarded test. Do not infer Guacamole availability.

## Slide 27
FORTIGATE ADMINISTRATOR COURSE
027 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Guided CLI exercise: inspect, create, back up and clean up
27
STARTING STATE
• Assigned Student N FortiGate on 7.6.7
• Management access works; baseline routes/interfaces untouched
• GUI download location or tested SFTP destination available
STUDENT TASK
• Run get system status and use ? in two contexts
• Create student0N-temp-cli for 10.N.10.10/32
• Inspect with show; export a dated backup
• Delete the temporary object
EXPECTED RESULT + CLEANUP
• Object displays the correct /32 and comment
• Backup exists at the recorded destination
• Object is absent after delete
• Management, baseline routes and shared infrastructure are unchanged
COMMAND CHECKPOINT
config firewall address → delete "student0N-temp-cli" → end → show firewall address "student0N-temp-cli"
[CHANGE] Dedicated address object only • [INSPECTION] help/show/status • [DISRUPTIVE] restore/firmware are not student tasks
Notes: Exercise duration 20–25 minutes. Exact starting state: assigned Student N FortiGate on 7.6.7; management access functioning; instructor baseline export retained; browser download location or tested SFTP service available. Students must not modify management interfaces, routes, policies, cfg-save mode or instructor resources. Expected: temporary object uses 10.N.10.10 255.255.255.255; backup filename includes pod and date; deletion succeeds because the object is not referenced. If `show firewall address "student0N-temp-cli"` after cleanup returns no object, cleanup is complete. Instructor checks the exported file location and retains/deletes it according to storage policy.

## Slide 28
DAY 1 • 13:00–14:30
Segmentation, Zones & Firewall Policy Design
Foundations • Day 1 of 2
LEARNING OBJECTIVES
• Choose LAN/WAN/DMZ boundaries using least privilege
• Explain FortiSwitch/FortiLink roles without assuming lab availability
• Build ordered policies from reusable objects and logging requirements
PREREQUISITES + PRACTICE RESERVE
• Block 1 routing/session concepts
• Known trust zones and application flows
• FortiSwitch hardware is instructor-demo only unless supplied
Teach ~54 min • reserve ~36 min for guided activity, discussion and debrief
028
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Choose LAN/WAN/DMZ boundaries using least privilege; Explain FortiSwitch/FortiLink roles without assuming lab availability; Build ordered policies from reusable objects and logging requirements
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.

## Slide 29
029
Segmentation permits named flows and denies everything else
Zones simplify references; they do not create isolation by themselves
29
LAN ZONE
10.1.10.0/24
DMZ ZONE
10.1.20.0/24
WAN
untrusted
GUEST ZONE
10.10.30.0/24
HTTPS 443 allowed
published HTTPS
DNS only
DENY
Policy intent
• LAN → DMZ: HTTPS only
• Guest → LAN/DMZ: denied
• WAN → DMZ: VIP + HTTPS
• Zone membership alone permits nothing
LESSON
Draw the permitted arrows first; each arrow becomes a narrowly scoped firewall policy and a positive/negative test.
Notes: Expected result: the HTTPS test matches the intended policy ID; a guest-to-DMZ test is denied. Source: FortiOS 7.6.7 Administration Guide — Zones and firewall policies.

## Slide 30
30
Zones simplify policy only when members share intent
• A zone groups interfaces for policy references and consistent treatment
• Do not combine interfaces with different trust or logging requirements
• Intra-zone traffic behavior must be explicitly understood and tested
• Naming should reveal function, not physical port number
ILLUSTRATIVE SCENARIO
Zone BRANCH-LANS can be useful; zone TRUSTED-MIX is usually ambiguous
EXPECTED RESULT
List each member and prove that one policy intent applies to all.
Expected observation
The test flow matches the intended policy; the denied flow is logged by the implicit or explicit deny.
030 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A zone groups interfaces for policy references and consistent treatment; Do not combine interfaces with different trust or logging requirements; Intra-zone traffic behavior must be explicitly understood and tested; Naming should reveal function, not physical port number
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.

## Slide 31
31
FortiLink joins FortiGate policy with managed switching
FORTIGATE
FORTILINK
FORTISWITCH
VLAN ENDPOINTS
Conceptual exercise: place users, voice, APs and servers into VLANs and policies
• FortiLink is the management/control connection for supported FortiSwitch deployments
• FortiGate can manage switch ports, VLANs and topology from the Security Fabric/LAN edge workflow
• Access, trunk and native VLAN choices remain layer-2 design decisions
• Model, FortiOS/FortiSwitchOS and topology support must be confirmed
Instructor demo only unless a compatible FortiSwitch, links and supported versions exist.
031 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: [OPTIONAL DEEP DIVE] Stable ID: D1-B03-S031
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: FortiLink is the management/control connection for supported FortiSwitch deployments; FortiGate can manage switch ports, VLANs and topology from the Security Fabric/LAN edge workflow; Access, trunk and native VLAN choices remain layer-2 design decisions; Model, FortiOS/FortiSwitchOS and topology support must be confirmed
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.

## Slide 32
32
First match wins: specificity and order are design tools
01
Ingress pair
02
Address match
03
Service/schedule
04
First match
05
Action + profiles
What to observe
• The first matching enabled policy supplies action, NAT, logging and profiles
• Broad rules above narrow rules can shadow intended controls
• Objects and groups reduce error when they have clear names and owners
INSTRUCTOR DEMONSTRATION
Use policy lookup/hit counters and logs to prove the matched policy.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
032 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A policy is evaluated in sequence for ingress/egress, addresses, service, schedule and other selectors; The first matching enabled policy supplies action, NAT, logging and profiles; Broad rules above narrow rules can shadow intended controls; Objects and groups reduce error when they have clear names and owners
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.

## Slide 33
033
Policy from a flow matrix
33
01
Name business flow
02
Create address/service objects
03
Order specific rule
04
Enable required logging
05
Test allow and deny
EXPECTED RESULT
The test flow matches the intended policy; the denied flow is logged by the implicit or explicit deny.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: State business flow: source zone, destination, service and owner; Create address/service objects with durable names; Order narrow exceptions before broad patterns; Enable the logging required for operations and audit
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.

## Slide 34
034
Common mistakes—and how to correct them
34
MISTAKE
CORRECTION — AND WHY IT HELPS
Use all objects to save time
Create named source, destination and service objects; scope becomes reviewable and reusable.
Put unlike interfaces in one zone
Group only interfaces with the same policy intent; zones do not create isolation.
Put broad allow above exceptions
Place specific rules first and use policy lookup; first match otherwise shadows them.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.

## Slide 35
35
Troubleshooting workflow: narrow the failed decision
01
Confirm ingress and expected egress interfaces
02
Resolve object membership to concrete IP/port values
03
Check policy order and shadowing
04
Inspect hit count and traffic log
05
Test an explicit negative case
What to observe
• Check policy order and shadowing
• Inspect hit count and traffic log
• Test an explicit negative case
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
035 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm ingress and expected egress interfaces; Resolve object membership to concrete IP/port values; Check policy order and shadowing; Inspect hit count and traffic log; Test an explicit negative case
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.

## Slide 36
36
Practical handoff: Build LAN-to-DMZ Segmentation
• START / PREREQUISITES: Student N p2 LAN and p3 DMZ configured; validated Linux client/server available.
• CHANGE / INVESTIGATE: Create LAN/DMZ objects and least-privilege policies; test one allowed service and one denied flow.
• EXPECTED RESULT: Allowed traffic matches the intended policy and logs; the denied flow is blocked and identifiable.
• CLEANUP / RESET: Remove temporary broad rules/test objects; retain the approved segmented baseline.
• DELIVERY: Hands-on on the assigned pod; policy-and-log walkthrough fallback.
PLANNED EXERCISE
Create LAN/DMZ objects and least-privilege policies; test one allowed service and one denied flow.
EXPECTED RESULT
Allowed traffic matches the intended policy and logs; the denied flow is blocked and identifiable.
DELIVERY MODE
Hands-on; walkthrough fallback
036 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: Exercise: Build LAN-to-DMZ Segmentation (hands-on when endpoints exist).
Preparation: planned Linux LAN client/DMZ server, assigned host IPs, and baseline policy backup.
Answer key: only the assigned service from LAN to DMZ is accepted and logged; unrelated service is denied. Objects use Student N subnets, not invented host addresses.
Reset: remove temporary broad policy or test objects and retain the approved least-privilege baseline.

## Slide 37
37
Knowledge check — explain the result
QUESTION 1
• What decides which of two matching policies is used?
QUESTION 2
• When is a zone a poor abstraction?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
037 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What decides which of two matching policies is used?; When is a zone a poor abstraction?
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Knowledge check answer key:
Q: What decides which of two matching policies is used?
A: The first enabled policy in sequence that matches all selectors.
Q: When is a zone a poor abstraction?
A: When member interfaces have different trust, logging or policy intent.

## Slide 38
DAY 1 • 14:30–16:00
NAT, Logging & CLI Troubleshooting
Foundations • Day 1 of 2
LEARNING OBJECTIVES
• Trace SNAT/PAT, DNAT/VIP and hairpin flows in both directions
• Select Traffic, Event and Security logs for the question asked
• Use session, sniffer and debug-flow diagnostics safely
PREREQUISITES + PRACTICE RESERVE
• Routing and policy fundamentals
• A test client and reachable service
• Authorization to clear sessions or enable debug
Teach ~56 min • reserve ~34 min for guided activity, discussion and debrief
038
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Trace SNAT/PAT, DNAT/VIP and hairpin flows in both directions; Select Traffic, Event and Security logs for the question asked; Use session, sniffer and debug-flow diagnostics safely
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.

## Slide 39
039
SNAT/PAT changes the source tuple—and reverses it for the reply
Illustrative outbound HTTPS session
39
CLIENT
10.1.10.10:51514
original
FORTIGATE
SNAT/PAT session
translated
SERVER
203.0.113.80:443
OUTBOUND
10.1.10.10:51514 → 203.0.113.80:443
WIRE TUPLE
198.51.100.2:62001 → 203.0.113.80:443
REPLY: 203.0.113.80:443 → 198.51.100.2:62001 • FortiGate reverses to 10.1.10.10:51514
LESSON
Record both directions: NAT succeeds only when the return packet matches the translated reply tuple.
Notes: Expected result: the session lists original and reply tuples; WAN capture shows 198.51.100.2:62001 while LAN capture shows 10.1.10.10:51514. Source: FortiOS 7.6.7 Administration Guide — Source NAT and sessions.

## Slide 40
040
A VIP translates the published destination before forwarding
Conceptual example — publication flow; endpoint host addresses are placeholders
40
EXTERNAL CLIENT
<external client IP>:53000
public tuple
VIP ON FORTIGATE
<published IP>:443
→ 10.1.20.10:8443
mapped tuple
10.1.20.10:8443
10.1.20.10:8443
FIREWALL POLICY
• Ingress: WAN
• Destination: VIP object
• Service: HTTPS
• Egress route: DMZ
Reply translation
10.1.20.10:8443 → client becomes <published IP>:443 → client
LESSON
A VIP defines translation; the firewall policy, route and return path still decide whether the service works.
Notes: Expected result: WAN capture targets 198.51.100.10:443, DMZ capture targets 10.1.20.10:8443, and the traffic log shows the VIP policy ID. Source: FortiOS 7.6.7 Administration Guide — Virtual IPs and DNAT.

## Slide 41
041
Hairpin access uses the public VIP from an internal network
Internal client and server remain in separate segments
41
LAN CLIENT
10.1.10.10:51514
public address
FORTIGATE VIP
198.51.100.10:443 → 10.1.20.10:8443
DNAT + policy
DMZ SERVER
10.1.20.10:8443
Why source NAT may be required
• Without SNAT, the server may reply directly to the client
• Direct reply bypasses the FortiGate session and breaks symmetry
• SNAT forces the reply through FortiGate for reverse translation
• Split DNS can avoid hairpinning when appropriate
Expected packet path
LAN → FortiGate → DMZ DMZ → FortiGate → LAN
LESSON
Hairpin troubleshooting must check DNAT, optional SNAT, policy and the server’s return route as one session.
Notes: Expected result: one session shows the VIP destination mapping and, when required by the design, a translated source that returns through FortiGate. Source: FortiOS 7.6.7 Administration Guide — Hairpin NAT / VIP examples.

## Slide 42
42
Logs and CLI answer different layers of the incident
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
diagnose sys session filter clear diagnose sys session filter src <client-ip> diagnose sys session list diagnose sniffer packet any "host <ip> and port <port>" 4 0 l diagnose debug reset
READ THE OUTPUT
• Traffic logs show policy, action, interfaces, addresses, ports and bytes
• Event logs show system/admin/HA/routing events
• Security logs show profile detections and actions
• Session table shows live state; sniffer shows packets; debug flow explains decisions
Safe operation
A deny without a session points to policy/route processing; a session without replies points downstream/return path
042 • DAY 1 • BLOCK 04 • NAT, Logging & CLI Troubleshooting
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Traffic logs show policy, action, interfaces, addresses, ports and bytes; Event logs show system/admin/HA/routing events; Security logs show profile detections and actions; Session table shows live state; sniffer shows packets; debug flow explains decisions
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.

## Slide 43
043
NAT in both directions
43
01
Record original tuple
02
Read translated session tuple
03
Capture LAN side
04
Capture WAN/server side
05
Match reply translation
EXPECTED RESULT
The session shows original and translated tuples, and packet captures show the reverse translation on the reply.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Record original client/server tuple; Record translated tuple at WAN or server side; Match the return packet to the reply direction; Confirm log policy ID and byte counters increase
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.

## Slide 44
044
Common mistakes—and how to correct them
44
MISTAKE
CORRECTION — AND WHY IT HELPS
Check only the public side of DNAT
Capture WAN and DMZ sides; comparing tuples shows whether the VIP translated and forwarded.
Run unfiltered debug flow
Filter by address/port and bound the capture; this prevents noise and operational impact.
Clear all sessions after a change
Use a new five-tuple or narrow session filter; broad clearing disrupts unrelated users.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.

## Slide 45
45
Troubleshooting workflow: narrow the failed decision
01
Define the expected original and translated tuples
02
Check route and matching policy/VIP
03
Inspect live session state
04
Capture at two interfaces to localize loss
05
Run filtered debug flow; disable/reset immediately
What to observe
• Inspect live session state
• Capture at two interfaces to localize loss
• Run filtered debug flow; disable/reset immediately
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
045 • DAY 1 • BLOCK 04 • NAT, Logging & CLI Troubleshooting
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Define the expected original and translated tuples; Check route and matching policy/VIP; Inspect live session state; Capture at two interfaces to localize loss; Run filtered debug flow; disable/reset immediately
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.

## Slide 46
46
Practical handoff: Publish, NAT and Troubleshoot a DMZ Service
• START / PREREQUISITES: Student N DMZ service host placeholder assigned by instructor; inbound test source and logging prepared.
• CHANGE / INVESTIGATE: Create a VIP and policy, test publication, then diagnose one safe NAT/policy/return-path fault.
• EXPECTED RESULT: The external tuple translates to the assigned DMZ server placeholder; logs/captures show the correct policy and return traffic.
• CLEANUP / RESET: Remove the test VIP/fault or restore the saved baseline; stop captures and session filters.
• DELIVERY: Hands-on only with the planned DMZ server; instructor packet-trace fallback.
PLANNED EXERCISE
Create a VIP and policy, test publication, then diagnose one safe NAT/policy/return-path fault.
EXPECTED RESULT
The external tuple translates to the assigned DMZ server placeholder; logs/captures show the correct policy and return traffic.
DELIVERY MODE
Hands-on when DMZ server exists
046 • DAY 1 • BLOCK 04 • NAT, Logging & CLI Troubleshooting
Notes: Exercise: Publish, NAT and Troubleshoot a DMZ Service.
Preparation: assign the DMZ server host IP and published test IP/port from the lab worksheet; do not use the documentation addresses from conceptual slides.
Fault choices: wrong VIP mapping, wrong policy destination/service, missing DMZ return route, or stale session. Inject one only.
Answer key: WAN-side tuple translates to the assigned DMZ server; policy ID and captures match; reply translation is visible.
Reset: remove the fault/test VIP as directed, clear only test sessions, stop capture/debug.

## Slide 47
47
Knowledge check — explain the result
QUESTION 1
• Which log best proves the firewall policy and NAT result for a connection?
QUESTION 2
• What must be done after a debug-flow demonstration?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
047 • DAY 1 • BLOCK 04 • NAT, Logging & CLI Troubleshooting
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Which log best proves the firewall policy and NAT result for a connection?; What must be done after a debug-flow demonstration?
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: Which log best proves the firewall policy and NAT result for a connection?
A: The Traffic log, correlated with session and packet state/output.
Q: What must be done after a debug-flow demonstration?
A: Disable debug output and reset filters/state; retain only necessary state/output.

## Slide 48
DAY 2 • 09:00–10:30
Routing Fundamentals & Route Selection
Foundations • Day 2 of 2
LEARNING OBJECTIVES
• Interpret static and default routes in the routing table
• Explain longest prefix, administrative distance, priority and ECMP
• Validate next-hop and return-path behavior
PREREQUISITES + PRACTICE RESERVE
• Day 1 five-tuple and interface concepts
• Illustrative addresses from slide 3
• Two next hops for ECMP demonstration if available
Teach ~52 min • reserve ~38 min for guided activity, discussion and debrief
048
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Interpret static and default routes in the routing table; Explain longest prefix, administrative distance, priority and ECMP; Validate next-hop and return-path behavior
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.

## Slide 49
49
Route selection starts with the most specific prefix
CANDIDATES
• 10.2.10.0/24 via VPN, distance 10
• 10.20.0.0/16 via WAN2, distance 5
• 0.0.0.0/0 via WAN1, distance 10
WINNER
• The /24 wins by longest prefix
• Distance is compared only among equal prefixes
• Return path requires an independent lookup
KEY DISTINCTION
10.20.10.25 matches /24 over /16 over /0
049 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Connected, static and dynamic routes can all be candidates; Longest prefix match chooses the narrowest destination range first; Administrative distance compares route sources for the same prefix; Priority can break ties within the same route source; verify exact behavior in the deployed build
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.

## Slide 50
50
A default route is a last-resort candidate
• 0.0.0.0/0 matches any IPv4 destination but loses to every more-specific route
• The next hop must be reachable on the configured interface
• Multiple defaults can provide preference or ECMP depending on distance/priority and state
• Default gateway on a host points to FortiGate; default route on FortiGate points upstream
ILLUSTRATIVE SCENARIO
Student01 default gateway 10.1.10.4; shared Internet breakout is provided by the instructor FortiGate
EXPECTED RESULT
Test gateway reachability with source interface/address specified.
Expected observation
The routing table installs the most-specific eligible route with the expected next hop.
050 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: 0.0.0.0/0 matches any IPv4 destination but loses to every more-specific route; The next hop must be reachable on the configured interface; Multiple defaults can provide preference or ECMP depending on distance/priority and state; Default gateway on a host points to FortiGate; default route on FortiGate points upstream
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.

## Slide 51
51
Administrative distance expresses source trust, not path quality
• Lower distance is preferred for equal prefixes
• Different protocols have defaults; explicit changes should be documented
• A lower distance does not fix an unreachable next hop
• Use SD-WAN/health logic for measured service quality rather than abusing distance
ILLUSTRATIVE SCENARIO
Conceptual route-choice example; a second WAN path is not deployed in the base lab
EXPECTED RESULT
Inspect both protocol database and active routing table.
Expected observation
The routing table installs the most-specific eligible route with the expected next hop.
051 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Lower distance is preferred for equal prefixes; Different protocols have defaults; explicit changes should be documented; A lower distance does not fix an unreachable next hop; Use SD-WAN/health logic for measured service quality rather than abusing distance
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.

## Slide 52
52
ECMP installs equal-cost next hops; sessions choose a path
CLIENT FLOWS
FORTIGATE ECMP HASH
CONCEPTUAL PATH A / PATH B
Optional second path: two equal defaults distribute new sessions; one session does not split packet by packet
• Routes must be equal under relevant selection criteria
• A session is normally pinned to one selected next hop
• Per-packet assumptions are unsafe; hashing and platform behavior require confirmation
• Symmetry, NAT and upstream state affect failover outcomes
Generate multiple five-tuples and compare the egress interface recorded in each session.
052 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Routes must be equal under relevant selection criteria; A session is normally pinned to one selected next hop; Per-packet assumptions are unsafe; hashing and platform behavior require confirmation; Symmetry, NAT and upstream state affect failover outcomes
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.

## Slide 53
053
Candidate route selection
53
01
List matching prefixes
02
Choose longest prefix
03
Compare distance for ties
04
Resolve next hop
05
Check return route
EXPECTED RESULT
The routing table installs the most-specific eligible route with the expected next hop.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: List every matching prefix; Choose longest prefix; For equal prefixes compare distance then applicable priority/metric; Confirm next-hop/interface state and perform return lookup
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.

## Slide 54
054
Common mistakes—and how to correct them
54
MISTAKE
CORRECTION — AND WHY IT HELPS
Compare distance across different prefixes
Choose longest prefix first; distance is compared among equal prefixes.
Assume ECMP splits each packet
Generate multiple sessions; ECMP generally selects per flow/session.
Ignore the reverse route
Run a lookup for the client prefix; the reply uses an independent decision.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.

## Slide 55
55
Troubleshooting workflow: narrow the failed decision
01
Look up the exact destination
02
Verify the selected prefix and next hop
03
Test next-hop reachability from the expected source
04
Check policy/session egress
05
Repeat lookup for return destination
What to observe
• Test next-hop reachability from the expected source
• Check policy/session egress
• Repeat lookup for return destination
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
055 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Look up the exact destination; Verify the selected prefix and next hop; Test next-hop reachability from the expected source; Check policy/session egress; Repeat lookup for return destination
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.

## Slide 56
56
Practical handoff: Route Selection and Failure Analysis
• START / PREREQUISITES: Student N connected routes plus instructor-provided candidate routes; protected tunnel route may be simulated.
• CHANGE / INVESTIGATE: Predict longest-prefix/distance choice, inspect the active route, then diagnose one withdrawn or less-preferred route.
• EXPECTED RESULT: Learners identify the winning route and explain the forwarding change after the controlled failure.
• CLEANUP / RESET: Restore the original route set and confirm management and default Internet breakout still work.
• DELIVERY: Hands-on with isolated routes; worked route-table scenario fallback.
PLANNED EXERCISE
Predict longest-prefix/distance choice, inspect the active route, then diagnose one withdrawn or less-preferred route.
EXPECTED RESULT
Learners identify the winning route and explain the forwarding change after the controlled failure.
DELIVERY MODE
Hands-on or route-table scenario
056 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: Exercise: Route Selection and Failure Analysis.
Preparation: provide isolated candidate routes and preserve the management/default-breakout path.
Answer key: longest prefix wins before distance/priority comparisons among equivalent prefixes. The active route and forwarding test must change consistently after the controlled withdrawal.
Reset: restore original routes and verify management plus shared Internet breakout.

## Slide 57
57
Knowledge check — explain the result
QUESTION 1
• Which criterion is evaluated before administrative distance?
QUESTION 2
• Why might equal routes not visibly split one connection?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
057 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Which criterion is evaluated before administrative distance?; Why might equal routes not visibly split one connection?
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: Which criterion is evaluated before administrative distance?
A: Longest prefix match.
Q: Why might equal routes not visibly split one connection?
A: Path selection is generally session/flow based, so one five-tuple remains pinned.

## Slide 58
DAY 2 • 10:30–12:00
Object Management & Policy Design Best Practices
Foundations • Day 2 of 2
LEARNING OBJECTIVES
• Create clear address, service and group objects
• Apply naming, reuse and ownership conventions
• Review policies for maintainability and operational clarity
PREREQUISITES + PRACTICE RESERVE
• Day 1 policy evaluation
• Agreed naming standard or instructor example
• Read-only review is sufficient for shared labs
Teach ~50 min • reserve ~40 min for guided activity, discussion and debrief
058
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Create clear address, service and group objects; Apply naming, reuse and ownership conventions; Review policies for maintainability and operational clarity
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
[OPTIONAL SUPPLEMENT — IDENTITY/AUTHENTICATION, 10–15 MINUTES IF NEEDED]
LDAP: FortiGate binds/searches a directory using a configured base DN and attributes; connectivity, TLS trust, bind permissions and group lookup are separate failure points. LDAP validates directory credentials/attributes but does not by itself create an IP-to-user mapping for transparent policy.
RADIUS: the FortiGate acts as a network access client and receives Access-Accept, Access-Reject or Access-Challenge. Shared secret, client/NAS identity, source IP, timeout and returned group attributes must agree. Preserve a local break-glass administrator.
FSSO: collector/agent methods learn user logon information and map user/group to workstation IP for identity-aware policy. Shared/NATed devices, stale logoff data, collector reachability and group filters affect accuracy. Validate the live user/IP mapping and matched policy rather than assuming directory success proves FSSO.
Optional demo: test one LDAP/RADIUS server object, then inspect one FSSO user/IP mapping; do not let this supplement displace routing, VPN, EMS, HA or SD-WAN.
Official preparation references: FortiGate/FortiOS 7.6.7 Administration Guide — LDAP servers, RADIUS servers, Firewall authentication and FSSO. Confirm FortiOS 7.6.7 build and authentication architecture.

## Slide 59
59
Objects turn intent into reusable selectors
• Address objects represent hosts, subnets, ranges, FQDNs or interfaces as supported
• Service objects represent protocol and port ranges
• Groups reduce repetition but can hide overly broad membership
• Comments, owners and lifecycle information improve change safety
ILLUSTRATIVE SCENARIO
APP-PROD-10.1.20.10 and SVC-HTTPS-8443 are clearer than “server1” and “custom1”
EXPECTED RESULT
Expand group membership and confirm the concrete match values.
Expected observation
The policy references the intended reusable objects and the test traffic matches that policy ID.
059 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Address objects represent hosts, subnets, ranges, FQDNs or interfaces as supported; Service objects represent protocol and port ranges; Groups reduce repetition but can hide overly broad membership; Comments, owners and lifecycle information improve change safety
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.

## Slide 60
60
Naming should survive interface and personnel changes
• Name by function, environment and scope rather than transient ticket numbers
• Avoid embedding unverified geography or ownership
• Use consistent prefixes only when they add search value
• Document exceptions and expiration dates for temporary objects
ILLUSTRATIVE SCENARIO
TEMP-VENDOR-HTTPS-EXP-2026-10-31 is auditable if lifecycle is enforced
EXPECTED RESULT
Search for duplicates, unused objects and ambiguous names before adding new ones.
Expected observation
The policy references the intended reusable objects and the test traffic matches that policy ID.
060 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Name by function, environment and scope rather than transient ticket numbers; Avoid embedding unverified geography or ownership; Use consistent prefixes only when they add search value; Document exceptions and expiration dates for temporary objects
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.

## Slide 61
61
Reusability must not erase policy intent
• Reuse canonical network/service objects
• Create a group when members genuinely share policy treatment
• Do not create mega-groups that make logging and review opaque
• FQDN/dynamic objects add resolution dependencies that must be monitored
ILLUSTRATIVE SCENARIO
A web-services group may be valid; “ALL-SERVERS” usually needs review
EXPECTED RESULT
Trace one object from definition to policy and traffic log.
Expected observation
The policy references the intended reusable objects and the test traffic matches that policy ID.
061 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Reuse canonical network/service objects; Create a group when members genuinely share policy treatment; Do not create mega-groups that make logging and review opaque; FQDN/dynamic objects add resolution dependencies that must be monitored
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.

## Slide 62
62
Maintainable policy has a clear purpose and owner
CLEAR
• Specific objects
• Single business purpose
• Expected logging/profile
• Named owner/lifecycle
FRAGILE
• all/all services
• Mixed purposes
• No comment or owner
• Permanent temporary access
KEY DISTINCTION
A policy name should let an operator predict source, destination and service
062 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Place narrow exceptions intentionally; Separate flows with different owners, logging or security profiles; Use comments and change records to explain why a rule exists; Review zero-hit, expired and shadowed policies carefully before removal
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.

## Slide 63
063
Policy review
63
01
Expand object groups
02
Compare scope to intent
03
Check rule order
04
Review logs/hits
05
Retain rollback
EXPECTED RESULT
The policy references the intended reusable objects and the test traffic matches that policy ID.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Resolve all object/group members; Compare scope to the documented flow; Check ordering and overlapping rules; Confirm logs and security profiles support operations
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.

## Slide 64
064
Common mistakes—and how to correct them
64
MISTAKE
CORRECTION — AND WHY IT HELPS
Create duplicate objects
Search existing objects first; canonical objects reduce inconsistent policy scope.
Use mega-groups for convenience
Group only members with the same owner and treatment; large mixed groups hide access.
Delete a zero-hit rule immediately
Confirm logging window, seasonality and owner; zero hits alone does not prove obsolescence.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.

## Slide 65
65
Troubleshooting workflow: narrow the failed decision
01
Start from a failing/desired five-tuple
02
Resolve object membership
03
Check service protocol and port ranges
04
Inspect order, action, NAT and profiles
05
Use traffic logs, hit counters and change history
What to observe
• Check service protocol and port ranges
• Inspect order, action, NAT and profiles
• Use traffic logs, hit counters and change history
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
065 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Start from a failing/desired five-tuple; Resolve object membership; Check service protocol and port ranges; Inspect order, action, NAT and profiles; Use log/hit state/output and change history
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.

## Slide 66
66
Practical handoff: Refactor a Bad Firewall Rulebase
• START / PREREQUISITES: Instructor-supplied flawed rulebase copy; current Student N baseline backed up.
• CHANGE / INVESTIGATE: Find shadowing, broad selectors, duplicate objects and missing logging; refactor without changing intended access.
• EXPECTED RESULT: Required flows still pass, forbidden flows stay blocked, and policy hits/logs map to a simpler ordered rulebase.
• CLEANUP / RESET: Export the revised policy set, then restore the approved course baseline.
• DELIVERY: Hands-on in the student VDOM/unit; offline configuration review fallback.
PLANNED EXERCISE
Find shadowing, broad selectors, duplicate objects and missing logging; refactor without changing intended access.
EXPECTED RESULT
Required flows still pass, forbidden flows stay blocked, and policy hits/logs map to a simpler ordered rulebase.
DELIVERY MODE
Hands-on; offline review fallback
066 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: Exercise: Refactor a Bad Firewall Rulebase.
Preparation: distribute a flawed copy, never the only known-good configuration.
Answer key: remove/merge duplicate objects, narrow broad selectors, order specific rules before broader intent where required, and enable useful logging. Required flows remain allowed; prohibited flows remain denied.
Reset: export work for review and restore the approved baseline.

## Slide 67
67
Knowledge check — explain the result
QUESTION 1
• When should objects be grouped?
QUESTION 2
• Why is a zero hit count insufficient to delete a rule?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
067 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: When should objects be grouped?; Why is a zero hit count insufficient to delete a rule?
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Knowledge check answer key:
Q: When should objects be grouped?
A: When all members share the same policy intent and lifecycle.
Q: Why is a zero hit count insufficient to delete a rule?
A: The observation window, logging, seasonality and dependency/change history may be incomplete.

## Slide 68
DAY 2 • 13:00–14:30
Security Services & SSL Inspection
Day 2 core uses planned local Linux client/server traffic; Internet/FortiGuard-dependent extensions are optional
LEARNING OBJECTIVES
• Explain AV, IPS, Web Filter and Application Control roles
• Sequence security profiles with inspection prerequisites
• Compare certificate and deep inspection with PKI and operational impacts
PREREQUISITES + PRACTICE RESERVE
• Working outbound policy and logging
• Instructor-managed test content only
• Trusted inspection CA distribution for deep-inspection lab
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
068
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain AV, IPS, Web Filter and Application Control roles; Sequence security profiles with inspection prerequisites; Compare certificate and deep inspection with PKI and operational impacts
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.

## Slide 69
69
Security profiles answer different detection questions
CONTENT
• Antivirus
• Web content/category
BEHAVIOR
• IPS exploits/protocols
• Application signatures
KEY DISTINCTION
One session may trigger multiple profile decisions; logs must be correlated by time/session
069 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Antivirus scans supported content/files for malware; IPS matches exploit/protocol behavior using signatures and engines; Web Filter classifies and controls web destinations/categories; Application Control identifies applications beyond simple port labels
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.

## Slide 70
70
Inspection mode determines what profiles can see
• Flow mode streams traffic through engines with lower buffering
• Proxy mode terminates/proxies supported protocols for deeper protocol handling
• Feature behavior and availability vary by profile/protocol/release
• Choose mode by required controls and tested compatibility, not habit
ILLUSTRATIVE SCENARIO
Document the required visibility first; then choose inspection/profile combination
EXPECTED RESULT
Check policy inspection mode and profile attachment in the FortiOS 7.6.7 build.
Expected observation
The client trusts the inspection certificate and the relevant security profile records the intended action.
070 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Flow mode streams traffic through engines with lower buffering; Proxy mode terminates/proxies supported protocols for deeper protocol handling; Feature behavior and availability vary by profile/protocol/release; Choose mode by required controls and tested compatibility, not habit
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.

## Slide 71
71
Certificate inspection and deep inspection solve different problems
CERTIFICATE
• Handshake metadata
• No payload decryption
• Lower endpoint impact
DEEP
• Payload visible to profiles
• Inspection CA required
• Compatibility/performance impact
KEY DISTINCTION
Certificate inspection can categorize based on visible data; deep inspection enables content scanning
071 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Certificate inspection observes TLS handshake/certificate metadata without decrypting payload; Deep inspection decrypts and re-encrypts TLS traffic to expose content; Deep inspection requires endpoint trust in the inspection CA and policy/privacy approval; Exceptions are often needed for pinning, unsupported protocols or regulated traffic
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.

## Slide 72
072
Deep inspection creates two TLS connections
Certificate inspection reads handshake metadata but does not decrypt the application payload
72
CLIENT
trusts Inspection CA
TLS #1
FORTIGATE
decrypt • inspect • re-encrypt
TLS #2
SERVER
original certificate
Certificate presented to client
Replacement certificate for server name signed by the FortiGate Inspection CA
Certificate received from server
Original server certificate validated by FortiGate
CERTIFICATE INSPECTION
• No payload decryption
• Reads visible TLS metadata
• Cannot scan encrypted content
LESSON
The browser trusts the replacement certificate only when the inspection CA is installed and trusted on the endpoint.
Notes: Expected result: under deep inspection, the browser certificate issuer is the configured inspection CA; under certificate inspection, the original server certificate remains end to end. Source: FortiOS 7.6.7 Administration Guide — SSL/SSH inspection and deep inspection.

## Slide 73
073
HTTPS profile interaction
73
01
Policy selects SSL profile
02
TLS visibility is established
03
Security profiles inspect
04
Traffic/security logs record action
05
Client receives allow/block
EXPECTED RESULT
The client trusts the inspection certificate and the relevant security profile records the intended action.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Policy permits and selects inspection mode; TLS inspection exposes available metadata/content; AV/IPS/Web/App engines apply relevant controls; Traffic and security logs record different state/output
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.

## Slide 74
074
Common mistakes—and how to correct them
74
MISTAKE
CORRECTION — AND WHY IT HELPS
Enable deep inspection without CA deployment
Install and trust the inspection CA on managed clients; otherwise browsers reject replacement certificates.
Expect certificate inspection to scan payload
Use deep inspection when content scanning is required; certificate inspection does not decrypt payload.
Blame the profile before checking TLS
Check certificate chain, time and pinning first; TLS can fail before a profile scans content.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.

## Slide 75
75
Troubleshooting workflow: narrow the failed decision
01
Prove basic path and policy first
02
Check TLS handshake/certificate errors
03
Confirm inspection mode and client trust
04
Identify which profile blocked or reset the session
05
Test an approved exception without broad bypass
What to observe
• Confirm inspection mode and client trust
• Identify which profile blocked or reset the session
• Test an approved exception without broad bypass
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
075 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prove basic path and policy first; Check TLS handshake/certificate errors; Confirm inspection mode and client trust; Identify which profile blocked or reset the session; Test an approved exception without broad bypass
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.

## Slide 76
76
Practical handoff: Inspect and Block Controlled Security Events
• START / PREREQUISITES: Validated Linux LAN client and DMZ HTTP/HTTPS server; logging and inspection CA package prepared.
• CHANGE / INVESTIGATE: Core: EICAR AV test, web-filter/log review, app-control observation, and certificate-vs-deep inspection with CA trust.
• EXPECTED RESULT: EICAR is blocked/logged; web/app actions are interpretable; deep inspection succeeds only after the inspection CA is trusted.
• CLEANUP / RESET: Delete test files, restore policy/profile and endpoint trust snapshot, and stop captures/debug.
• DELIVERY: Hands-on local core; controlled IPS and Internet/FortiGuard extensions only after instructor prevalidation.
PLANNED EXERCISE
Core: EICAR AV test, web-filter/log review, app-control observation, and certificate-vs-deep inspection with CA trust.
EXPECTED RESULT
EICAR is blocked/logged; web/app actions are interpretable; deep inspection succeeds only after the inspection CA is trusted.
DELIVERY MODE
Hands-on core; optional extensions
076 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: Exercise: Inspect and Block Controlled Security Events.
Core local exercise: planned Linux LAN client to planned DMZ HTTP/HTTPS server. Run safe EICAR AV test, review web-filter action/log, observe application-control classification, compare certificate inspection with deep inspection, and troubleshoot inspection-CA trust.
Expected core: EICAR is blocked/quarantined or denied according to the prevalidated profile and logged; certificate inspection sees TLS metadata; deep inspection re-signs the server certificate and works only when the client trusts the FortiGate inspection CA.
Optional extensions: controlled IPS-trigger traffic and Internet/FortiGuard-dependent web/app tests. Prevalidate the exact IPS signature, traffic recipe, target service, entitlement, profile action and expected log before class. Do not use arbitrary scans or promise a trigger.
Reset: remove EICAR/test files, restore profiles/policy and client trust snapshot, stop captures/debug. Keep local core manageable; move procedures and exact signatures to the lab guide.

## Slide 77
77
Knowledge check — explain the result
QUESTION 1
• What payload does certificate inspection decrypt?
QUESTION 2
• Why can deep inspection break an otherwise reachable site?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
077 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What payload does certificate inspection decrypt?; Why can deep inspection break an otherwise reachable site?
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Knowledge check answer key:
Q: What payload does certificate inspection decrypt?
A: None; it uses visible TLS handshake and certificate metadata.
Q: Why can deep inspection break an otherwise reachable site?
A: The client may not trust the inspection CA, the application may pin certificates, or protocol/privacy exceptions may apply.

## Slide 78
DAY 2 • 14:30–16:00
FortiGate Hardware Architecture, Monitoring & Operations
Foundations • Day 2 of 2
LEARNING OBJECTIVES
• Distinguish management, control and data planes
• Explain NP/CP acceleration versus Azure FGVM datapaths
• Monitor performance and plan supervised backup/restore/firmware maintenance
PREREQUISITES + PRACTICE RESERVE
• Read-only operational access
• FortiOS 7.6.7 Azure FGVM baseline
• Tested backup, image and recovery path before disruptive maintenance
Teach ~54 min • reserve ~36 min for guided activity, discussion and debrief
078
Notes: Day 2 operations owns deeper maintenance/recovery discussion. Revisit backup compatibility, recovery access, release notes, upgrade path, firmware validation and post-reboot checks. Live restore or firmware change remains instructor-supervised on a disposable appliance only.

## Slide 79
79
Planes separate configuration, decisions and packet work
MANAGEMENT
• GUI/CLI/API
• Admins/config
CONTROL
• Routes/HA/state
• Protocol decisions
DATA
• Sessions/forwarding
• NAT/security engines
KEY DISTINCTION
GUI responsiveness does not prove packet forwarding health; forwarding does not prove routing adjacency health
079 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Management plane serves GUI/CLI/API and administration; Control plane learns routing, HA and system state; Data plane forwards sessions and applies security processing; A plane can be healthy while another is constrained
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.

## Slide 80
080
Appliance offload and Azure FGVM use different datapaths
First packets and unsupported features remain on the CPU path
80
PHYSICAL FORTIGATE APPLIANCE
CPU
session setup route • policy • NAT
eligible
NP
accelerated forwarding
CP assists supported content / crypto processing on applicable models and features.
TRAFFIC THAT STAYS ON CPU
• First packets and session setup
• Unsupported/offload-ineligible features
• Exceptional traffic and control-plane work
AZURE FORTIGATE-VM LAB
vCPU
FortiOS software path
vNIC
AZURE NETWORK
VM/vNIC/cloud acceleration
• No physical NP/CP ASIC datapath
• Use CPU/session counters for lab learning
• Do not extrapolate FGVM results to appliance capacity
LESSON
Teach appliance NP/CP concepts separately from what learners can actually verify in the Azure FGVM lab.
Notes: Instructor review: use model-specific hardware guides for NP/CP eligibility and counters. The Azure FGVM lab demonstrates software processing and Azure networking, not FortiASIC offload. Source: FortiOS 7.6.7 Administration Guide — Hardware acceleration; FortiGate-VM for Azure documentation.

## Slide 81
81
Fast path and slow path describe processing eligibility
• Session setup and exceptional traffic require CPU decisions
• Established eligible sessions may be offloaded
• Inspection, fragmentation, tunneling or feature choices can affect eligibility
• No-offload is not automatically a fault; compare with documented support
ILLUSTRATIVE SCENARIO
A session can work correctly without offload but consume more CPU
EXPECTED RESULT
Inspect session offload flags/counters only with platform-specific documentation.
Expected observation
CPU, memory and session values are recorded; appliance-only offload counters are not inferred from Azure FGVM.
081 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Session setup and exceptional traffic require CPU decisions; Established eligible sessions may be offloaded; Inspection, fragmentation, tunneling or feature choices can affect eligibility; No-offload is not automatically a fault; compare with documented support
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.

## Slide 82
082
Operations baseline
82
01
Record build and uptime
02
Count sessions
03
Sample CPU/memory
04
Check Conserve Mode events
05
Compare with normal baseline
EXPECTED RESULT
CPU, memory and session values are recorded; appliance-only offload counters are not inferred from Azure FGVM.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm firmware build and support policy before change; Back up configuration and document rollback; Track session count, CPU and memory against normal workload; Recognize Conserve Mode as protective behavior under memory pressure
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.

## Slide 83
083
Common mistakes—and how to correct them
83
MISTAKE
CORRECTION — AND WHY IT HELPS
Expect NP/CP counters in Azure FGVM
Use VM CPU/session counters in the lab; ASIC offload requires a physical appliance.
Upgrade without backup and release review
Back up and read 7.6.7 release notes/upgrade path; this preserves rollback.
Treat Conserve Mode as one process fault
Check memory trend, sessions, proxy use and top processes; multiple consumers can trigger it.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.

## Slide 84
84
Troubleshooting workflow: narrow the failed decision
01
Confirm current build/model/VM and recent changes
02
Compare CPU, memory and session counts to baseline
03
Identify top consumers and inspection load
04
Check Conserve Mode thresholds/events and proxy behavior
05
Mitigate safely; preserve evidence before restart/upgrade
What to observe
• Identify top consumers and inspection load
• Check Conserve Mode thresholds/events and proxy behavior
• Mitigate safely; preserve evidence before restart/upgrade
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
084 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm current build/model/VM and recent changes; Compare CPU, memory and session counts to baseline; Identify top consumers and inspection load; Check Conserve Mode thresholds/events and proxy behavior; Mitigate safely; preserve state/output before restart/upgrade
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.

## Slide 85
85
Practical handoff: Operate and Observe the Firewall
• START / PREREQUISITES: Known-good Student N traffic and read-only dashboard/CLI/log access; baseline metrics recorded.
• CHANGE / INVESTIGATE: Correlate sessions, logs, interface counters, CPU/memory and one bounded packet capture during a test flow.
• EXPECTED RESULT: The team explains the flow from packet to session/log and distinguishes normal baseline from one supplied anomaly.
• CLEANUP / RESET: Stop capture/debug, clear filters and leave configuration unchanged.
• DELIVERY: Hands-on observation; instructor metric snapshot fallback.
PLANNED EXERCISE
Correlate sessions, logs, interface counters, CPU/memory and one bounded packet capture during a test flow.
EXPECTED RESULT
The team explains the flow from packet to session/log and distinguishes normal baseline from one supplied anomaly.
DELIVERY MODE
Hands-on; snapshot fallback
085 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: Exercise: Operate and Observe the Firewall.
Answer key: a single timestamped tuple links session, traffic log, interface counters and packet capture. CPU/memory are compared to the recorded baseline, not generic thresholds.
Reset: configuration unchanged; stop captures/debug and clear filters.

## Slide 86
86
Knowledge check — explain the result
QUESTION 1
• Why can a VM lab not prove NP/CP offload behavior?
QUESTION 2
• What is Conserve Mode?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
086 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Why can a VM lab not prove NP/CP offload behavior?; What is Conserve Mode?
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.
Knowledge check answer key:
Q: Why can a VM lab not prove NP/CP offload behavior?
A: The VM does not contain the appliance’s ASIC datapath; acceleration depends on virtual platform capabilities.
Q: What is Conserve Mode?
A: A protective FortiOS state triggered by memory pressure that changes/limits processing to preserve system stability; investigate causes and thresholds for the exact build.

## Slide 87
DAY 3 • 09:00–10:30
Route Selection, PBR & OSPF
Advanced • Day 1 of 2
LEARNING OBJECTIVES
• Explain route selection interactions with PBR
• Plan controlled route redistribution
• Establish OSPF neighbors and trace LSA-to-route exchange
PREREQUISITES + PRACTICE RESERVE
• Static routing mastery
• Required instructor preparation: isolated training tunnel
• Supplied tunnel IPs/router IDs; shared management protected
Teach ~56 min • reserve ~34 min for guided activity, discussion and debrief
087
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain route selection interactions with PBR; Plan controlled route redistribution; Establish OSPF neighbors and trace LSA-to-route exchange
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.

## Slide 88
88
PBR can override destination-route intent for selected traffic
01
Packet fields
02
PBR match?
03
Next hop valid?
04
Forward
05
Fallback route
What to observe
• If matched and valid, it directs a next hop/interface before normal route selection
• A supporting route and reachable next hop are still required
• PBR increases operational complexity; document scope and fallback
INSTRUCTOR DEMONSTRATION
Inspect policy-route list and debug-flow route decision for the exact test tuple.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
088 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A policy route matches fields such as ingress, source, destination and service as supported; If matched and valid, it directs a next hop/interface before normal route selection; A supporting route and reachable next hop are still required; PBR increases operational complexity; document scope and fallback
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.

## Slide 89
89
Redistribution moves selected routes between protocols
• Redistribute only intentional prefixes with route maps/prefix filters
• Metrics and tags help prevent loops and control preference
• A route in one database is not automatically advertised into another
• Default-route origination should be conditional and documented
ILLUSTRATIVE SCENARIO
Student01 10.1.10.0/24 enters OSPF only if it passes the prefix policy
EXPECTED RESULT
Verify source route, redistribution rule, advertised LSA and remote installation.
Expected observation
The OSPF neighbor reaches Full and the advertised Student01 prefix is installed with the expected next hop.
089 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Redistribute only intentional prefixes with route maps/prefix filters; Metrics and tags help prevent loops and control preference; A route in one database is not automatically advertised into another; Default-route origination should be conditional and documented
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.

## Slide 90
090
OSPF neighbors exchange LSAs; SPF installs the best route
Actual lab addressing; morning exercise uses the instructor-provided training tunnel
90
INSTRUCTOR FGT
RID <instructor RID>
Hello / DBD / LSA
AREA 0
transit network
LSA / ACK
STUDENT01 FGT
RID <Student01 RID>
STUDENT01 LAN
10.1.10.0/24
LAN
NEIGHBOR STATE
Down → Init → 2-Way → ExStart → Exchange → Loading → Full
INSTRUCTOR ROUTING TABLE
O 10.1.10.0/24 via <training-tunnel next hop>
LESSON
Full adjacency is necessary, but the learned prefix must also appear in the LSDB and active routing table.
Notes: Expected result: the neighbor reaches Full; the LSDB contains the branch prefix; HQ installs 10.2.10.0/24 with the intended OSPF next hop. Source: FortiOS 7.6.7 Administration Guide — OSPF neighbors, LSDB and routing table.

## Slide 91
91
LSAs build a shared topology; SPF installs best paths
R1 AREA 0
LSA FLOOD
R2 LSDB
SPF → ROUTE
A connected /24 is advertised, appears in LSDB, then installs as OSPF route
• Routers flood link-state information within defined scope
• Area design limits flooding and supports hierarchy
• The LSDB is not the routing table; SPF derives candidate paths
• Route type and metric influence the installed result
Compare the OSPF database, installed route and one forwarded test flow.
091 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Routers flood link-state information within defined scope; Area design limits flooding and supports hierarchy; The LSDB is not the routing table; SPF derives candidate paths; Route type and metric influence the installed result
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.

## Slide 92
092
OSPF route exchange
92
01
Reach Full neighbor
02
Receive/flood LSA
03
Run SPF
04
Install route
05
Forward test traffic
EXPECTED RESULT
The OSPF neighbor reaches Full and Student01/Student02 lab prefixes install through the training tunnel.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm interface and router ID; Reach Full neighbor state where expected; Verify prefix exists in LSDB with intended LSA/type; Verify active route and return route; Test traffic and preserve packet/session state/output
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.

## Slide 93
093
Common mistakes—and how to correct them
93
MISTAKE
CORRECTION — AND WHY IT HELPS
Troubleshoot only the routing table
Check neighbor state and LSDB first; no route installs until adjacency and LSA exchange succeed.
Redistribute every route
Apply prefix/route-map filters; controlled redistribution prevents leaks and loops.
Use PBR to hide a return-path problem
Correct both route directions; PBR only changes selected matching traffic.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.

## Slide 94
94
Troubleshooting workflow: narrow the failed decision
01
Check physical/IP reachability and PBR scope
02
Verify OSPF interface/area/timers/authentication/MTU
03
Inspect neighbor state transition
04
Inspect LSDB and redistribution filter
05
Confirm active route, policy and return path
What to observe
• Inspect neighbor state transition
• Inspect LSDB and redistribution filter
• Confirm active route, policy and return path
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
094 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check physical/IP reachability and PBR scope; Verify OSPF interface/area/timers/authentication/MTU; Inspect neighbor state transition; Inspect LSDB and redistribution filter; Confirm active route, policy and return path
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.

## Slide 95
95
Practical handoff: Dynamic Routing across the Overlay
• START / PREREQUISITES: Required preparation: instructor-provided training tunnel is up and isolated from management; router IDs/tunnel IPs supplied.
• CHANGE / INVESTIGATE: Build/inspect OSPF on that tunnel, advertise Student01/Student02 lab prefixes, and trace neighbor → LSA → route → traffic.
• EXPECTED RESULT: Neighbor reaches Full and the expected Student pod prefix installs through the training tunnel.
• CLEANUP / RESET: Remove only student OSPF changes or restore the routing snapshot; do not alter the tunnel or shared access.
• DELIVERY: Hands-on objective; instructor demonstration fallback if the prepared tunnel is not validated.
PLANNED EXERCISE
Build/inspect OSPF on that tunnel, advertise Student01/Student02 lab prefixes, and trace neighbor → LSA → route → traffic.
EXPECTED RESULT
Neighbor reaches Full and the expected Student pod prefix installs through the training tunnel.
DELIVERY MODE
Hands-on; demo fallback
095 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: Exercise: Dynamic Routing across the Overlay.
Required preparation: build and validate an instructor-provided training tunnel before class; supply tunnel IPs, router IDs and reset snapshot. This is a preparation requirement, not a claim that the deployment already exists.
Students may change OSPF only. They must not delete/rename the tunnel or alter shared management routes.
Answer key: OSPF reaches Full; expected Student01/Student02 prefix appears in LSDB and active table; test traffic follows the training tunnel.
Fallback: instructor demonstration if validation is incomplete. Reset only routing changes.

## Slide 96
96
Knowledge check — explain the result
QUESTION 1
• Which command output shows route exchange beyond adjacency?
QUESTION 2
• Why filter redistribution?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
096 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Which state/output proves route exchange beyond adjacency?; Why filter redistribution?
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: Which state/output proves route exchange beyond adjacency?
A: The expected LSA/prefix in the database and installed route on the peer.
Q: Why filter redistribution?
A: To limit scope, prevent loops/leaks and preserve predictable path selection.

## Slide 97
DAY 3 • 10:30–12:00
BGP exchanges policy-controlled reachability between autonomous systems
Small route exchange across the required instructor-provided morning training tunnel
BGP IN ONE MINUTE
• An autonomous system (AS) applies one routing policy under an AS number
• eBGP peers use different ASes; iBGP peers share an AS
• TCP/179 and OPEN/KEEPALIVE must succeed before UPDATE messages
• Filters control which prefixes are accepted and advertised
PEERING STATE
• Route to neighbor and TCP reachability
• State progresses to Established
• Intended prefix is advertised/received
• Best path installs with reachable next hop
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
097
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain autonomous systems, eBGP/iBGP and neighbor establishment; Advertise only intended prefixes; Use attributes and filters to predict path selection
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 98
098
BGP policy controls which reachable prefixes cross an AS boundary
Actual lab prefixes; peer tunnel IPs, ASNs and router IDs remain instructor preparation items
98
STUDENT01 • AS <S01 AS>
advertises 10.1.10.0/24
eBGP TCP/179
TRAINING TUNNEL
preconfigured / isolated
accepted prefix
STUDENT02 • AS <S02 AS>
receives UPDATE
OUTBOUND FILTER AT STUDENT01
permit 10.1.10.0/24
deny all other prefixes
CONTROL → FORWARDING
1 Prefix received
2 Policy permits
3 Best path selected
4 Next hop reachable
5 Route installed
INSTALLED ROUTE
B 10.1.10.0/24 via <training-tunnel next hop>
LESSON
Troubleshoot BGP in order: peer Established → prefix permitted → best path selected → next hop resolved → route installed.
Notes: Expected result: only 10.1.10.0/24 is advertised; the peer receives it, marks one path best, resolves the next hop and installs the route. Source: FortiOS 7.6.7 Administration Guide — BGP, route maps and prefix lists.

## Slide 99
99
BGP neighbor state reveals the failed stage
01
Idle
02
Connect
03
OpenSent
04
OpenConfirm
05
Established
What to observe
• OpenSent/OpenConfirm indicate BGP capability/parameter exchange
• Established permits UPDATE messages
• Timers, source address, multihop, password and AS configuration must agree
INSTRUCTOR DEMONSTRATION
get router info bgp summary; inspect peer state, uptime and received/advertised counts.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
099 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Idle/Connect/Active indicate transport or retry state; OpenSent/OpenConfirm indicate BGP capability/parameter exchange; Established permits UPDATE messages; Timers, source address, multihop, password and AS configuration must agree
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 100
100
eBGP and iBGP serve different propagation roles
eBGP
• Different AS
• External policy boundary
• AS_PATH changes
iBGP
• Same AS
• Internal distribution
• Full mesh or RR design
KEY DISTINCTION
Route reflector design is optional deep dive; do not infer full-mesh scalability
100 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: eBGP exchanges routes across AS boundaries and commonly changes next-hop behavior; iBGP distributes external/internal reachability within one AS; iBGP split-horizon requires full mesh or route reflectors at scale; IGP reachability to BGP next hops remains essential
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 101
101
Prefix advertisement requires route presence and policy permission
• A network statement/redistribution mechanism does not create reachability by itself
• The prefix must meet the platform’s origination conditions
• Outbound filters prevent accidental leaks
• Inbound filters and maximum-prefix controls limit accepted scope
ILLUSTRATIVE SCENARIO
Advertise Student01 10.1.10.0/24 only; reject all unrelated prefixes
EXPECTED RESULT
Compare local route, advertised-routes, peer received-routes and active table.
Expected observation
The peer reaches Established, the permitted prefix is received, and the selected BGP path is installed.
101 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A network statement/redistribution mechanism does not create reachability by itself; The prefix must meet the platform’s origination conditions; Outbound filters prevent accidental leaks; Inbound filters and maximum-prefix controls limit accepted scope
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 102
102
BGP path selection is ordered, not a vote
PATH A
• local-pref 200
• AS_PATH 65020 65100
• next hop reachable
PATH B
• local-pref 100
• AS_PATH 65200
• next hop reachable
RESULT
• A wins at local preference
• Later criteria not evaluated
• Validate best-path marker
KEY DISTINCTION
Two /24 paths: higher local preference can win before shorter AS_PATH
102 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Policy can set weight/local preference and other attributes depending on scope; AS_PATH length, origin, MED, eBGP/iBGP and IGP cost are evaluated in an implementation-defined order; Only compare attributes when earlier criteria tie; Document which attributes are locally significant and confirm exact FortiOS order
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 103
103
Route maps and prefix lists implement routing policy
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
get router info bgp summary get router info bgp network get router info bgp neighbors <peer> advertised-routes get router info bgp neighbors <peer> received-routes
READ THE OUTPUT
• Prefix lists match address and prefix-length ranges
• Route maps match and permit/deny or set attributes
• Direction matters: inbound changes acceptance; outbound changes advertisement
• Always include an explicit policy for default/unmatched routes
Safe operation
Outbound permit for 10.2.10.0/24; deny everything else
103 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prefix lists match address and prefix-length ranges; Route maps match and permit/deny or set attributes; Direction matters: inbound changes acceptance; outbound changes advertisement; Always include an explicit policy for default/unmatched routes
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 104
104
BGP state connects peer, prefix selection and forwarding
• Peer state: Established with stable uptime
• Control plane: expected prefix received/advertised and best path selected
• Routing table: BGP route installed with intended next hop
• Data plane: policy/session/packet behavior follows that next hop
ILLUSTRATIVE SCENARIO
A received route can lose selection or fail installation; never stop at prefix count
EXPECTED RESULT
Capture summary, detailed prefix, route table and one test flow.
Expected observation
The peer reaches Established, the permitted prefix is received, and the selected BGP path is installed.
104 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Peer state: Established with stable uptime; Control plane: expected prefix received/advertised and best path selected; Routing table: BGP route installed with intended next hop; Data plane: policy/session/packet state/output follows that next hop
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 105
105
Controlled BGP advertisement
105
01
Peer reaches Established
02
Prefix list permits /24
03
UPDATE advertises prefix
04
Peer selects best path
05
Route installs
EXPECTED RESULT
The peer is Established; only the permitted Student pod prefix is received, selected and installed.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Establish one eBGP peer; Originate one exact lab prefix; Apply outbound prefix filter; Confirm remote receipt and best path; Withdraw or deny and observe controlled change
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 106
106
Common mistakes—and how to correct them
106
MISTAKE
CORRECTION — AND WHY IT HELPS
Call Active state healthy
Check TCP/179 and peer parameters; BGP Active means the session is not Established.
Advertise a broad default accidentally
Use an explicit outbound prefix list and review advertised-routes before activation.
Tune attributes before next-hop reachability
Resolve the next hop first; an unusable path cannot enter forwarding.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 107
107
Troubleshooting workflow: narrow the failed decision
01
Verify route and TCP/179 reachability to peer
02
Check local/remote AS, update source, password and timers
03
Reach Established; inspect notifications if not
04
Verify origination and inbound/outbound filters
05
Confirm best path, active route and return path
What to observe
• Reach Established; inspect notifications if not
• Verify origination and inbound/outbound filters
• Confirm best path, active route and return path
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
107 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Verify route and TCP/179 reachability to peer; Check local/remote AS, update source, password and timers; Reach Established; inspect notifications if not; Verify origination and inbound/outbound filters; Confirm best path, active route and return path
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.

## Slide 108
108
Practical handoff: Small BGP Route Exchange
• START / PREREQUISITES: Morning training tunnel preserved; instructor supplies peer tunnel IPs, ASNs and router IDs.
• CHANGE / INVESTIGATE: Form one eBGP peering and advertise one Student pod /24 through an explicit prefix list.
• EXPECTED RESULT: Peer is Established; only the permitted prefix is received, selected and installed with a reachable next hop.
• CLEANUP / RESET: Remove the BGP neighbor/filter changes or restore snapshot; keep the training tunnel and management path intact.
• DELIVERY: Hands-on objective on the prepared tunnel; instructor demonstration fallback.
PLANNED EXERCISE
Form one eBGP peering and advertise one Student pod /24 through an explicit prefix list.
EXPECTED RESULT
Peer is Established; only the permitted prefix is received, selected and installed with a reachable next hop.
DELIVERY MODE
Hands-on; demo fallback
108 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: Exercise: Small BGP Route Exchange.
Required preparation: reuse the protected morning training tunnel without changing it; supply peer tunnel IPs, ASNs and router IDs.
Answer key: TCP/179 succeeds, peer reaches Established, explicit prefix list permits one Student pod /24, peer receives/selects/installs it, next hop resolves.
Reset BGP/filter changes only. Preserve tunnel and management access.

## Slide 109
109
Knowledge check — explain the result
QUESTION 1
• What does Established prove?
QUESTION 2
• Which path wins if local preference differs?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
109 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What does Established prove?; Which path wins if local preference differs?
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: What does Established prove?
A: The BGP session exchanged OPEN/KEEPALIVE successfully; it does not prove any particular prefix is permitted or installed.
Q: Which path wins if local preference differs?
A: The higher local preference wins before later criteria such as AS_PATH, subject to the exact FortiOS selection order.

## Slide 110
DAY 3 • 13:00–14:30
IPsec VPN Architecture & ADVPN
Advanced • Day 1 of 2
LEARNING OBJECTIVES
• Relate IKEv2 Phase 1, Phase 2 and route-based forwarding
• Design selectors, routes and policies as one system
• Explain ADVPN underlay/overlay, hub/spoke and shortcut behavior
PREREQUISITES + PRACTICE RESERVE
• Working Student01/Student02 underlay reachability
• Separate afternoon baseline or tunnel
• ADVPN shortcut/OSPF objective prevalidated or demo fallback
Teach ~60 min • reserve ~30 min for guided activity, discussion and debrief
110
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Relate IKEv2 Phase 1, Phase 2 and route-based forwarding; Design selectors, routes and policies as one system; Explain ADVPN underlay/overlay, hub/spoke and shortcut behavior
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.

## Slide 111
111
Route-based IPsec connects protected subnets over an underlay
Afternoon exercise: separate tunnel or isolated baseline; morning training tunnel remains intact
111
STUDENT01 LAN
10.1.10.0/24
STUDENT01 FGT
port1 10.1.0.4
AZURE UNDERLAY
transport reachability
STUDENT02 FGT
port1 10.2.0.4
STUDENT02 LAN
10.2.10.0/24
UDP 500/4500
IKEv2
IPsec overlay / selectors: 10.1.10.0/24 ↔ 10.2.10.0/24
CONTROL
IKE_SA_INIT → IKE_AUTH → CHILD SA
DATA
route → tunnel interface → policy → encrypted packets
LESSON
A tunnel can be “up” while application traffic fails because route, policy, selectors or return path are wrong.
Notes: Expected result: IKE and IPsec SAs are established, the branch route points to the tunnel interface, matching policies allow the flow, and encaps/decaps counters increase. Source: FortiOS 7.6.7 Administration Guide — IKEv2 and route-based IPsec VPN.

## Slide 112
112
IKEv2 negotiation produces authenticated secure state
01
IKE_SA_INIT
02
IKE_AUTH
03
CHILD SA
04
Route/policy
05
Protected traffic
What to observe
• Proposal, authentication method, IDs and reachability must be compatible
• NAT traversal and fragmentation behavior depend on path/design
• Logs/debug should be filtered by peer and stopped after capture
INSTRUCTOR DEMONSTRATION
Use tunnel summary and filtered IKE diagnostics; do not paste invented output.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
112 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Peers exchange proposals, identities, authentication and key material; Proposal, authentication method, IDs and reachability must be compatible; NAT traversal and fragmentation behavior depend on path/design; Logs/debug should be filtered by peer and stopped after capture
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.

## Slide 113
113
Phase 2 selectors define permitted protected traffic
• Route-based designs may use broad selectors but still require routing/policy boundaries
• Mismatched local/remote selectors prevent or limit SA establishment
• Overlapping prefixes complicate route and identity decisions
• Rekey/lifetime mismatches can appear as intermittent failures
ILLUSTRATIVE SCENARIO
Student01 local 10.1.10.0/24 matches Student02 remote 10.1.10.0/24 reciprocally
EXPECTED RESULT
Compare selectors on both peers and active SA packet counters.
Expected observation
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
113 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Route-based designs may use broad selectors but still require routing/policy boundaries; Mismatched local/remote selectors prevent or limit SA establishment; Overlapping prefixes complicate route and identity decisions; Rekey/lifetime mismatches can appear as intermittent failures
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.

## Slide 114
114
VPN design begins with failure domains and scale
• Define underlay resilience, addressing, routing ownership and crypto standards
• Choose static mesh, hub-spoke or dynamic overlay based on scale and traffic patterns
• Account for MTU/MSS, NAT, asymmetric paths and overlapping networks
• Document monitoring, certificate/PSK lifecycle and change coordination
ILLUSTRATIVE SCENARIO
A tunnel “up” with no traffic can still be a routing, policy or return-path failure
EXPECTED RESULT
Design review must include data-plane test cases, not only IKE settings.
Expected observation
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
114 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Define underlay resilience, addressing, routing ownership and crypto standards; Choose static mesh, hub-spoke or dynamic overlay based on scale and traffic patterns; Account for MTU/MSS, NAT, asymmetric paths and overlapping networks; Document monitoring, certificate/PSK lifecycle and change coordination
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.

## Slide 115
115
ADVPN starts through the hub, then builds a spoke shortcut
Planned protected overlay; validate shortcut behavior before class
115
STUDENT01
LAN 10.1.10.0/24
INSTRUCTOR HUB
control / discovery
STUDENT02
LAN 10.2.10.0/24
1 initial data → hub
1 hub → spoke B
2 Dynamic shortcut tunnel: subsequent spoke-to-spoke application traffic
UNDERLAY
Public/private transport routes reach hub and spoke tunnel endpoints.
OVERLAY
Protected prefixes and dynamic routing choose the logical tunnel path.
LESSON
Shortcut formation changes the data path; hub discovery/control activity and underlay reachability remain essential.
Notes: Instructor review: ADVPN generation and OSPF-over-ADVPN behavior are release/design dependent. Confirm the supported FortiOS 7.6.7 Azure topology before lab use. Source: FortiOS 7.6.7 Administration Guide — ADVPN and dynamic routing over IPsec.

## Slide 116
116
OSPF over ADVPN requires intentional network behavior
• Neighbor model, network type and area design must fit the overlay
• Shortcut routing must not break next-hop resolution
• Hub route reflection/advertisement choices affect spoke reachability
• Scale testing must include neighbors, LSAs, routes, tunnels and CPU/memory
ILLUSTRATIVE SCENARIO
Objective remains practical; exact tunnel IPs/network type are instructor preparation items
EXPECTED RESULT
Prevalidate FortiOS 7.6.7 behavior; use an instructor demonstration if the shortcut/OSPF build is not ready.
Expected observation
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
116 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [OPTIONAL DEEP DIVE] Stable ID: D3-B11-S116
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Neighbor model, network type and area design must fit the overlay; Shortcut routing must not break next-hop resolution; Hub route reflection/advertisement choices affect spoke reachability; Scale testing must include neighbors, LSAs, routes, tunnels and CPU/memory
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.

## Slide 117
117
ADVPN sizing tracks spokes, tunnels, routes and sessions
• Estimate concurrent hub-spoke and shortcut tunnels
• Account for route scale, neighbor scale, session count, crypto throughput and inspection
• Use platform data sheets and validated design guides, not slide estimates
• Failure/rekey storms can be more demanding than steady state
ILLUSTRATIVE SCENARIO
Sizing remains an instructor design exercise without a declared appliance/model and traffic profile
EXPECTED RESULT
Record assumptions and validate against current Fortinet sizing guidance.
Expected observation
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
117 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [OPTIONAL DEEP DIVE] Stable ID: D3-B11-S117
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Estimate concurrent hub-spoke and shortcut tunnels; Account for route scale, neighbor scale, session count, crypto throughput and inspection; Use platform data sheets and validated design guides, not slide estimates; Failure/rekey storms can be more demanding than steady state
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.

## Slide 118
118
Route-based VPN
118
01
Reach peer over underlay
02
Create IKE SA
03
Create CHILD SA
04
Route points to tunnel
05
Policy permits protected flow
EXPECTED RESULT
IKE/IPsec SAs, protected route and counters are correct; observe shortcut/OSPF state when prevalidated.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Underlay reaches peer address; IKEv2 authenticates peers and creates IKE SA; CHILD SA selectors protect intended prefixes; Routes send traffic to tunnel; policies permit both directions; Return route and session counters prove bidirectional flow
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.

## Slide 119
119
Common mistakes—and how to correct them
119
MISTAKE
CORRECTION — AND WHY IT HELPS
Check only tunnel-up status
Verify selectors, route, policy and bidirectional counters; IKE state alone does not carry traffic.
Confuse underlay and overlay routes
Check peer reachability separately from protected-prefix routes; they solve different paths.
Copy one ADVPN recipe everywhere
Confirm the supported 7.6.7 ADVPN generation and routing design before configuration.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.

## Slide 120
120
Troubleshooting workflow: narrow the failed decision
01
Prove underlay route and UDP/500/4500 reachability
02
Validate Phase 1 identity/proposal/authentication
03
Validate Phase 2 selectors/proposals and counters
04
Check overlay route, policies and return path
05
Capture filtered packets/IKE diagnostics; reset debug
What to observe
• Validate Phase 2 selectors/proposals and counters
• Check overlay route, policies and return path
• Capture filtered packets/IKE diagnostics; reset debug
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
120 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prove underlay route and UDP/500/4500 reachability; Validate Phase 1 identity/proposal/authentication; Validate Phase 2 selectors/proposals and counters; Check overlay route, policies and return path; Capture filtered packets/IKE diagnostics; reset debug
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.

## Slide 121
121
Practical handoff: Build Hub-and-Spoke IPsec and Observe the Overlay
• START / PREREQUISITES: Afternoon isolated baseline or separate tunnel; underlay reachability and protected prefixes confirmed.
• CHANGE / INVESTIGATE: Build route-based IPsec, observe hub/spoke state, then test ADVPN shortcut and OSPF-over-overlay objectives.
• EXPECTED RESULT: IKE/IPsec SAs, protected route and counters are correct; shortcut/OSPF state is observed when validated.
• CLEANUP / RESET: Restore the isolated afternoon baseline; never modify the morning tunnel or shared management access.
• DELIVERY: Hands-on tunnel build; instructor-demo fallback for unvalidated ADVPN shortcut or OSPF-over-overlay steps.
PLANNED EXERCISE
Build route-based IPsec, observe hub/spoke state, then test ADVPN shortcut and OSPF-over-overlay objectives.
EXPECTED RESULT
IKE/IPsec SAs, protected route and counters are correct; shortcut/OSPF state is observed when validated.
DELIVERY MODE
Hands-on build; demo fallback
121 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: Exercise: Build Hub-and-Spoke IPsec and Observe the Overlay.
Preparation: after lunch, use a separate tunnel or restore an isolated exercise baseline. The morning training tunnel remains untouched.
Core answer: underlay reaches peers; IKE/IPsec SAs form; protected route and policies select the tunnel; encap/decap counters increase.
Planned practical objectives retained: observe ADVPN shortcut and OSPF over the overlay. Prevalidate exact FortiOS 7.6.7 configuration and reset. If not validated, demonstrate these steps—do not silently downgrade the objective.
Reset the isolated afternoon baseline.

## Slide 122
122
Knowledge check — explain the result
QUESTION 1
• What does a route-based tunnel still need after SAs are up?
QUESTION 2
• What is the ADVPN shortcut for?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
122 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What does a route-based tunnel still need after SAs are up?; What is the ADVPN shortcut for?
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Knowledge check answer key:
Q: What does a route-based tunnel still need after SAs are up?
A: Routes, firewall policies, matching selectors and a valid return path.
Q: What is the ADVPN shortcut for?
A: To let eligible spoke-to-spoke data bypass the hub after dynamic discovery, while the underlay still reaches tunnel endpoints.

## Slide 123
DAY 3 • 14:30–16:00
VPN Troubleshooting & Operational Validation
Advanced • Day 1 of 2
LEARNING OBJECTIVES
• Localize failure across underlay, IKE, IPsec, routing, policy and return path
• Interpret Phase 1/2 state and selectors
• Use packet capture and CLI diagnostics without uncontrolled debug
PREREQUISITES + PRACTICE RESERVE
• Separate afternoon exercise tunnel or isolated baseline
• Known-good endpoint placeholders and snapshot
• Morning training tunnel and management access protected
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
123
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Localize failure across underlay, IKE, IPsec, routing, policy and return path; Interpret Phase 1/2 state and selectors; Use packet capture and CLI diagnostics without uncontrolled debug
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 124
124
Tunnel establishment is a layered dependency chain
01
Underlay
02
IKE SA
03
IPsec SA
04
Route
05
Policy/session
06
Return path
What to observe
• IKE SA precedes CHILD/IPsec SA
• Selectors and traffic triggers affect Phase 2
• Routes, policies and return path determine usable data flow
INSTRUCTOR DEMONSTRATION
Record state and timestamps before remediation.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
124 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Underlay route and peer reachability precede IKE; IKE SA precedes CHILD/IPsec SA; Selectors and traffic triggers affect Phase 2; Routes, policies and return path determine usable data flow
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 125
125
Phase 1 state isolates reachability, identity and proposal faults
• No response suggests path, NAT or peer availability
• Proposal mismatch prevents cryptographic agreement
• Authentication/ID mismatch fails after initial exchange
• Certificate failures require time, chain and identity checks
ILLUSTRATIVE SCENARIO
Filter IKE diagnostics to the peer; avoid broad debug on production
EXPECTED RESULT
Compare both peers’ timestamps and stated failure reason.
Expected observation
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
125 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: No response suggests path, NAT or peer availability; Proposal mismatch prevents cryptographic agreement; Authentication/ID mismatch fails after initial exchange; Certificate failures require time, chain and identity checks
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 126
126
Phase 2 state links selectors to directional packet counters
• An IKE SA can be healthy while no CHILD SA exists
• Selector mismatch or proposal mismatch prevents data SA
• Encaps/decaps counters show directionality
• Rekey failures may preserve old state briefly, causing intermittent symptoms
ILLUSTRATIVE SCENARIO
Encaps increasing with zero decaps points toward the remote policy, path or return route
EXPECTED RESULT
Compare both endpoints’ SA and packet counters.
Expected observation
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
126 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: An IKE SA can be healthy while no CHILD SA exists; Selector mismatch or proposal mismatch prevents data SA; Encaps/decaps counters show directionality; Rekey failures may preserve old state briefly, causing intermittent symptoms
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 127
127
Routing chooses the tunnel; policy permits the chosen path
• Route lookup must select the tunnel for the protected destination
• Policy ingress/egress pair must match actual interfaces
• A broader WAN route can steal traffic if overlay route is absent
• Return path must choose the reciprocal tunnel or valid symmetric design
ILLUSTRATIVE SCENARIO
Tunnel-up does not override a more-specific route to another interface
EXPECTED RESULT
Run route lookup for both destination directions.
Expected observation
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
127 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Route lookup must select the tunnel for the protected destination; Policy ingress/egress pair must match actual interfaces; A broader WAN route can steal traffic if overlay route is absent; Return path must choose the reciprocal tunnel or valid symmetric design
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 128
128
Sessions preserve the chosen VPN and NAT state
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
get vpn ipsec tunnel summary diagnose vpn tunnel list get router info routing-table details <protected-ip> diagnose sys session filter dst <protected-ip> diagnose sys session list
READ THE OUTPUT
• Existing sessions can continue using old routing/policy decisions
• A configuration fix may require a new test tuple or authorized session clear
• NAT is usually unintended for site-to-site protected traffic unless designed
• Asymmetric return creates one-sided counters and incomplete sessions
Safe operation
Use a new source port before disruptive session clearing
128 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Existing sessions can continue using old routing/policy decisions; A configuration fix may require a new test tuple or authorized session clear; NAT is usually unintended for site-to-site protected traffic unless designed; Asymmetric return creates one-sided counters and incomplete sessions
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 129
129
Packet capture shows where protected traffic stops
• Capture IKE on the underlay and protected traffic on LAN/tunnel-relevant interfaces
• One-sided protected packets reveal where forwarding stops
• ESP versus UDP/4500 depends on NAT traversal/path
• Schematic output must be labelled illustrative unless captured in the declared lab
ILLUSTRATIVE SCENARIO
Use host/port filters and bounded packet counts
EXPECTED RESULT
Stop capture/debug and sanitize addresses before sharing.
Expected observation
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
129 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Capture IKE on the underlay and protected traffic on LAN/tunnel-relevant interfaces; One-sided protected packets reveal where forwarding stops; ESP versus UDP/4500 depends on NAT traversal/path; Schematic output must be labelled illustrative unless captured in the declared lab
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 130
130
TLS inspection reminder for VPN troubleshooting
OPTION A
• Certificate inspection: TLS/certificate metadata only
• Deep inspection: decrypts and re-signs application TLS
OPTION B
• Deep inspection needs endpoint trust in the FortiGate inspection CA
• Full security-services treatment is in Day 2
KEY DISTINCTION
If VPN is up but HTTPS fails, check the policy SSL profile and client CA trust before changing the tunnel.
130 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Certificate inspection reads TLS handshake/certificate metadata without decrypting application payload; Deep inspection proxies TLS and exposes payload to security profiles; Deep inspection requires endpoint trust in the FortiGate inspection CA; Pinning, privacy policy and performance may require scoped exceptions
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 131
131
VPN fault isolation
131
01
Underlay reachability
02
Phase 1 state
03
Phase 2 selectors/counters
04
Overlay route/policy
05
Return traffic
EXPECTED RESULT
The failed layer is identified without changing the morning tunnel or shared management path.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Symptom: Branch cannot reach HQ server; Check underlay and IKE state; Check CHILD SA selectors/counters; Check route and policy on both peers; Check session and captures; remediate only the failed layer
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 132
132
Common mistakes—and how to correct them
132
MISTAKE
CORRECTION — AND WHY IT HELPS
Restart IKE before collecting state
Record peer/SA error and counters first; restart removes the failing condition.
Clear every session
Use a fresh test flow or narrow filter; broad clearing hides scope and disrupts service.
Declare success from Phase 1
Require route, policy and increasing encap/decap counters; Phase 1 authenticates only the peers.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 133
133
Troubleshooting workflow: narrow the failed decision
01
Underlay route/capture
02
Phase 1 peer/proposal/identity
03
Phase 2 selectors/proposal/counters
04
Overlay route and policies
05
Session, NAT and return-path capture
What to observe
• Phase 2 selectors/proposal/counters
• Overlay route and policies
• Session, NAT and return-path capture
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
133 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Underlay route/capture; Phase 1 peer/proposal/identity; Phase 2 selectors/proposal/counters; Overlay route and policies; Session, NAT and return-path capture
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.

## Slide 134
134
Practical handoff: Broken VPN Ticket
• START / PREREQUISITES: Separate afternoon exercise tunnel with known-good snapshot and one instructor-injected safe fault.
• CHANGE / INVESTIGATE: Diagnose underlay, IKE, selectors, route, policy and directional counters without broad debug.
• EXPECTED RESULT: The failed layer is named, one reversible fix restores bidirectional protected traffic, and the ticket records before/after state.
• CLEANUP / RESET: Remove the intentional fault, stop debug/capture and restore the isolated snapshot.
• DELIVERY: Hands-on ticket; instructor trace demonstration if the exercise tunnel is unavailable.
PLANNED EXERCISE
Diagnose underlay, IKE, selectors, route, policy and directional counters without broad debug.
EXPECTED RESULT
The failed layer is named, one reversible fix restores bidirectional protected traffic, and the ticket records before/after state.
DELIVERY MODE
Hands-on ticket; trace fallback
134 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Exercise: Broken VPN Ticket.
Inject one prevalidated fault in the separate afternoon tunnel: disabled test policy, selector mismatch, missing protected route, or safe Phase 1 dependency. Record the solution separately from student materials.
Answer key follows underlay → IKE → IPsec selectors/counters → route → policy → return path. The final retest has bidirectional counters and service success.
Reset every fault and restore the known-good afternoon snapshot; morning tunnel and management stay untouched.

## Slide 135
135
Knowledge check — explain the result
QUESTION 1
• If encaps increases but decaps stays zero, what does it suggest?
QUESTION 2
• Why use a new five-tuple after a route change?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
135 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: If encaps increases but decaps stays zero, what does it suggest?; Why use a new five-tuple after a route change?
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: If encaps increases but decaps stays zero, what does it suggest?
A: Local traffic enters encryption but return protected traffic is not arriving; inspect remote routing/policy/peer path.
Q: Why use a new five-tuple after a route change?
A: Existing session state may retain the previous egress/policy decision.

## Slide 136
DAY 4 • 09:00–10:30
FortiClient Architecture & EMS Awareness
Advanced • Day 2 of 2
LEARNING OBJECTIVES
• Describe FortiClient components, VPN profiles and endpoint integration
• Explain EMS telemetry and centralized profile management
• Compare EMS and Intune by use case without claiming equivalence
PREREQUISITES + PRACTICE RESERVE
• No FortiClient/EMS infrastructure in the base lab
• Theory materials prepared
• Optional demo requires supported versions, license and a managed endpoint
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
136
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Describe FortiClient components, VPN profiles and endpoint integration; Explain EMS telemetry and centralized profile management; Compare EMS and Intune by use case without claiming equivalence
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 137
137
FortiClient is an endpoint platform with modular capabilities
ENDPOINT
FORTICLIENT MODULES
FORTIGATE / EMS
Treat “FortiClient installed” as insufficient scope; state the module and management mode
• Available modules depend on edition, platform, license and EMS policy
• VPN, endpoint telemetry, ZTNA and security features have separate prerequisites
• FortiGate remote-access settings and FortiClient profile must align
• Client logs show failures that the status icon does not explain
Record client version, OS, enabled features and profile source.
137 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Available modules depend on edition, platform, license and EMS policy; VPN, endpoint telemetry, ZTNA and security features have separate prerequisites; FortiGate remote-access settings and FortiClient profile must align; Client logs are essential state/output when GUI status is insufficient
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 138
138
VPN profiles encode gateway and authentication intent
• Profile defines gateway, tunnel type and user/certificate parameters as supported
• Split/full tunnel and DNS behavior affect traffic path
• MFA/SSO/certificate methods require matching FortiGate identity design
• Remote-access option support must be checked for exact FortiOS/FortiClient release
ILLUSTRATIVE SCENARIO
Use placeholders <vpn-gateway> and <auth-method>; do not invent tenant values
EXPECTED RESULT
Check client log, assigned address/routes/DNS and the FortiGate session.
Expected observation
The endpoint shows its assigned FortiClient profile and EMS connection; FortiGate logs the resulting access session.
138 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Profile defines gateway, tunnel type and user/certificate parameters as supported; Split/full tunnel and DNS behavior affect traffic path; MFA/SSO/certificate methods require matching FortiGate identity design; Remote-access option support must be checked for exact FortiOS/FortiClient release
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 139
139
EMS distributes FortiClient policy and receives endpoint telemetry
FortiGate still makes network/VPN access decisions from its configured policy
139
EMS
profiles • inventory telemetry • endpoint tags
policy / telemetry
FORTICLIENT
VPN • certificates posture / logs
VPN / ZTNA
FORTIGATE
auth • policy • session
application
PRIVATE APP
10.2.20.10
MANAGEMENT PLANE
EMS → assigned profile; endpoint → telemetry/status
ACCESS PATH
Endpoint traffic → FortiGate VPN/policy → application
EMS is not implied by installing FortiClient. Check the endpoint’s EMS connection and assigned profile.
LESSON
Correlate endpoint profile, client logs, EMS status and the FortiGate session rather than treating one console as the whole path.
Notes: Expected result: the endpoint is registered to the intended EMS, receives the assigned profile, and its VPN/access session appears on FortiGate. FortiClient/EMS exact release and licensing remain instructor review items. Source: official FortiClient EMS Administration Guide and FortiOS 7.6.7 Administration Guide — endpoint integration.

## Slide 140
140
Endpoint integration connects identity, posture and network policy
• Endpoint tags/posture can inform access policy where supported
• Certificate deployment and trust stores can enable deep inspection or VPN authentication
• Client upgrades/profile changes need staged rollout and rollback
• Privacy and endpoint-ownership boundaries must be documented
ILLUSTRATIVE SCENARIO
A managed device may receive VPN profile and inspection CA through different management systems
EXPECTED RESULT
Prove which system owns each control.
Expected observation
The endpoint shows its assigned FortiClient profile and EMS connection; FortiGate logs the resulting access session.
140 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Endpoint tags/posture can inform access policy where supported; Certificate deployment and trust stores can enable deep inspection or VPN authentication; Client upgrades/profile changes need staged rollout and rollback; Privacy and endpoint-ownership boundaries must be documented
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 141
141
Managed endpoint trust: EMS-specific context
CERTIFICATE INSPECTION
• EMS can distribute a supported certificate/profile
• FortiGate—not EMS—performs TLS inspection
DEEP INSPECTION
• Diagnose profile assignment and endpoint trust separately
• Inspection behavior was established in Day 2
KEY DISTINCTION
Default delivery is architecture analysis; use a live EMS demonstration only when the optional environment is built.
141 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Certificate inspection uses visible TLS metadata and does not decrypt payload; Deep inspection requires endpoint trust in the inspection CA and exposes payload to profiles; EMS can help distribute relevant FortiClient/endpoint policy in supported designs; Intune may distribute certificates/configuration, but it does not become EMS or replace FortiGate inspection policy
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 142
142
EMS and Intune overlap only in selected endpoint-management tasks
EMS FIT
• FortiClient profiles
• FortiClient telemetry
• ZTNA/network integration
INTUNE FIT
• Device enrollment
• Broad configuration/app policy
• Microsoft compliance ecosystem
COEXISTENCE
• Clear ownership
• Avoid duplicate settings
• Test precedence/rollback
KEY DISTINCTION
Map each requirement—VPN profile, CA, app compliance, FortiClient telemetry—to an accountable system
142 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: EMS is FortiClient-centric: profiles, telemetry and network-access integrations; Intune manages broader device/app/compliance configuration in Microsoft ecosystems; They can coexist: Intune enrolls/configures device; EMS manages FortiClient-specific posture/profile; Replacement is use-case specific; never claim blanket feature equivalence
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 143
143
Client troubleshooting correlates endpoint, EMS and FortiGate state
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
Endpoint: record FortiClient version/profile, route table and DNS EMS: confirm endpoint registration and assigned profile (if deployed) FortiGate: correlate auth/VPN/traffic session logs Use exact product documentation for log locations
READ THE OUTPUT
• Endpoint network state and routes/DNS
• FortiClient event/VPN logs
• EMS profile/telemetry status if used
• FortiGate authentication, VPN, policy and session logs
Safe operation
A client-side “connected” icon does not prove protected application reachability
143 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Endpoint network state and routes/DNS; FortiClient event/VPN logs; EMS profile/telemetry status if used; FortiGate authentication, VPN, policy and session logs
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 144
144
Managed VPN profile
144
01
Endpoint registers to EMS
02
EMS assigns profile
03
FortiClient applies gateway/auth
04
FortiGate authenticates
05
Session reaches application
EXPECTED RESULT
Learners place gateway, profile, telemetry and CA-trust decisions correctly; live state is optional.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Requirement: consistent VPN gateway and certificate trust; Choose EMS, Intune or coexistence based on ownership and supported controls; Deploy to a pilot group; Validate client and FortiGate state/output; Define rollback and help-desk signals
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 145
145
Common mistakes—and how to correct them
145
MISTAKE
CORRECTION — AND WHY IT HELPS
Assume installed FortiClient is EMS-managed
Check the EMS connection and assigned profile; installation alone is not centralized management.
Treat EMS and Intune as equivalent
Assign each requirement to the product that supports it; they overlap only for selected endpoint tasks.
Troubleshoot only FortiGate
Correlate client logs, endpoint routes/DNS, EMS profile and FortiGate session state.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 146
146
Troubleshooting workflow: narrow the failed decision
01
Confirm endpoint OS/client/version/license
02
Verify assigned profile and gateway reachability
03
Check authentication/certificate trust
04
Inspect client and EMS logs
05
Correlate FortiGate VPN, policy and session state
What to observe
• Check authentication/certificate trust
• Inspect client and EMS logs
• Correlate FortiGate VPN, policy and session state
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
146 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm endpoint OS/client/version/license; Verify assigned profile and gateway reachability; Check authentication/certificate trust; Inspect client and EMS logs; Correlate FortiGate VPN/policy/session state/output
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.

## Slide 147
147
Practical handoff: FortiClient / EMS Architecture Exercise
• START / PREREQUISITES: No EMS is assumed. Instructor provides architecture artefacts; live tenant/client only if built and licensed.
• CHANGE / INVESTIGATE: Map endpoint, FortiClient, EMS and FortiGate responsibilities; optionally observe profile assignment and logs.
• EXPECTED RESULT: Learners locate policy, telemetry, VPN and certificate-trust decisions in the correct component.
• CLEANUP / RESET: Remove demo profile/client artefacts only; no student pod change is required.
• DELIVERY: Theory plus optional instructor demonstration; conceptual architecture exercise by default.
PLANNED EXERCISE
Map endpoint, FortiClient, EMS and FortiGate responsibilities; optionally observe profile assignment and logs.
EXPECTED RESULT
Learners locate policy, telemetry, VPN and certificate-trust decisions in the correct component.
DELIVERY MODE
Theory plus optional demo
147 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: Default delivery: FortiClient/EMS theory plus optional instructor demonstration.
Base lab does not include EMS. Provide an architecture/profile/log artefact set. If a supported tenant, license and managed endpoint are built, demonstrate registration and profile assignment.
Answer key: EMS manages supported endpoint policy/telemetry; FortiClient applies the assigned profile; FortiGate makes gateway/policy/VPN decisions. CA distribution can support trust but does not move TLS inspection into EMS.
Reset optional demo artefacts only.

## Slide 148
148
Knowledge check — explain the result
QUESTION 1
• When can EMS and Intune coexist?
QUESTION 2
• What does FortiClient “connected” fail to prove?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
148 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: When can EMS and Intune coexist?; What does FortiClient “connected” fail to prove?
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Knowledge check answer key:
Q: When can EMS and Intune coexist?
A: When ownership is explicit—for example, Intune manages broad device configuration while EMS manages FortiClient-specific profiles and telemetry.
Q: What does FortiClient “connected” fail to prove?
A: That routes, DNS, FortiGate policy and the target application path are working end to end.

## Slide 149
DAY 4 • 10:30–12:00
FortiGate High Availability Fundamentals
Advanced • Day 2 of 2
LEARNING OBJECTIVES
• Explain FGCP prerequisites, heartbeat, election and synchronization
• Trace Active-Passive failover and session impact
• Separate appliance HA demonstration from cloud HA designs
PREREQUISITES + PRACTICE RESERVE
• Base lab: one FortiGate per student
• Dedicated instructor HA pair only if built
• Otherwise use the supplied event/configuration analysis
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
149
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain FGCP prerequisites, heartbeat, election and synchronization; Trace Active-Passive failover and session impact; Separate appliance HA demonstration from cloud HA designs
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Azure lab emphasis: use an Azure-supported HA design only if the required pair and Azure networking components are provisioned. The heartbeat, election and session-synchronization explanation also covers physical appliances, but cable/link demonstrations require separate hardware.

## Slide 150
150
Active/passive HA synchronizes state before a controlled failover
Physical appliance concepts shown; Azure deployment mechanics require the Fortinet Azure design
150
PRIMARY
forwarding traffic
SECONDARY
standby / synchronized
HEARTBEAT
health • election config/session sync
before
UPSTREAM / DOWNSTREAM
traffic via primary
after
UPSTREAM / DOWNSTREAM
traffic via new primary
FAILOVER TRIGGER
monitored failure → election → role change → adjacent-network convergence
LESSON
Session continuity depends on synchronized eligible state; role change alone does not guarantee zero application interruption.
Notes: Expected result: before failover, members are synchronized and one unit is primary; after the approved trigger, the secondary becomes primary and eligible sessions recover as designed. Azure HA requires the current Fortinet Azure architecture. Source: FortiOS 7.6.7 Administration Guide — FGCP HA, session pickup and failover; FortiGate-VM for Azure HA guide.

## Slide 151
151
Election selects the current primary using ordered criteria
• Priority, override behavior, monitored interfaces and uptime/state influence election according to configuration
• Preemption/override choices affect whether the preferred unit reclaims primary
• A stable cluster is more important than repeatedly forcing preferred ownership
• Document expected primary and the exact trigger for change
ILLUSTRATIVE SCENARIO
Predict election before disconnecting anything
EXPECTED RESULT
Show member state and election-relevant values on both units.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
151 • DAY 4 • BLOCK 14 • High Availability
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Priority, override behavior, monitored interfaces and uptime/state influence election according to configuration; Preemption/override choices affect whether the preferred unit reclaims primary; A stable cluster is more important than repeatedly forcing preferred ownership; Document expected primary and the exact trigger for change
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.

## Slide 152
152
Synchronization preserves cluster configuration and selected runtime state
• Most configuration is synchronized; some member-specific settings remain local
• Session pickup/session synchronization must be configured and supported for desired protocols/features
• Security engine and dynamic state behavior may vary during failover
• Checksum mismatch requires investigation before relying on redundancy
ILLUSTRATIVE SCENARIO
Configuration sync does not guarantee every session survives
EXPECTED RESULT
Compare cluster checksums and one test session before/after controlled failover.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
152 • DAY 4 • BLOCK 14 • High Availability
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Most configuration is synchronized; some member-specific settings remain local; Session pickup/session synchronization must be configured and supported for desired protocols/features; Security engine and dynamic state behavior may vary during failover; Checksum mismatch requires investigation before relying on redundancy
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.

## Slide 153
153
Monitored failures trigger role change only when configured
01
Failure detected
02
Heartbeat/election
03
New primary
04
L2/L3 convergence
05
Session recovery
What to observe
• Link-monitor/path health mechanisms may be needed beyond physical interface state
• Failover time includes detection, election, forwarding convergence and upstream learning
• Flapping monitored links can cause repeated disruption
INSTRUCTOR DEMONSTRATION
Declare the trigger, expected timer and convergence checkpoints before the test.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
153 • DAY 4 • BLOCK 14 • High Availability
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Heartbeat loss, monitored interface failure and device failure are distinct events; Link-monitor/path health mechanisms may be needed beyond physical interface state; Failover time includes detection, election, forwarding convergence and upstream learning; Flapping monitored links can cause repeated disruption
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.

## Slide 154
154
Session behavior depends on synchronization and traffic type
• Synced eligible sessions can continue with limited interruption
• Unsynchronized or unsupported sessions must be re-established
• NAT, IPsec, routing and authentication state have specific HA considerations
• Measure user impact, not only role change
ILLUSTRATIVE SCENARIO
A long-lived TCP stream and a new connection reveal different effects
EXPECTED RESULT
Track session on both members and packet loss during failover.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
154 • DAY 4 • BLOCK 14 • High Availability
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Synced eligible sessions can continue with limited interruption; Unsynchronized or unsupported sessions must be re-established; NAT, IPsec, routing and authentication state have specific HA considerations; Measure user impact, not only role change
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.

## Slide 155
155
Common HA faults cluster around prerequisites and Layer 2
• Firmware/model mismatch prevents expected formation
• Heartbeat VLAN/switch behavior can introduce loss or loops
• Duplicate management/IP design can make a healthy cluster appear unreachable
• Upstream/downstream MAC/ARP convergence can dominate outage time
ILLUSTRATIVE SCENARIO
Separate cluster health from surrounding-network convergence
EXPECTED RESULT
Capture heartbeat/role events plus adjacent switch/router state.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
155 • DAY 4 • BLOCK 14 • High Availability
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Firmware/model mismatch prevents expected formation; Heartbeat VLAN/switch behavior can introduce loss or loops; Duplicate management/IP design can make a healthy cluster appear unreachable; Upstream/downstream MAC/ARP convergence can dominate outage time
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.

## Slide 156
156
Cloud HA is a provider-integrated design, not an appliance clone
• Cloud instances lack physical heartbeat/transparent L2 assumptions in many designs
• Routing, load balancers, APIs and provider failover mechanisms may be required
• Licensing and bootstrap/state synchronization depend on marketplace/deployment model
• Use the exact Fortinet cloud deployment guide for the platform
ILLUSTRATIVE SCENARIO
A physical-appliance cable-pull does not validate Azure FGVM failover
EXPECTED RESULT
Cloud HA stays theory unless a dedicated instructor demo design, permissions and pair are provided.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
156 • DAY 4 • BLOCK 14 • High Availability
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B14-S156
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Cloud instances lack physical heartbeat/transparent L2 assumptions in many designs; Routing, load balancers, APIs and provider failover mechanisms may be required; Licensing and bootstrap/state synchronization depend on marketplace/deployment model; Use the exact Fortinet cloud deployment guide for the platform
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.

## Slide 157
157
Controlled HA failover
157
01
Confirm sync/primary
02
Start eligible test session
03
Trigger monitored failure
04
Secondary becomes primary
05
Measure application recovery
EXPECTED RESULT
With a demo pair: sync and failover state match prediction. Without it: learners diagnose the supplied event/configuration record.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Record primary/secondary and sync state; Generate an eligible test session; Trigger one approved monitored failure; Measure role, packet loss and session result; Restore and confirm stable resynchronization
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.

## Slide 158
158
Common mistakes—and how to correct them
158
MISTAKE
CORRECTION — AND WHY IT HELPS
Build HA from mismatched members
Match supported model/build/mode and HA settings before joining; compatibility is prerequisite.
Assume config sync means every session survives
Enable/verify supported session pickup and test the traffic type; runtime state varies.
Use appliance failover assumptions in Azure
Follow the Fortinet Azure HA architecture; cloud routing/load-balancing changes the mechanism.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.

## Slide 159
159
Troubleshooting workflow: narrow the failed decision
01
Check member compatibility and heartbeat
02
Confirm role/election and sync checksums
03
Inspect monitored failure event
04
Separate role change from network convergence
05
Validate session/application recovery and resync
What to observe
• Inspect monitored failure event
• Separate role change from network convergence
• Validate session/application recovery and resync
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
159 • DAY 4 • BLOCK 14 • High Availability
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check member compatibility and heartbeat; Confirm role/election and sync checksums; Inspect monitored failure event; Separate role change from network convergence; Validate session/application recovery and resync
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.

## Slide 160
160
Practical handoff: HA Demonstration or Event Analysis
• START / PREREQUISITES: Base lab has one FortiGate per student; dedicated instructor HA pair is optional.
• CHANGE / INVESTIGATE: Predict election, sync and session outcome; observe controlled failover if the pair exists, otherwise analyze events/config.
• EXPECTED RESULT: Learners identify primary/secondary state, failover trigger, synchronization status and expected session impact.
• CLEANUP / RESET: Return the demo pair to healthy synchronized state, or reset the analysis worksheet.
• DELIVERY: Instructor demonstration with a dedicated pair; event/configuration analysis by default.
PLANNED EXERCISE
Predict election, sync and session outcome; observe controlled failover if the pair exists, otherwise analyze events/config.
EXPECTED RESULT
Learners identify primary/secondary state, failover trigger, synchronization status and expected session impact.
DELIVERY MODE
Demo pair or event analysis
160 • DAY 4 • BLOCK 14 • High Availability
Notes: Default delivery: theory plus event/configuration analysis. Use a live demonstration only with a dedicated instructor HA pair.
Preparation for live demo: compatible pair, heartbeat links, synchronized config, monitored interface and recovery plan. Do not reuse student base units as an assumed pair.
Answer key: identify primary/secondary, sync state, election/failover trigger and session impact. Azure FGVM observations are distinct from physical FGCP/NP/CP behavior.
Reset demo pair to healthy synchronized state.

## Slide 161
161
Knowledge check — explain the result
QUESTION 1
• What is the heartbeat used for?
QUESTION 2
• Why can traffic remain interrupted after the secondary becomes primary?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
161 • DAY 4 • BLOCK 14 • High Availability
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What is the heartbeat used for?; Why can traffic remain interrupted after the secondary becomes primary?
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Knowledge check answer key:
Q: What is the heartbeat used for?
A: Member health, election and synchronization/control exchange between cluster units.
Q: Why can traffic remain interrupted after the secondary becomes primary?
A: Adjacent network convergence, unsynchronized sessions or dependent routing/security state may still be recovering.

## Slide 162
DAY 4 • 13:00–14:30
Fortinet SD-WAN & Design Considerations
Advanced • Day 2 of 2
LEARNING OBJECTIVES
• Build SD-WAN from members, zones, health checks and rules
• Predict SLA-based application path selection and failover
• Place FortiAnalyzer, FortiManager and security services without inventing entitlements
PREREQUISITES + PRACTICE RESERVE
• Default: worked two-path state scenarios
• Hands-on only with a second independently controllable path
• FortiAnalyzer/FortiManager covered as architecture/operations
Teach ~60 min • reserve ~30 min for guided activity, discussion and debrief
162
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Build SD-WAN from members, zones, health checks and rules; Predict SLA-based application path selection and failover; Place FortiAnalyzer, FortiManager and security services without inventing entitlements
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 163
163
SD-WAN selects a member from rule intent and measured SLA
Conceptual optional extension: two controllable paths; voice SLA values are illustrative
163
VOICE SESSION
10.1.10.10 → SaaS
SD-WAN RULE
voice → best-quality member
BEFORE DEGRADATION
ISP-A 18 ms / 4 ms / 0.2% ✓ ISP-B 35 ms / 8 ms / 0.4% ✕ latency
select A
ISP-A
selected egress
AFTER ISP-A DEGRADES
ISP-A 42 ms / 15 ms / 2.0% ✕ ISP-B 20 ms / 6 ms / 0.3% ✓
new → B
ISP-B
selected for new session
LESSON
Link-up is insufficient: the rule considers measured SLA, and existing sessions may behave differently from new sessions.
Notes: Illustrative values only. Expected result: before degradation, the new voice session uses ISP-A; after ISP-A fails the stated SLA, a new session uses ISP-B. Confirm actual egress in SD-WAN service state and session output. Source: FortiOS 7.6.7 Administration Guide — SD-WAN performance SLA and rules.

## Slide 164
164
Health checks must measure the service you care about
• Target should represent the path/service dependency, not only the next-hop router
• Latency, jitter and packet loss thresholds define SLA state as supported
• Probe interval/fail/recovery settings trade responsiveness against instability
• Multiple targets can reduce false positives but complicate interpretation
ILLUSTRATIVE SCENARIO
An ISP gateway can respond while SaaS path is impaired
EXPECTED RESULT
Compare raw measurements, SLA state and application experience.
Expected observation
The SD-WAN rule selects the member that meets the stated SLA, and the session egress matches that member.
164 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Target should represent the path/service dependency, not only the next-hop router; Latency, jitter and packet loss thresholds define SLA state as supported; Probe interval/fail/recovery settings trade responsiveness against instability; Multiple targets can reduce false positives but complicate interpretation
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 165
165
SLA criteria turn measurements into path eligibility
ISP-A
• 35 ms latency
• 0.5% loss
• SLA: fail for voice
ISP-B
• 18 ms latency
• 0.1% loss
• SLA: pass
RESULT
• Voice → ISP-B
• New session path
• Verify actual egress
CONCEPTUAL OPTIONAL EXTENSION
Two controllable paths are not in the base lab; in this worked scenario, the voice rule chooses B when its SLA passes.
165 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A member can be up but out of SLA; Rules can prefer, balance or choose based on quality/cost strategies as supported; Hysteresis/recovery behavior prevents oscillation; Existing sessions may remain pinned while new sessions choose differently
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 166
166
Application steering depends on identification timing
• Rules can use address/service/application constructs depending on design
• Application identity may be learned after initial packets
• Fallback/default rule must be intentional
• Security profiles and SSL visibility affect application identification
ILLUSTRATIVE SCENARIO
A first packet can use a provisional path before application is identified
EXPECTED RESULT
Use session details and logs to confirm the final matched rule/member.
Expected observation
The SD-WAN rule selects the member that meets the stated SLA, and the session egress matches that member.
166 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Rules can use address/service/application constructs depending on design; Application identity may be learned after initial packets; Fallback/default rule must be intentional; Security profiles and SSL visibility affect application identification
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 167
167
Failover is detection plus session/application recovery
01
SLA breach
02
Member ineligible
03
Rule recalculates
04
New egress
05
Application recovery
What to observe
• Rule removes or de-prioritizes member
• New sessions select another eligible path
• Existing session continuity depends on NAT, remote state and design
INSTRUCTOR DEMONSTRATION
Test new and long-lived flows separately.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
167 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Probe detects threshold breach; Rule removes or de-prioritizes member; New sessions select another eligible path; Existing session continuity depends on NAT, remote state and design
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 168
168
Verify the actual egress path, not the intended diagram
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
diagnose sys sdwan health-check diagnose sys sdwan service get router info routing-table details <destination> diagnose sys session filter dst <destination> diagnose sys session list
READ THE OUTPUT
• Check member/health-check state
• Confirm rule match and priority/strategy
• Inspect route/policy/session chosen interface
• Capture packets at candidate egresses
Safe operation
Use unique test tuple and timestamp to avoid stale session confusion
168 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check member/health-check state; Confirm rule match and priority/strategy; Inspect route/policy/session chosen interface; Capture packets at candidate egresses; Correlate traffic logs with SLA events
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 169
169
FortiAnalyzer and FortiManager solve different operational problems
FORTIOS
• Local config/GUI/CLI
• Routing, policy, SD-WAN
• Local logs within capacity
FORTIANALYZER
• Central logs/analytics
• Reports/incidents
• Retention architecture
FORTIMANAGER
• Central config/policy
• Templates/ADOM workflow
• Controlled deployment
KEY DISTINCTION
Architecture and operational positioning only; no FortiAnalyzer or FortiManager appliance is in the base lab
169 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: FortiAnalyzer centralizes logs, analytics and reporting workflows; FortiManager centralizes configuration, policy packages and controlled deployment; FortiOS includes local management, routing, SD-WAN and security capabilities subject to platform/build; Security services and cloud subscriptions add update/intelligence/management value; exact entitlement must be verified
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 170
170
Licensing boundaries are a validation task, not a memory test
• Base FortiOS feature availability varies by model/release
• FortiGuard services require relevant subscriptions and connectivity
• Manager/analyzer cloud/on-prem offerings have separate sizing and licensing
• Avoid promising retention, device counts or service entitlement without current documentation
ILLUSTRATIVE SCENARIO
Mark every design dependency as built-in, subscription, external platform or instructor-confirmed
EXPECTED RESULT
Create a validation checklist rather than a price/entitlement claim.
Expected observation
The SD-WAN rule selects the member that meets the stated SLA, and the session egress matches that member.
170 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B15-S170
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Base FortiOS feature availability varies by model/release; FortiGuard services require relevant subscriptions and connectivity; Manager/analyzer cloud/on-prem offerings have separate sizing and licensing; Avoid promising retention, device counts or service entitlement without current documentation
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 171
171
Confirm SD-WAN selection in SLA state, rule match and session egress
Conceptual optional extension — the second controllable path is not part of the base lab
171
1 HEALTH CHECK
Probe the service-relevant target. Record latency, jitter and loss.
2 SLA STATE
ISP-A: out of SLA ISP-B: in SLA
3 RULE MATCH
Voice rule removes A and chooses B
4 SESSION
Egress: ISP-B NAT: ISP-B address
BEFORE
voice session → ISP-A
AFTER
new voice session → ISP-B
Existing-session behavior depends on application/NAT/remote state; test long-lived and new flows separately.
LESSON
Do not stop at the intent diagram—confirm the matched SD-WAN rule and the actual session egress member.
Notes: Expected result: ISP-A reports out-of-SLA values, the voice rule selects ISP-B, and a new session shows ISP-B as egress with the expected source NAT. Source: FortiOS 7.6.7 Administration Guide — SD-WAN diagnostics and session verification.

## Slide 172
172
Common mistakes—and how to correct them
172
MISTAKE
CORRECTION — AND WHY IT HELPS
Probe only the ISP gateway
Probe a service-relevant target; a local gateway can stay up while the application path fails.
Expect an existing session to move seamlessly
Test both new and long-lived flows; NAT and remote state can require reconnection.
Assume managers are bundled
Check current licensing and architecture; FortiManager and FortiAnalyzer have distinct roles.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 173
173
Troubleshooting workflow: narrow the failed decision
01
Check member/link and probe reachability
02
Review SLA raw values and threshold state
03
Confirm matched SD-WAN rule
04
Inspect route, policy, session and NAT egress
05
Capture both links; test new session and recovery
What to observe
• Confirm matched SD-WAN rule
• Inspect route, policy, session and NAT egress
• Capture both links; test new session and recovery
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
173 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check member/link and probe reachability; Review SLA raw values and threshold state; Confirm matched SD-WAN rule; Inspect route, policy, session and NAT egress; Capture both links; test new session and recovery
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.

## Slide 174
174
Practical handoff: SD-WAN Path-Selection Exercise
• START / PREREQUISITES: Base lab has one controllable path; instructor provides two-path state tables unless a second path is built.
• CHANGE / INVESTIGATE: Predict member selection from rule/SLA state and verify the chosen path for new sessions in the supplied scenario.
• EXPECTED RESULT: The selected member follows the stated SLA/rule and the session egress matches the prediction.
• CLEANUP / RESET: Restore SLA/rule state or reset the worksheet; preserve shared Internet breakout.
• DELIVERY: Worked path-selection exercise; hands-on extension only with a second independently controllable path.
PLANNED EXERCISE
Predict member selection from rule/SLA state and verify the chosen path for new sessions in the supplied scenario.
EXPECTED RESULT
The selected member follows the stated SLA/rule and the session egress matches the prediction.
DELIVERY MODE
Worked scenario; hands-on optional
174 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: Default delivery: worked SD-WAN path-selection scenarios.
Base lab has one controllable path. Hands-on is an optional extension only when a second independently controllable path exists.
Answer key: health-check result changes member eligibility; rule chooses among eligible members; a new session confirms actual egress and NAT. Existing sessions may not move.
FortiAnalyzer/FortiManager are architecture and operational positioning only; no appliance is assumed.
Reset optional SLA/rule changes and preserve shared Internet breakout.

## Slide 175
175
Knowledge check — explain the result
QUESTION 1
• What is the difference between a member being up and in SLA?
QUESTION 2
• What proves the selected path?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
175 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What is the difference between a member being up and in SLA?; What proves the selected path?
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Knowledge check answer key:
Q: What is the difference between a member being up and in SLA?
A: Up indicates basic availability; in-SLA means measured criteria meet the rule’s thresholds.
Q: What proves the selected path?
A: Rule/service state plus session egress/NAT and packet or traffic-log state/output on the chosen member.

## Slide 176
DAY 4 • 14:30–16:00
Performance Optimization, Advanced Troubleshooting & Capstone
Advanced • Day 2 of 2
LEARNING OBJECTIVES
• Relate session scale, offload, inspection and resource use
• Troubleshoot CPU, memory and Conserve Mode from measured state
• Complete an integrated policy/routing/VPN/SD-WAN capstone
PREREQUISITES + PRACTICE RESERVE
• Read-only performance access
• Baseline or instructor-provided metrics
• Safe fault injection in an isolated lab only
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
176
Notes: Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Relate session scale, offload, inspection and resource use; Troubleshoot CPU, memory and Conserve Mode from state/output; Complete an integrated policy/routing/VPN/SD-WAN capstone
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 177
177
Session-table sizing begins with traffic behavior
• Concurrent sessions differ from new sessions per second
• Long-lived, idle and half-open sessions consume different operational attention
• NAT, inspection and logging add state/resources
• Use model datasheet and measured baseline; never copy a generic maximum into design
ILLUSTRATIVE SCENARIO
A branch with many short web sessions stresses setup rate differently from persistent VPN flows
EXPECTED RESULT
Compare session count/rate, timeout distribution and peak trend.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
177 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Concurrent sessions differ from new sessions per second; Long-lived, idle and half-open sessions consume different operational attention; NAT, inspection and logging add state/resources; Use model datasheet and measured baseline; never copy a generic maximum into design
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 178
178
Hardware offload validation must be platform specific
• Check whether the session and enabled features are eligible
• First packets and exception traffic can remain on CPU
• Azure FGVM performance uses VM/vNIC/cloud acceleration—not a physical NP/CP ASIC datapath
• A no-offload flag requires investigation; it is not automatically a misconfiguration
ILLUSTRATIVE SCENARIO
Physical NP/CP behavior is theory; Azure FGVM observations use VM counters and documented acceleration status
EXPECTED RESULT
Use model-specific documentation and session diagnostics.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
178 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S178
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check whether the session and enabled features are eligible; First packets and exception traffic can remain on CPU; VM acceleration uses hypervisor/cloud mechanisms rather than appliance NP/CP; A no-offload flag is state/output to investigate, not automatic misconfiguration
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 179
179
CPU troubleshooting starts with time and workload correlation
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
get system performance status diagnose sys top 1 20 diagnose sys session stat # Stop interactive top with the documented key sequence
READ THE OUTPUT
• Identify whether load is sustained or bursty
• Locate responsible processes/cores and traffic changes
• Correlate policy/profile, routing events, logging and session setup
• Record process, session and memory state before restarting or changing load
Safe operation
High CPU during an IPS update differs from sustained packet-processing saturation
179 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Identify whether load is sustained or bursty; Locate responsible processes/cores and traffic changes; Correlate policy/profile, routing events, logging and session setup; Avoid restarting before preserving state/output and understanding impact
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 180
180
Memory management requires trend, consumers and thresholds
• Track used memory, proxy buffers, sessions and process growth
• Conserve Mode is triggered by system memory thresholds and protects stability
• Entry/exit thresholds and behavior must be confirmed for exact build/model
• A reboot removes transient state and may only postpone recurrence
ILLUSTRATIVE SCENARIO
Collect event log, process and session state before mitigation
EXPECTED RESULT
Use release-specific Conserve Mode documentation and support guidance.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
180 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Track used memory, proxy buffers, sessions and process growth; Conserve Mode is triggered by system memory thresholds and protects stability; Entry/exit thresholds and behavior must be confirmed for exact build/model; A reboot removes state/output and may only postpone recurrence
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 181
181
Conserve Mode changes the troubleshooting priority
01
Threshold crossed
02
Protective behavior
03
Identify consumer
04
Scoped mitigation
05
Stable recovery
What to observe
• Identify whether sessions, proxy inspection or a process dominates
• Apply scoped mitigation and monitor exit/re-entry
• Escalate with timestamps, process samples and memory trends when a defect is suspected
INSTRUCTOR DEMONSTRATION
Resolution includes stable memory below recovery threshold and no recurring event.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
181 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: First protect stability and reduce unsafe load; Identify whether sessions, proxy inspection or a process dominates; Apply scoped mitigation and monitor exit/re-entry; Escalate with state/output when leak/defect is suspected
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 182
182
SSL inspection has measurable compute and compatibility cost
• Deep inspection adds TLS termination, certificate generation and content scanning
• Cipher suites, key sizes, session resumption and traffic mix affect cost
• Certificate inspection has lower visibility and generally lower processing cost
• Capacity planning must use representative encrypted traffic and enabled profiles
ILLUSTRATIVE SCENARIO
Measure throughput/latency/CPU with and without the intended profile in a controlled test
EXPECTED RESULT
Do not extrapolate one lab VM result to appliance capacity.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
182 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Deep inspection adds TLS termination, certificate generation and content scanning; Cipher suites, key sizes, session resumption and traffic mix affect cost; Certificate inspection has lower visibility and generally lower processing cost; Capacity planning must use representative encrypted traffic and enabled profiles
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 183
183
Security profiles consume resources according to traffic mix
• AV, IPS, Web and App Control engage different engines and update packages
• Encrypted traffic requires sufficient inspection visibility before content scanning
• Logging volume and disk/remote transport can become bottlenecks
• Profile tuning should preserve security requirements and use representative measurements
ILLUSTRATIVE SCENARIO
Optimize exclusions/signatures only with risk owner approval and rollback
EXPECTED RESULT
Compare security events, CPU/memory and user impact.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
183 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: AV, IPS, Web and App Control engage different engines and update packages; Encrypted traffic requires sufficient inspection visibility before content scanning; Logging volume and disk/remote transport can become bottlenecks; Profile tuning should preserve security requirements and use measured state/output
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 184
184
A layered workflow prevents random configuration changes
01
Symptom
02
Route
03
Policy/NAT
04
Overlay/SD-WAN
05
Profiles
06
Resources
What to observe
• Check policy/NAT/session
• Check VPN/SD-WAN/security-profile layers as applicable
• Check resource pressure and recent changes last/throughout
INSTRUCTOR DEMONSTRATION
Stop, reset and document debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
184 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Start with symptom and exact five-tuple/time; Check physical/interface and routing; Check policy/NAT/session; Check VPN/SD-WAN/security-profile layers as applicable; Check resource pressure and recent changes last/throughout
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 185
185
Enterprise Branch Incident uses the actual Student N pod
LINUX LAN CLIENT
10.N.10.10
STUDENT N FGT
p2 10.N.10.4 • p3 10.N.20.4
POLICY • ROUTE
SECURITY INSPECTION
INSTRUCTOR HUB / NVA
FGT p1 10.0.0.4 • NVA 10.0.40.4
LINUX DMZ SERVER
10.N.20.10
Mandatory path uses the validated Student N LAN/DMZ baseline; shared management access stays protected
• Client 10.N.10.10 → FortiGate port2 10.N.10.4
• DMZ server 10.N.20.10 → FortiGate port3 10.N.20.4
• Internet path uses NVA 10.0.40.4 and Instructor FGT 10.0.0.4
• Pod addressing is fixed and validated
Existing: FortiGate-VM, Linux endpoints and routed underlay • Future: IPsec/ADVPN overlay • Optional: SD-WAN, HA and EMS
185 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Mandatory capstone uses the validated base pod: client 10.N.10.10, FortiGate p2 10.N.10.4 and p3 10.N.20.4, DMZ server 10.N.20.10. Internet breakout uses Transit NVA 10.0.40.4 and Instructor FortiGate 10.0.0.4. The IPsec/ADVPN overlay is future work and must not be required.

## Slide 186
186
Enterprise Branch Incident: the protected service fails
• Linux client 10.N.10.10 cannot complete the assigned HTTP/HTTPS test to DMZ server 10.N.20.10
• Management access and shared Internet breakout must remain intact
• Faults may involve policy/object, local route/return path, or certificate trust/security inspection
• Change only one variable at a time
MANDATORY SCENARIO
Start from the validated Student N FortiGate, client and DMZ server baseline
EXPECTED RESULT
Localize the failed decision, apply one reversible fix, and restore the assigned service without harming management.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
186 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: User reports HTTPS timeout to branch application; DNS answer is correct and must be recorded; Traffic may fail at policy, overlay route, SD-WAN rule or resource pressure; Teams must avoid changing more than one variable at a time
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 187
187
Mandatory faults stay inside the completed base platform
• Policy/object: wrong service, address or ordering
• Routing: wrong local inter-zone/return-path decision
• Inspection: wrong SSL profile or untrusted inspection CA
• Future/optional variants only: VPN overlay, SD-WAN, HA or EMS
INSTRUCTOR-SELECTED FAULT SET
Inject only faults that were prevalidated against the current snapshot; solutions remain in notes
EXPECTED RESULT
The mandatory capstone does not depend on IPsec/ADVPN, a second WAN path, HA, EMS, FortiAnalyzer or FortiManager.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
187 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Instructor-only fault menu and solutions.
Policy/object: wrong service/address/order → compare exact tuple and matched policy; restore approved object/policy.
Routing: missing/wrong protected prefix → verify lookup; restore expected overlay route.
VPN: disabled test policy or selector dependency → verify SA/selectors/counters; restore known-good tunnel dependency.
Inspection trust: deep-inspection profile with untrusted CA → install the prepared CA or restore certificate-inspection baseline as directed.
Inject only prevalidated faults. Do not require SD-WAN, HA, EMS, FortiAnalyzer or FortiManager for the mandatory case.

## Slide 188
188
Capstone record connects every relevant layer
• Student N tuple, timestamp and expected local path
• Route and return-path decision
• Matched policy, objects, NAT and session state
• Certificate chain/profile action for HTTPS
• Relevant capture/log output and reset checkpoint
ILLUSTRATIVE SCENARIO
Screenshots alone need labels and context; CLI output must be captured from the actual lab
EXPECTED RESULT
Teams submit a concise before/after state table and the exact reset they performed.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
188 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Exact test tuple, timestamp and expected path; Route/PBR/SD-WAN decision; Matched policy, NAT and session state; VPN SA/selectors/counters when used; Packet/log state/output and CPU/memory status
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 189
189
Capstone workflow: localize before remediation
• Reproduce once and freeze the test definition
• Predict the local route, policy and inspection state
• Collect minimally invasive diagnostics
• Name the failed decision and proposed change
• Apply approved change; retest; restore the injected-fault baseline
ILLUSTRATIVE SCENARIO
Use fresh five-tuple after route/policy changes to avoid stale session state
EXPECTED RESULT
Document every disruptive command.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
189 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Reproduce once and freeze the test definition; Predict path using route, policy and overlay state; Collect minimally invasive state/output; Name the failed decision and proposed change; Apply approved change; retest; restore injected fault baseline
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 190
190
Capstone resolution criteria are observable
• Expected local route/interface selected
• Correct object, policy, NAT and security profile applied
• Bidirectional packets and session counters increase
• HTTPS trust is correct when deep inspection is used
• Intentional faults removed; management and Internet breakout still work
ILLUSTRATIVE SCENARIO
“Ping works” is not sufficient for HTTPS success
EXPECTED RESULT
Success includes service restoration and a verified clean reset to the known-good baseline.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
190 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Expected route/member/tunnel selected; Correct policy/VIP/NAT and security profile applied; Bidirectional packets and session byte counters increase; Application succeeds without Conserve Mode or abnormal resource trend; Rollback remains available and intentional faults are removed
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 191
191
Capstone checkpoint: policy and NAT
Mandatory Student N exercise—client 10.N.10.10 and DMZ server 10.N.20.10
191
01
Which policy ID should match the test tuple?
02
Is NAT required, and what should the translated tuple be?
03
Which traffic-log fields distinguish deny, accept and security-profile action?
LESSON
Do not reveal the injected fault; require the team to connect each conclusion to the actual lab state.
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S191
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Expected result: route and tunnel are healthy; debug/log shows deny or wrong policy/service; Fix: restore intended lab object/policy order/action; Retest: new HTTPS tuple matches intended policy and logs accept; Debrief: route reachability did not imply policy permission
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 192
192
Capstone checkpoint: route and return path
Mandatory base-lab exercise; the future IPsec/ADVPN overlay is not required
192
01
Which route/interface should carry LAN-to-DMZ traffic?
02
Does the DMZ server return through 10.N.20.4?
03
Which session counters or captures identify the failing direction?
LESSON
Do not reveal the injected fault; require the team to connect each conclusion to the actual lab state.
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S192
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Expected result: policy is plausible but route selects wrong interface or Phase 2 counters are one-sided; Fix: restore exact lab route or reciprocal selector/return route; Retest: tunnel counters increase both directions and session uses tunnel; Debrief: Phase 1 up did not prove the protected subnet path
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 193
193
Capstone checkpoint: inspection trust and resources
Mandatory base-lab checks; SD-WAN, HA and EMS are optional variants
193
01
Which SSL profile and certificate chain should the HTTPS flow use?
02
Does the Linux client trust the inspection CA when deep inspection is enabled?
03
Are session counters, logs, CPU and memory consistent with the restored service?
LESSON
Keep optional infrastructure out of the mandatory fault path; verify CA trust before changing policy or routing.
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S193
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Expected result: rule/SLA selects degraded member, or instructor snapshot shows memory protection event; Fix: correct lab SLA target/rule or apply scoped resource mitigation per runbook; Retest: new session uses healthy member; memory remains stable below recovery threshold; Debrief: link-up and role state were incomplete state/output
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 194
194
Operational escalation package makes support efficient
• State model, exact FortiOS build and topology
• Give timestamps, timezone, symptom and reproduction
• Include filtered diagnostics and before/after change record
• Remove credentials/private data and identify business impact
ILLUSTRATIVE SCENARIO
A timestamped, reproducible diagnostic bundle is more useful than a long unfiltered debug
EXPECTED RESULT
Follow organizational and Fortinet support data-collection guidance.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
194 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S194
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: State model, exact FortiOS build and topology; Give timestamps, timezone, symptom and reproduction; Include filtered diagnostics and before/after change record; Remove credentials/private data and identify business impact
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 195
195
Enterprise Branch Incident
195
01
Define tuple and symptom
02
Check route / local path
03
Check policy/NAT/session
04
Check inspection trust / resources
05
Apply one reversible fix
EXPECTED RESULT
The assigned service works bidirectionally, the failed decision is explained, and every intentional fault is removed.
LESSON
The mandatory workflow uses the validated Student N pod; VPN, SD-WAN, HA and EMS variants are future/optional extensions.
Notes: Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Teams receive symptom plus one or two declared achievable faults; They predict expected path and collect route/policy/session/overlay/resource state/output; They propose one reversible change; They prove restoration and remove intentional faults; Class compares state/output quality and false leads
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 196
196
Common mistakes—and how to correct them
196
MISTAKE
CORRECTION — AND WHY IT HELPS
Change policy, route and tunnel together
Change one layer at a time with rollback; otherwise the causal fix is unknown.
Restart before recording the failure
Capture route/session/protocol/resource state first; restart destroys transient clues.
Use FGVM results as appliance capacity data
Use model data sheets and representative appliance testing; VM results do not prove ASIC capacity.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 197
197
Troubleshooting workflow: narrow the failed decision
01
Define tuple/time/symptom
02
Check route/PBR/SD-WAN/VPN state
03
Check policy/NAT/session/logs
04
Check packet direction and security profile
05
Check CPU/memory/Conserve events and validate one reversible fix
What to observe
• Check policy/NAT/session/logs
• Check packet direction and security profile
• Check CPU/memory/Conserve events and validate one reversible fix
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
197 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Define tuple/time/symptom; Check route/PBR/SD-WAN/VPN state; Check policy/NAT/session/logs; Check packet direction and security profile; Check CPU/memory/Conserve events and validate one reversible fix
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.

## Slide 198
198
Practical handoff: Enterprise Branch Incident
• START / PREREQUISITES: Validated Student N FortiGate, Linux client 10.N.10.10, DMZ server 10.N.20.10 and known-good snapshot.
• CHANGE / INVESTIGATE: Diagnose achievable policy/object, local routing/return-path and certificate-trust/security-inspection faults.
• EXPECTED RESULT: The assigned service works bidirectionally and policy, route, session and inspection state match the expected local path.
• CLEANUP / RESET: Remove every intentional fault and confirm management plus Internet breakout.
• DELIVERY: Mandatory hands-on base-lab capstone; VPN, SD-WAN, HA and EMS are future/optional variants.
PLANNED EXERCISE
Diagnose policy/object, local route/return path and certificate-trust/security-inspection faults using Student N addressing.
EXPECTED RESULT
Required service works bidirectionally; route, policy, session and inspection state match the expected local path.
DELIVERY MODE
Mandatory base lab; future/optional variants
198 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Enterprise Branch Incident mandatory faults must stay inside the validated base lab: policy/object, local route/return path, session/NAT and certificate trust/security inspection. VPN/ADVPN, SD-WAN, HA and EMS are future or optional extensions only.

## Slide 199
199
Knowledge check — explain the result
QUESTION 1
• What is the first deliverable in the capstone?
QUESTION 2
• When is the incident resolved?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
199 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What is the first deliverable in the capstone?; When is the incident resolved?
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Knowledge check answer key:
Q: What is the first deliverable in the capstone?
A: A precise symptom/test definition: timestamp, five-tuple, expected path and success criterion.
Q: When is the incident resolved?
A: When the intended path/policy/overlay is proven, bidirectional application traffic succeeds, resources are stable and injected faults are removed with rollback retained.

## Slide 200
COURSE WRAP-UP
Operate from packet state, logs and protocol state
A complete diagnosis connects packet fields to route, policy, session, overlay, inspection and resource state.
01
Every block includes theory, a worked mechanism, mistakes, troubleshooting, practical handoff and knowledge check
02
Advanced coverage completes BGP, IPsec/ADVPN, VPN validation, FortiClient/EMS, HA, SD-WAN and performance
03
Optional deep dives are marked in notes; practice time is protected
04
Instructor validates FortiOS 7.6.7 build, platform, licensing and lab topology before delivery
Final Q&A • capstone debrief • remove intentional faults • retain diagnostics and rollback
Notes: Approximate timing: 5–10 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Every block includes theory, worked state/output, mistakes, troubleshooting, practical handoff and knowledge check; Advanced coverage completes BGP, IPsec/ADVPN, VPN validation, FortiClient/EMS, HA, SD-WAN and performance; Optional deep dives are marked in notes; practice time is protected; Instructor validates FortiOS 7.6.7 build, platform, licensing and lab topology before delivery
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Knowledge check answer key:
Q: What state/output chain should a FortiGate administrator build?
A: Tuple/time → route/PBR/SD-WAN/VPN → policy/NAT/session → packet/log/profile → CPU/memory state.
Q: What remains to be confirmed before delivery?
A: Exact FortiOS 7.6.x build, platform/model, feature support, licensing and actual lab resources.

## Slide 201
FortiGate Foundations + Advanced | Lab: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
201
Instructor preparation: what changed in version 1.5
LAB-ALIGNED
Actual instructor and Student N addressing replaces the generic HQ/branch reference design; endpoint IPs remain assigned placeholders.
EXERCISES
All 16 practical handoffs now name the planned activity, start state, expected result, reset and delivery mode.
DEPENDENCIES
Morning routing uses a required prepared tunnel; afternoon VPN uses a separate tunnel or isolated baseline.
OPTIONALITY
EMS, HA and dual-path SD-WAN are accurately labelled; capstone mandatory faults stay inside the base lab.
CHANGE SUMMARY
INSTRUCTOR APPENDIX
Notes: Version 1.4 change summary for instructors only. The source architecture, status and exercise constraints are based on the supplied Fortinet training-lab mapping requirements. Keep this appendix out of normal student delivery.

## Slide 202
FortiGate Foundations + Advanced | Lab: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
202
Instructor preparation decisions before delivery
DECLARED LAB BASELINE
• Confirm Student01–Student08 access URL/SSH target and credentials
• Record Guacamole as TBD until deployed and validated
• Provision browser-download storage or a tested SFTP destination
• Retain per-pod known-good FortiOS 7.6.7 exports
SAFE LAB BOUNDARIES
• Test backup/restore compatibility and recovery access
• Pre-stage the exact FGVM firmware image only for an instructor demo
• Read release notes and upgrade path; document post-reboot checks
• Never restore a file across pods without reviewing addresses
OPTIONAL CONTEXT
• Keep management interfaces, baseline routes and shared infrastructure out of the student CLI exercise
• Store real credentials and backup encryption passwords outside slides
• Record unresolved menu placement or transfer-service details in the runbook
Current sources: Architecture.md, Deployment.md and Instructor-Guide.md • Guacamole and SFTP destination remain TBD.
ASSUMPTIONS + VALIDATION
INSTRUCTOR APPENDIX
Notes: Unresolved preparation: final access URLs/SSH targets and credential delivery; Guacamole deployment; backup storage destination; SFTP service/host/account/reachability; configuration scope and encryption policy; tested restore and emergency-access procedure; authorized FGVM firmware image and upgrade/recovery procedure. The three attached lab documents intentionally do not establish these details.

## Slide 203
FortiGate Foundations + Advanced | Lab: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
203
Coverage matrix — blocks 1–8
All eight Foundations blocks retained; practical handoffs are lab-aligned
# | DAY | SLIDES | BLOCK
1 | 1 | 4–13 | Network Foundations & FortiGate Packet Flow
2 | 1 | 14–27 | FortiGate Introduction, Basic Administration & CLI
3 | 1 | 28–37 | Segmentation, Zones & Firewall Policy Design
4 | 1 | 38–47 | NAT, Logging & CLI Troubleshooting
5 | 2 | 48–57 | Routing Fundamentals & Route Selection
6 | 2 | 58–67 | Object Management & Policy Design Best Practices
7 | 2 | 68–77 | Security Services & SSL Inspection
8 | 2 | 78–86 | Hardware Architecture, Monitoring & Operations
COVERAGE MATRIX • BLOCKS 1–8
INSTRUCTOR APPENDIX
Notes: Coverage matrix verified after Day 1 Block 2 expansion. All 16 blocks remain covered. Day 1 Block 2 now spans slides 14–27; all subsequent block ranges shift by four slides.

## Slide 204
FortiGate Foundations + Advanced | Lab: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
204
Coverage matrix — blocks 9–16
All eight Advanced blocks retained; prerequisites and optional capabilities are explicit
# | DAY | SLIDES | BLOCK
9 | 3 | 87–96 | Route Selection, PBR & OSPF
10 | 3 | 97–109 | BGP Fundamentals & Practical Use
11 | 3 | 110–122 | IPsec VPN Architecture & ADVPN
12 | 3 | 123–135 | VPN Troubleshooting & Operational Validation
13 | 4 | 136–148 | FortiClient Architecture & EMS Awareness
14 | 4 | 149–161 | FortiGate High Availability Fundamentals
15 | 4 | 162–175 | Fortinet SD-WAN & Design Considerations
16 | 4 | 176–199 | Performance, Troubleshooting & Capstone
COVERAGE MATRIX • BLOCKS 9–16
INSTRUCTOR APPENDIX
Notes: Coverage matrix verified after Day 1 Block 2 expansion. All 16 blocks remain covered. Day 1 Block 2 now spans slides 14–27; all subsequent block ranges shift by four slides.