## Slide 1
FORTIGATE
Administrator Course
Foundations + Advanced • v1.3
Four days • 16 instructor-led blocks • theory with practical handoffs
Lab baseline: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
09:00–16:00 daily | Four 90-minute blocks per day
Editable theory deck • illustrative addressing • observable packet and protocol behavior
Notes: [CORE LECTURE] Stable ID: D1-B01-S001
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Four-day instructor-led theory course; Days 1–2 Foundations; Days 3–4 Advanced
Instructor demonstration / expected result: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Course cover” before showing the answer.

## Slide 2
2
Four days build from packet behavior to integrated operations
Every 90-minute block reserves time for practice and discussion
DAY 1
09:00–10:30
Network Foundations & FortiGate Packet Flow
10:30–12:00
FortiGate Introduction & Initial Configuration
13:00–14:30
Segmentation, Zones & Firewall Policy Design
14:30–16:00
NAT, Logging & CLI Troubleshooting
DAY 2
09:00–10:30
Routing Fundamentals & Route Selection
10:30–12:00
Object Management & Policy Design Best Practices
13:00–14:30
Security Services & SSL Inspection
14:30–16:00
FortiGate Hardware Architecture, Monitoring & Operations
DAY 3
09:00–10:30
Route Selection, PBR & OSPF
10:30–12:00
BGP Fundamentals & Practical Use
13:00–14:30
IPsec VPN Architecture & ADVPN
14:30–16:00
VPN Troubleshooting & Operational Validation
DAY 4
09:00–10:30
FortiClient Architecture & EMS Awareness
10:30–12:00
FortiGate High Availability Fundamentals
13:00–14:30
Fortinet SD-WAN & Design Considerations
14:30–16:00
Performance Optimization, Advanced Troubleshooting & Capstone
COURSE MAP
Notes: [CORE LECTURE] Stable ID: D1-B01-S002
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Four 90-minute blocks each day; Days 1–2 Foundations; Days 3–4 Advanced; Practice and debrief are protected within every block
Instructor demonstration / expected result: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Four-day map” before showing the answer.

## Slide 3
003
Reference topology for all worked examples
Illustrative RFC 1918 and documentation ranges; Azure interface names remain instructor-supplied
3
HQ USERS
10.10.10.0/24
HTTPS / DNS
HQ FGVM
LAN 10.10.10.1 DMZ 10.10.20.1
DMZ SERVER
10.10.20.10
underlay
AZURE WAN
ISP-A 203.0.113.0/30 ISP-B 198.51.100.0/30
IPsec
BRANCH FGVM
overlay endpoint
HTTPS
BRANCH SERVER
10.20.10.50
LOGICAL OVERLAY
Protected prefixes: 10.10.10.0/24 ↔ 10.20.10.0/24
LESSON
Use the same addresses throughout the course; separate Azure underlay reachability from VPN/SD-WAN overlay decisions.
Notes: Instructor preparation: map the illustrative interfaces to the actual Azure FortiGate-VM NICs, VNets, subnets, NSGs and UDRs. Do not infer a deployed topology. Source: FortiOS 7.6.7 Administration Guide — Azure deployment, routing, IPsec VPN and SD-WAN topics.

## Slide 4
DAY 1 • 09:00–10:30
Network Foundations & FortiGate Packet Flow
Foundations • Day 1 of 2
LEARNING OBJECTIVES
• Explain packet fields, DNS, TCP/UDP and forwarding decisions
• Trace a new session through FortiGate decision stages
• Distinguish flow/proxy inspection and locate implicit deny
PREREQUISITES + PRACTICE RESERVE
• Basic IPv4 subnetting
• Illustrative topology on slide 3
• GUI/CLI access is demonstrated in the next block
Teach ~54 min • reserve ~36 min for guided activity, discussion and debrief
008
Notes: [CORE LECTURE] Stable ID: D1-B01-S008
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain packet fields, DNS, TCP/UDP and forwarding decisions; Trace a new session through FortiGate decision stages; Distinguish flow/proxy inspection and locate implicit deny
Instructor demonstration / expected result: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Network Foundations & FortiGate Packet Flow” before showing the answer.

## Slide 5
5
The five-tuple is the identity of a unidirectional flow
FortiGate session matching begins with concrete packet fields, not application names
FIELD | EXAMPLE | WHY IT MATTERS
Source IP | 10.10.10.25 | Which host originated the packet
Destination IP | 203.0.113.80 | Which host the packet targets
Source port | 51514 | Ephemeral client-side transport port
Destination port | 443 | Service endpoint; not proof of the application
Protocol | TCP (6) | Separates TCP from UDP/ICMP flows
SESSION CONSEQUENCE
The return packet reverses source and destination. FortiGate associates it with the existing session and applies the stored policy, NAT and security state.
Worked packet
10.10.10.25:51514 → 203.0.113.80:443 / TCP Return: 203.0.113.80:443 → translated client tuple
Validate: diagnose sys session filter src 10.10.10.25; diagnose sys session list
009 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: [CORE LECTURE] Stable ID: D1-B01-S009
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Source and destination IP locate endpoints; Source and destination ports identify transport sockets; Protocol distinguishes TCP, UDP, ICMP and others; Reverse traffic is associated with the created session
Instructor demonstration / expected result: Filter the session table by source and inspect the forward/reverse tuple.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “The five-tuple defines a transport conversation” before showing the answer.

## Slide 6
6
DNS turns names into routable destinations
01
Client query
02
Resolver cache
03
Authority lookup
04
Answer + TTL
What to observe
• Recursive resolution follows cache, root, TLD and authoritative data as needed
• A/AAAA answers provide addresses; TTL controls cache lifetime
• DNS success does not prove policy or route success to the returned address
INSTRUCTOR DEMONSTRATION
Use a filtered packet capture on UDP/TCP 53 and compare query, response and TTL.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
010 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: [CORE LECTURE] Stable ID: D1-B01-S010
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Client asks a resolver, not the authoritative server directly in most enterprise designs; Recursive resolution follows cache, root, TLD and authoritative data as needed; A/AAAA answers provide addresses; TTL controls cache lifetime; DNS success does not prove policy or route success to the returned address
Instructor demonstration / expected result: Use a filtered packet capture on UDP/TCP 53 and compare query, response and TTL.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “DNS turns names into routable destinations” before showing the answer.

## Slide 7
007
TCP handshake creates state that return traffic can reuse
New connection: client 10.10.10.25:51514 → server 203.0.113.80:443
7
CLIENT
10.10.10.25:51514
FORTIGATE
policy 12 • session 0042
SERVER
203.0.113.80:443
1 SYN →
1 SYN →
2 ← SYN-ACK
2 ← SYN-ACK
3 ACK →
3 ACK →
SESSION CREATED
The entry stores policy, route, NAT and TCP state. Return packets match the reverse tuple.
LESSON
Stateful inspection does not “trust replies”; it associates the reverse five-tuple with an existing allowed session.
Notes: Expected result: after the SYN is accepted, diagnose sys session list shows the original and reply tuples; reply packet/byte counters increase after SYN-ACK. Source: FortiOS 7.6.7 Administration Guide — Sessions and TCP session handling.

## Slide 8
008
New sessions take the full path; established sessions reuse state
Simplified teaching view—feature/platform exceptions exist
8
NEW SESSION
Ingress
packet + interface
Route/PBR
candidate egress
Policy
first matching rule
NAT
original ↔ translated
Inspection
profiles as configured
Create session
store decisions
ESTABLISHED SESSION
Reverse tuple
reply packet
Session lookup
policy/NAT/egress state
Forward + inspect
according to stored state
Update counters
bytes / timeout / TCP
Local-in traffic, proxy behavior, tunnels, hardware offload and special features can add or change stages.
LESSON
Use this as a troubleshooting map, not as a universal implementation pipeline.
Notes: Technical question for instructor review: compare this simplified teaching order with the exact FortiOS 7.6.7 “Life of a packet” documentation and features enabled in the Azure lab. Source: FortiOS 7.6.7 Administration Guide — Life of a packet, policy routes, firewall policy, NAT and security profiles.

## Slide 9
009
First HTTPS session
9
01
SYN enters LAN
02
Route selects WAN
03
Policy 12 accepts
04
SNAT creates reply tuple
05
SYN-ACK matches session
EXPECTED RESULT
A session entry shows the original tuple and the return packets increment the reply counters.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D1-B01-S013
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Packet arrives on LAN; source/destination and ingress interface are known; Route lookup identifies WAN and next hop; First-match policy permits traffic and applies SNAT; Session records original and translated tuples; security profiles inspect as configured
Instructor demonstration / expected result: Use debug flow filters plus session lookup; stop debug after the observation.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Worked flow: first HTTPS session” before showing the answer.

## Slide 10
010
Common mistakes—and how to correct them
10
MISTAKE
CORRECTION — AND WHY IT HELPS
DNS success proves the application path
Test the returned IP and TCP handshake; DNS only proves name resolution.
Port 443 proves HTTPS
Inspect the handshake/application state; a port number identifies a socket, not the application.
Policy is the only forwarding decision
Check route and return path first; policy cannot repair an absent route.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D1-B01-S014
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 11
11
Troubleshooting workflow: narrow the failed decision
01
Reproduce one flow and record its five-tuple
02
Check route and neighbor reachability
03
Identify the matched policy and NAT decision
04
Confirm session creation and reverse traffic
05
Use filtered sniffer/debug only if route, session and logs are inconclusive
What to observe
• Identify the matched policy and NAT decision
• Confirm session creation and reverse traffic
• Use filtered sniffer/debug only if route, session and logs are inconclusive
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
015 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: [CORE LECTURE] Stable ID: D1-B01-S015
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Reproduce one flow and record its five-tuple; Check route and neighbor reachability; Identify the matched policy and NAT decision; Confirm session creation and reverse traffic; Use filtered sniffer/debug only if earlier state/output is inconclusive
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 12
12
Practical handoff: predict, observe, explain
• Prerequisite: Basic IPv4 subnetting
• Prerequisite: Illustrative topology on slide 3
• Goal: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; capture: route, policy ID, session tuple and bidirectional packets.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; capture: route, policy ID, session tuple and bidirectional packets.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
A session entry shows the original tuple and the return packets increment the reply counters.
016 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: [CORE LECTURE] Stable ID: D1-B01-S016
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Basic IPv4 subnetting; Prerequisite: Illustrative topology on slide 3; Goal: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 13
13
Knowledge check — explain the result
QUESTION 1
• Which five values identify a TCP/UDP flow?
QUESTION 2
• Why can a return packet bypass a second full policy decision?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
017 • DAY 1 • BLOCK 01 • Network Foundations & Packet Flow
Notes: [CORE LECTURE] Stable ID: D1-B01-S017
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Which five values identify a TCP/UDP flow?; Why can a return packet bypass a second full policy decision?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: Which five values identify a TCP/UDP flow?
A: Source IP, destination IP, source port, destination port and IP protocol.
Q: Why can a return packet bypass a second full policy decision?
A: It matches established session state containing the stored forwarding, policy and NAT decisions.

## Slide 14
DAY 1 • 10:30–12:00
FortiGate Introduction & Initial Configuration
Foundations • Day 1 of 2
LEARNING OBJECTIVES
• Locate FortiGate in the Fortinet ecosystem and FortiOS management model
• Configure interfaces, administrative access and DNS safely
• Back up, restore and validate an initial configuration
PREREQUISITES + PRACTICE RESERVE
• Console or authorized management network
• Instructor-supplied credentials and interface mapping
• Maintenance window for restore demonstrations
Teach ~52 min • reserve ~38 min for guided activity, discussion and debrief
018
Notes: [CORE LECTURE] Stable ID: D1-B02-S018
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Locate FortiGate in the Fortinet ecosystem and FortiOS management model; Configure interfaces, administrative access and DNS safely; Back up, restore and validate an initial configuration
Instructor demonstration / expected result: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “FortiGate Introduction & Initial Configuration” before showing the answer.

## Slide 15
15
FortiOS combines forwarding, policy and security services
ADMIN
FORTIOS config + state
FORTIGUARD / MANAGERS
Use standalone FortiGate first; introduce managers as design choices, not prerequisites
• FortiGate enforces policy; FortiManager centralizes configuration workflows; FortiAnalyzer centralizes analytics/logging
• GUI and CLI operate on the same configuration database
• VDOMs can partition administration and forwarding when enabled
• Feature visibility changes the GUI, not underlying platform support
get system status; confirm serial/model/build and operation mode.
019 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Notes: [CORE LECTURE] Stable ID: D1-B02-S019
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: FortiGate enforces policy; FortiManager centralizes configuration workflows; FortiAnalyzer centralizes analytics/logging; GUI and CLI operate on the same configuration database; VDOMs can partition administration and forwarding when enabled; Feature visibility changes the GUI, not underlying platform support
Instructor demonstration / expected result: get system status; confirm serial/model/build and operation mode.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “FortiOS combines forwarding, policy and security services” before showing the answer.

## Slide 16
16
Management access must be deliberately bounded
GUI
• HTTPS session
• Role-scoped navigation
• Good for discovery and visual status
CLI
• SSH/console
• Scriptable and exact
• Required for many diagnostics
KEY DISTINCTION
Management station <admin-ip> reaches <mgmt-interface>; internet hosts must not
020 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Notes: [CORE LECTURE] Stable ID: D1-B02-S020
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Interface IP/mask establishes local reachability; Administrative access protocols are enabled per interface; Trusted hosts and administrative profiles restrict who can log in and what they can do; HTTPS/SSH are preferred; management exposure on WAN requires explicit risk treatment
Instructor demonstration / expected result: Confirm interface allowaccess, admin trusted hosts and routing from the management station.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Management access must be deliberately bounded” before showing the answer.

## Slide 17
17
Interfaces and DNS create the initial control-plane dependencies
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
show system interface <port> get system dns execute ping <resolver-ip> execute nslookup <fqdn>
READ THE OUTPUT
• Set role, alias, address/mask and administrative access intentionally
• Avoid overlapping subnets and accidental DHCP conflicts
• System DNS supports name resolution for updates, FQDN objects and services
• NTP and correct time are prerequisites for logs and certificates
Safe operation
Configure <lan-port> and resolver placeholders from the instructor worksheet
021 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Notes: [CORE LECTURE] Stable ID: D1-B02-S021
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Set role, alias, address/mask and administrative access intentionally; Avoid overlapping subnets and accidental DHCP conflicts; System DNS supports name resolution for updates, FQDN objects and services; NTP and correct time are prerequisites for logs and certificates
Instructor demonstration / expected result: show system interface <port>; execute ping <resolver-ip>; execute nslookup <name>.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Interfaces and DNS create the initial control-plane dependencies” before showing the answer.

## Slide 18
18
Backup and restore are change-control controls
• Export a configuration before significant change
• Protect backups because they contain sensitive configuration
• Restore can replace current configuration and trigger reboot or service interruption
• Match backup, firmware branch, model and VDOM context before reuse
ILLUSTRATIVE SCENARIO
Demonstrate backup; discuss restore without disrupting a shared class environment
EXPECTED RESULT
Compare revision metadata and perform restore only in an isolated appliance or instructor demo.
Expected observation
The configured interface is up, DNS resolves the test name, and the backup completes with the expected timestamp.
022 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Notes: [CORE LECTURE] Stable ID: D1-B02-S022
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Export a configuration before significant change; Protect backups because they contain sensitive configuration; Restore can replace current configuration and trigger reboot or service interruption; Match backup, firmware branch, model and VDOM context before reuse
Instructor demonstration / expected result: Compare revision metadata and perform restore only in an isolated appliance or instructor demo.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Backup and restore are change-control controls” before showing the answer.

## Slide 19
019
Initial operational check
19
01
Confirm FortiOS 7.6.7
02
Check interface link/IP
03
Resolve test FQDN
04
Reach expected next hop
05
Create dated backup
EXPECTED RESULT
The configured interface is up, DNS resolves the test name, and the backup completes with the expected timestamp.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D1-B02-S023
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm expected build, hostname, time and license/service status; Verify interface link/address and administrative reachability; Test DNS and next-hop reachability independently; Create and securely retain a pre-change backup
Instructor demonstration / expected result: get system status; get system interface physical; execute ping-options source <ip>.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Initial operational check” before showing the answer.

## Slide 20
020
Common mistakes—and how to correct them
20
MISTAKE
CORRECTION — AND WHY IT HELPS
Enable management on every interface
Restrict HTTPS/SSH to the management interface and trusted sources; this reduces exposure.
Restore without compatibility review
Check model, build and VDOM context before restore; incompatible backups can interrupt service.
Ping proves the initial setup
Test DNS, admin access, route and backup separately; ICMP does not cover those dependencies.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D1-B02-S024
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 21
21
Troubleshooting workflow: narrow the failed decision
01
Verify physical/link state and IP addressing
02
Confirm the admin station route and allowed protocol
03
Check trusted-host/profile restrictions
04
Validate DNS and time
05
Back up before remediation
What to observe
• Check trusted-host/profile restrictions
• Validate DNS and time
• Back up before remediation
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
025 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Notes: [CORE LECTURE] Stable ID: D1-B02-S025
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Verify physical/link state and IP addressing; Confirm the admin station route and allowed protocol; Check trusted-host/profile restrictions; Validate DNS and time; Back up before remediation
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 22
22
Practical handoff: predict, observe, explain
• Prerequisite: Console or authorized management network
• Prerequisite: Instructor-supplied credentials and interface mapping
• Goal: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The configured interface is up, DNS resolves the test name, and the backup completes with the expected timestamp.
026 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Notes: [CORE LECTURE] Stable ID: D1-B02-S026
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Console or authorized management network; Prerequisite: Instructor-supplied credentials and interface mapping; Goal: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 23
23
Knowledge check — explain the result
QUESTION 1
• Where is HTTPS/SSH administrative access enabled?
QUESTION 2
• Why must time be correct before certificate troubleshooting?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
027 • DAY 1 • BLOCK 02 • Introduction & Initial Configuration
Notes: [CORE LECTURE] Stable ID: D1-B02-S027
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Where is HTTPS/SSH administrative access enabled?; Why must time be correct before certificate troubleshooting?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling management on every interface; Restoring a configuration without model/build/VDOM review; Using ping success as proof that DNS and policy are correct
Practical handoff: Configure one designated interface and DNS using instructor-provided values; capture interface status, name-resolution state/output and a backup file. Restore remains instructor demo unless each learner has an isolated unit.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Connecting to the GUI/CLI; Interfaces; DNS; Configuration backups. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: Where is HTTPS/SSH administrative access enabled?
A: Per interface, then further restricted by administrator profile/trusted hosts and network controls.
Q: Why must time be correct before certificate troubleshooting?
A: Certificate validity and log correlation depend on accurate time.

## Slide 24
DAY 1 • 13:00–14:30
Segmentation, Zones & Firewall Policy Design
Foundations • Day 1 of 2
LEARNING OBJECTIVES
• Choose LAN/WAN/DMZ boundaries using least privilege
• Explain FortiSwitch/FortiLink roles without assuming lab availability
• Build ordered policies from reusable objects and logging requirements
PREREQUISITES + PRACTICE RESERVE
• Block 1 routing/session concepts
• Known trust zones and application flows
• FortiSwitch hardware is instructor-demo only unless supplied
Teach ~54 min • reserve ~36 min for guided activity, discussion and debrief
028
Notes: [CORE LECTURE] Stable ID: D1-B03-S028
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Choose LAN/WAN/DMZ boundaries using least privilege; Explain FortiSwitch/FortiLink roles without assuming lab availability; Build ordered policies from reusable objects and logging requirements
Instructor demonstration / expected result: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Practical handoff: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Discussion prompt: Ask learners to predict the state/output for “Segmentation, Zones & Firewall Policy Design” before showing the answer.

## Slide 25
025
Segmentation permits named flows and denies everything else
Zones simplify references; they do not create isolation by themselves
25
LAN ZONE
10.10.10.0/24
DMZ ZONE
10.10.20.0/24
WAN
untrusted
GUEST ZONE
10.10.30.0/24
HTTPS 443 allowed
published HTTPS
DNS only
DENY
Policy intent
• LAN → DMZ: HTTPS only
• Guest → LAN/DMZ: denied
• WAN → DMZ: VIP + HTTPS
• Zone membership alone permits nothing
LESSON
Draw the permitted arrows first; each arrow becomes a narrowly scoped firewall policy and a positive/negative test.
Notes: Expected result: the HTTPS test matches the intended policy ID; a guest-to-DMZ test is denied. Source: FortiOS 7.6.7 Administration Guide — Zones and firewall policies.

## Slide 26
26
Zones simplify policy only when members share intent
• A zone groups interfaces for policy references and consistent treatment
• Do not combine interfaces with different trust or logging requirements
• Intra-zone traffic behavior must be explicitly understood and tested
• Naming should reveal function, not physical port number
ILLUSTRATIVE SCENARIO
Zone BRANCH-LANS can be useful; zone TRUSTED-MIX is usually ambiguous
EXPECTED RESULT
List each member and prove that one policy intent applies to all.
Expected observation
The test flow matches the intended policy; the denied flow is logged by the implicit or explicit deny.
030 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: [CORE LECTURE] Stable ID: D1-B03-S030
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A zone groups interfaces for policy references and consistent treatment; Do not combine interfaces with different trust or logging requirements; Intra-zone traffic behavior must be explicitly understood and tested; Naming should reveal function, not physical port number
Instructor demonstration / expected result: List each member and prove that one policy intent applies to all.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Practical handoff: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Discussion prompt: Ask learners to predict the state/output for “Zones simplify policy only when members share intent” before showing the answer.

## Slide 27
27
FortiLink joins FortiGate policy with managed switching
FORTIGATE
FORTILINK
FORTISWITCH
VLAN ENDPOINTS
Conceptual exercise: place users, voice, APs and servers into VLANs and policies
• FortiLink is the management/control connection for supported FortiSwitch deployments
• FortiGate can manage switch ports, VLANs and topology from the Security Fabric/LAN edge workflow
• Access, trunk and native VLAN choices remain layer-2 design decisions
• Model, FortiOS/FortiSwitchOS and topology support must be confirmed
Instructor demo only unless a compatible FortiSwitch, links and supported versions exist.
031 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: [OPTIONAL DEEP DIVE] Stable ID: D1-B03-S031
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: FortiLink is the management/control connection for supported FortiSwitch deployments; FortiGate can manage switch ports, VLANs and topology from the Security Fabric/LAN edge workflow; Access, trunk and native VLAN choices remain layer-2 design decisions; Model, FortiOS/FortiSwitchOS and topology support must be confirmed
Instructor demonstration / expected result: Instructor demo only unless a compatible FortiSwitch, links and supported versions exist.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Practical handoff: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Discussion prompt: Ask learners to predict the state/output for “FortiLink joins FortiGate policy with managed switching” before showing the answer.

## Slide 28
28
First match wins: specificity and order are design tools
01
Ingress pair
02
Address match
03
Service/schedule
04
First match
05
Action + profiles
What to observe
• The first matching enabled policy supplies action, NAT, logging and profiles
• Broad rules above narrow rules can shadow intended controls
• Objects and groups reduce error when they have clear names and owners
INSTRUCTOR DEMONSTRATION
Use policy lookup/hit counters and logs to prove the matched policy.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
032 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: [CORE LECTURE] Stable ID: D1-B03-S032
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A policy is evaluated in sequence for ingress/egress, addresses, service, schedule and other selectors; The first matching enabled policy supplies action, NAT, logging and profiles; Broad rules above narrow rules can shadow intended controls; Objects and groups reduce error when they have clear names and owners
Instructor demonstration / expected result: Use policy lookup/hit counters and logs to prove the matched policy.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Practical handoff: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Discussion prompt: Ask learners to predict the state/output for “First match wins: specificity and order are design tools” before showing the answer.

## Slide 29
029
Policy from a flow matrix
29
01
Name business flow
02
Create address/service objects
03
Order specific rule
04
Enable required logging
05
Test allow and deny
EXPECTED RESULT
The test flow matches the intended policy; the denied flow is logged by the implicit or explicit deny.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D1-B03-S033
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: State business flow: source zone, destination, service and owner; Create address/service objects with durable names; Order narrow exceptions before broad patterns; Enable the logging required for operations and audit
Instructor demonstration / expected result: Test positive and negative cases; record matched policy ID.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Practical handoff: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Discussion prompt: Ask learners to predict the state/output for “Policy design from a flow matrix” before showing the answer.

## Slide 30
030
Common mistakes—and how to correct them
30
MISTAKE
CORRECTION — AND WHY IT HELPS
Use all objects to save time
Create named source, destination and service objects; scope becomes reviewable and reusable.
Put unlike interfaces in one zone
Group only interfaces with the same policy intent; zones do not create isolation.
Put broad allow above exceptions
Place specific rules first and use policy lookup; first match otherwise shadows them.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D1-B03-S034
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Practical handoff: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 31
31
Troubleshooting workflow: narrow the failed decision
01
Confirm ingress and expected egress interfaces
02
Resolve object membership to concrete IP/port values
03
Check policy order and shadowing
04
Inspect hit count and traffic log
05
Test an explicit negative case
What to observe
• Check policy order and shadowing
• Inspect hit count and traffic log
• Test an explicit negative case
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
035 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: [CORE LECTURE] Stable ID: D1-B03-S035
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm ingress and expected egress interfaces; Resolve object membership to concrete IP/port values; Check policy order and shadowing; Inspect hit count and traffic log; Test an explicit negative case
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Practical handoff: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 32
32
Practical handoff: predict, observe, explain
• Prerequisite: Block 1 routing/session concepts
• Prerequisite: Known trust zones and application flows
• Goal: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The test flow matches the intended policy; the denied flow is logged by the implicit or explicit deny.
036 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: [CORE LECTURE] Stable ID: D1-B03-S036
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Block 1 routing/session concepts; Prerequisite: Known trust zones and application flows; Goal: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Practical handoff: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 33
33
Knowledge check — explain the result
QUESTION 1
• What decides which of two matching policies is used?
QUESTION 2
• When is a zone a poor abstraction?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
037 • DAY 1 • BLOCK 03 • Segmentation, Zones & Policy
Notes: [CORE LECTURE] Stable ID: D1-B03-S037
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What decides which of two matching policies is used?; When is a zone a poor abstraction?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Using “all” because object creation feels slow; Grouping unlike interfaces into one zone; Leaving logging off until an incident occurs
Practical handoff: Build a two-flow policy matrix, implement with reusable objects, then prove one allowed and one denied flow. FortiSwitch/FortiLink remains conceptual or instructor demonstration unless hardware is declared.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall policy; Zones; Addresses and services; FortiLink/FortiSwitch integration. Confirm FortiSwitch compatibility matrix.
Knowledge check answer key:
Q: What decides which of two matching policies is used?
A: The first enabled policy in sequence that matches all selectors.
Q: When is a zone a poor abstraction?
A: When member interfaces have different trust, logging or policy intent.

## Slide 34
DAY 1 • 14:30–16:00
NAT, Logging & CLI Troubleshooting
Foundations • Day 1 of 2
LEARNING OBJECTIVES
• Trace SNAT/PAT, DNAT/VIP and hairpin flows in both directions
• Select Traffic, Event and Security logs for the question asked
• Use session, sniffer and debug-flow diagnostics safely
PREREQUISITES + PRACTICE RESERVE
• Routing and policy fundamentals
• A test client and reachable service
• Authorization to clear sessions or enable debug
Teach ~56 min • reserve ~34 min for guided activity, discussion and debrief
038
Notes: [CORE LECTURE] Stable ID: D1-B04-S038
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Trace SNAT/PAT, DNAT/VIP and hairpin flows in both directions; Select Traffic, Event and Security logs for the question asked; Use session, sniffer and debug-flow diagnostics safely
Instructor demonstration / expected result: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet state/output. Session clearing is optional and instructor-controlled because it disrupts traffic.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Practical handoff: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet state/output. Session clearing is optional and instructor-controlled because it disrupts traffic.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “NAT, Logging & CLI Troubleshooting” before showing the answer.

## Slide 35
035
SNAT/PAT changes the source tuple—and reverses it for the reply
Illustrative outbound HTTPS session
35
CLIENT
10.10.10.25:51514
original
FORTIGATE
SNAT/PAT session
translated
SERVER
203.0.113.80:443
OUTBOUND
10.10.10.25:51514 → 203.0.113.80:443
WIRE TUPLE
198.51.100.2:62001 → 203.0.113.80:443
REPLY: 203.0.113.80:443 → 198.51.100.2:62001 • FortiGate reverses to 10.10.10.25:51514
LESSON
Record both directions: NAT succeeds only when the return packet matches the translated reply tuple.
Notes: Expected result: the session lists original and reply tuples; WAN capture shows 198.51.100.2:62001 while LAN capture shows 10.10.10.25:51514. Source: FortiOS 7.6.7 Administration Guide — Source NAT and sessions.

## Slide 36
036
A VIP translates the published destination before forwarding
External access to the HQ DMZ server
36
EXTERNAL CLIENT
203.0.113.50:53000
public tuple
VIP ON FORTIGATE
198.51.100.10:443 → 10.10.20.10:8443
mapped tuple
DMZ SERVER
10.10.20.10:8443
FIREWALL POLICY
• Ingress: WAN
• Destination: VIP object
• Service: HTTPS
• Egress route: DMZ
Reply translation
10.10.20.10:8443 → client becomes 198.51.100.10:443 → client
LESSON
A VIP defines translation; the firewall policy, route and return path still decide whether the service works.
Notes: Expected result: WAN capture targets 198.51.100.10:443, DMZ capture targets 10.10.20.10:8443, and the traffic log shows the VIP policy ID. Source: FortiOS 7.6.7 Administration Guide — Virtual IPs and DNAT.

## Slide 37
037
Hairpin access uses the public VIP from an internal network
Internal client and server remain in separate segments
37
LAN CLIENT
10.10.10.25:51514
public address
FORTIGATE VIP
198.51.100.10:443 → 10.10.20.10:8443
DNAT + policy
DMZ SERVER
10.10.20.10:8443
Why source NAT may be required
• Without SNAT, the server may reply directly to the client
• Direct reply bypasses the FortiGate session and breaks symmetry
• SNAT forces the reply through FortiGate for reverse translation
• Split DNS can avoid hairpinning when appropriate
Expected packet path
LAN → FortiGate → DMZ DMZ → FortiGate → LAN
LESSON
Hairpin troubleshooting must check DNAT, optional SNAT, policy and the server’s return route as one session.
Notes: Expected result: one session shows the VIP destination mapping and, when required by the design, a translated source that returns through FortiGate. Source: FortiOS 7.6.7 Administration Guide — Hairpin NAT / VIP examples.

## Slide 38
38
Logs and CLI answer different layers of the incident
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
diagnose sys session filter clear diagnose sys session filter src <client-ip> diagnose sys session list diagnose sniffer packet any "host <ip> and port <port>" 4 0 l diagnose debug reset
READ THE OUTPUT
• Traffic logs show policy, action, interfaces, addresses, ports and bytes
• Event logs show system/admin/HA/routing events
• Security logs show profile detections and actions
• Session table shows live state; sniffer shows packets; debug flow explains decisions
Safe operation
A deny without a session points to policy/route processing; a session without replies points downstream/return path
042 • DAY 1 • BLOCK 04 • NAT, Logging & CLI Troubleshooting
Notes: [CORE LECTURE] Stable ID: D1-B04-S042
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Traffic logs show policy, action, interfaces, addresses, ports and bytes; Event logs show system/admin/HA/routing events; Security logs show profile detections and actions; Session table shows live state; sniffer shows packets; debug flow explains decisions
Instructor demonstration / expected result: Filter by time and five-tuple, then correlate policy ID and session ID.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Practical handoff: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet state/output. Session clearing is optional and instructor-controlled because it disrupts traffic.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Logs and CLI answer different layers of the incident” before showing the answer.

## Slide 39
039
NAT in both directions
39
01
Record original tuple
02
Read translated session tuple
03
Capture LAN side
04
Capture WAN/server side
05
Match reply translation
EXPECTED RESULT
The session shows original and translated tuples, and packet captures show the reverse translation on the reply.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D1-B04-S043
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Record original client/server tuple; Record translated tuple at WAN or server side; Match the return packet to the reply direction; Confirm log policy ID and byte counters increase
Instructor demonstration / expected result: Use safe filters; session clearing is disruptive and must be isolated/authorized.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Practical handoff: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet state/output. Session clearing is optional and instructor-controlled because it disrupts traffic.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “NAT state/output in both directions” before showing the answer.

## Slide 40
040
Common mistakes—and how to correct them
40
MISTAKE
CORRECTION — AND WHY IT HELPS
Check only the public side of DNAT
Capture WAN and DMZ sides; comparing tuples shows whether the VIP translated and forwarded.
Run unfiltered debug flow
Filter by address/port and bound the capture; this prevents noise and operational impact.
Clear all sessions after a change
Use a new five-tuple or narrow session filter; broad clearing disrupts unrelated users.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D1-B04-S044
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Practical handoff: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet state/output. Session clearing is optional and instructor-controlled because it disrupts traffic.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 41
41
Troubleshooting workflow: narrow the failed decision
01
Define the expected original and translated tuples
02
Check route and matching policy/VIP
03
Inspect live session state
04
Capture at two interfaces to localize loss
05
Run filtered debug flow; disable/reset immediately
What to observe
• Inspect live session state
• Capture at two interfaces to localize loss
• Run filtered debug flow; disable/reset immediately
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
045 • DAY 1 • BLOCK 04 • NAT, Logging & CLI Troubleshooting
Notes: [CORE LECTURE] Stable ID: D1-B04-S045
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Define the expected original and translated tuples; Check route and matching policy/VIP; Inspect live session state; Capture at two interfaces to localize loss; Run filtered debug flow; disable/reset immediately
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Practical handoff: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet state/output. Session clearing is optional and instructor-controlled because it disrupts traffic.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 42
42
Practical handoff: predict, observe, explain
• Prerequisite: Routing and policy fundamentals
• Prerequisite: A test client and reachable service
• Goal: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet behavior. Session clearing is optional and instructor-controlled because it disrupts traffic.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet behavior. Session clearing is optional and instructor-controlled because it disrupts traffic.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The session shows original and translated tuples, and packet captures show the reverse translation on the reply.
046 • DAY 1 • BLOCK 04 • NAT, Logging & CLI Troubleshooting
Notes: [CORE LECTURE] Stable ID: D1-B04-S046
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Routing and policy fundamentals; Prerequisite: A test client and reachable service; Goal: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet state/output. Session clearing is optional and instructor-controlled because it disrupts traffic.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Practical handoff: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet state/output. Session clearing is optional and instructor-controlled because it disrupts traffic.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 43
43
Knowledge check — explain the result
QUESTION 1
• Which log best proves the firewall policy and NAT result for a connection?
QUESTION 2
• What must be done after a debug-flow demonstration?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
047 • DAY 1 • BLOCK 04 • NAT, Logging & CLI Troubleshooting
Notes: [CORE LECTURE] Stable ID: D1-B04-S047
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Which log best proves the firewall policy and NAT result for a connection?; What must be done after a debug-flow demonstration?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Looking only at the public side of DNAT; Running unfiltered debug on a busy device; Forgetting to stop/reset debug or treating session clear as harmless
Practical handoff: Predict SNAT and VIP translations, generate one test flow, and collect a log plus two-side packet state/output. Session clearing is optional and instructor-controlled because it disrupts traffic.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: NAT; Virtual IPs; Logging; Session table; Packet sniffer; Debugging the packet flow. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: Which log best proves the firewall policy and NAT result for a connection?
A: The Traffic log, correlated with session and packet state/output.
Q: What must be done after a debug-flow demonstration?
A: Disable debug output and reset filters/state; retain only necessary state/output.

## Slide 44
DAY 2 • 09:00–10:30
Routing Fundamentals & Route Selection
Foundations • Day 2 of 2
LEARNING OBJECTIVES
• Interpret static and default routes in the routing table
• Explain longest prefix, administrative distance, priority and ECMP
• Validate next-hop and return-path behavior
PREREQUISITES + PRACTICE RESERVE
• Day 1 five-tuple and interface concepts
• Illustrative addresses from slide 3
• Two next hops for ECMP demonstration if available
Teach ~52 min • reserve ~38 min for guided activity, discussion and debrief
048
Notes: [CORE LECTURE] Stable ID: D2-B05-S048
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Interpret static and default routes in the routing table; Explain longest prefix, administrative distance, priority and ECMP; Validate next-hop and return-path behavior
Instructor demonstration / expected result: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Routing Fundamentals & Route Selection” before showing the answer.

## Slide 45
45
Route selection starts with the most specific prefix
CANDIDATES
• 10.20.10.0/24 via VPN, distance 10
• 10.20.0.0/16 via WAN2, distance 5
• 0.0.0.0/0 via WAN1, distance 10
WINNER
• The /24 wins by longest prefix
• Distance is compared only among equal prefixes
• Return path requires an independent lookup
KEY DISTINCTION
10.20.10.25 matches /24 over /16 over /0
049 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: [CORE LECTURE] Stable ID: D2-B05-S049
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Connected, static and dynamic routes can all be candidates; Longest prefix match chooses the narrowest destination range first; Administrative distance compares route sources for the same prefix; Priority can break ties within the same route source; verify exact behavior in the deployed build
Instructor demonstration / expected result: get router info routing-table details <destination> and identify selected route.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Route selection starts with the most specific prefix” before showing the answer.

## Slide 46
46
A default route is a last-resort candidate
• 0.0.0.0/0 matches any IPv4 destination but loses to every more-specific route
• The next hop must be reachable on the configured interface
• Multiple defaults can provide preference or ECMP depending on distance/priority and state
• Default gateway on a host points to FortiGate; default route on FortiGate points upstream
ILLUSTRATIVE SCENARIO
Client default gateway 10.10.10.1; FortiGate default route via ISP-A
EXPECTED RESULT
Test gateway reachability with source interface/address specified.
Expected observation
The routing table installs the most-specific eligible route with the expected next hop.
050 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: [CORE LECTURE] Stable ID: D2-B05-S050
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: 0.0.0.0/0 matches any IPv4 destination but loses to every more-specific route; The next hop must be reachable on the configured interface; Multiple defaults can provide preference or ECMP depending on distance/priority and state; Default gateway on a host points to FortiGate; default route on FortiGate points upstream
Instructor demonstration / expected result: Test gateway reachability with source interface/address specified.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “A default route is a last-resort candidate” before showing the answer.

## Slide 47
47
Administrative distance expresses source trust, not path quality
• Lower distance is preferred for equal prefixes
• Different protocols have defaults; explicit changes should be documented
• A lower distance does not fix an unreachable next hop
• Use SD-WAN/health logic for measured service quality rather than abusing distance
ILLUSTRATIVE SCENARIO
Static and OSPF learn the same /24; compare distance and installation
EXPECTED RESULT
Inspect both protocol database and active routing table.
Expected observation
The routing table installs the most-specific eligible route with the expected next hop.
051 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: [CORE LECTURE] Stable ID: D2-B05-S051
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Lower distance is preferred for equal prefixes; Different protocols have defaults; explicit changes should be documented; A lower distance does not fix an unreachable next hop; Use SD-WAN/health logic for measured service quality rather than abusing distance
Instructor demonstration / expected result: Inspect both protocol database and active routing table.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Administrative distance expresses source trust, not path quality” before showing the answer.

## Slide 48
48
ECMP installs equal-cost next hops; sessions choose a path
CLIENT FLOWS
FORTIGATE ECMP HASH
ISP-A / ISP-B
Two equal defaults distribute new sessions; one existing session does not split packet by packet
• Routes must be equal under relevant selection criteria
• A session is normally pinned to one selected next hop
• Per-packet assumptions are unsafe; hashing and platform behavior require confirmation
• Symmetry, NAT and upstream state affect failover outcomes
Generate multiple five-tuples and compare the egress interface recorded in each session.
052 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: [CORE LECTURE] Stable ID: D2-B05-S052
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Routes must be equal under relevant selection criteria; A session is normally pinned to one selected next hop; Per-packet assumptions are unsafe; hashing and platform behavior require confirmation; Symmetry, NAT and upstream state affect failover outcomes
Instructor demonstration / expected result: Generate multiple distinct five-tuples and compare egress/session state/output.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “ECMP installs equal-cost next hops; sessions choose a path” before showing the answer.

## Slide 49
049
Candidate route selection
49
01
List matching prefixes
02
Choose longest prefix
03
Compare distance for ties
04
Resolve next hop
05
Check return route
EXPECTED RESULT
The routing table installs the most-specific eligible route with the expected next hop.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D2-B05-S053
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: List every matching prefix; Choose longest prefix; For equal prefixes compare distance then applicable priority/metric; Confirm next-hop/interface state and perform return lookup
Instructor demonstration / expected result: Show selected route plus alternate state/output.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Candidate route decision” before showing the answer.

## Slide 50
050
Common mistakes—and how to correct them
50
MISTAKE
CORRECTION — AND WHY IT HELPS
Compare distance across different prefixes
Choose longest prefix first; distance is compared among equal prefixes.
Assume ECMP splits each packet
Generate multiple sessions; ECMP generally selects per flow/session.
Ignore the reverse route
Run a lookup for the client prefix; the reply uses an independent decision.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D2-B05-S054
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 51
51
Troubleshooting workflow: narrow the failed decision
01
Look up the exact destination
02
Verify the selected prefix and next hop
03
Test next-hop reachability from the expected source
04
Check policy/session egress
05
Repeat lookup for return destination
What to observe
• Test next-hop reachability from the expected source
• Check policy/session egress
• Repeat lookup for return destination
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
055 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: [CORE LECTURE] Stable ID: D2-B05-S055
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Look up the exact destination; Verify the selected prefix and next hop; Test next-hop reachability from the expected source; Check policy/session egress; Repeat lookup for return destination
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 52
52
Practical handoff: predict, observe, explain
• Prerequisite: Day 1 five-tuple and interface concepts
• Prerequisite: Illustrative addresses from slide 3
• Goal: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table result and test flow. Avoid changing shared default routes without rollback.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table result and test flow. Avoid changing shared default routes without rollback.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The routing table installs the most-specific eligible route with the expected next hop.
056 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: [CORE LECTURE] Stable ID: D2-B05-S056
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Day 1 five-tuple and interface concepts; Prerequisite: Illustrative addresses from slide 3; Goal: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 53
53
Knowledge check — explain the result
QUESTION 1
• Which criterion is evaluated before administrative distance?
QUESTION 2
• Why might equal routes not visibly split one connection?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
057 • DAY 2 • BLOCK 05 • Routing Fundamentals
Notes: [CORE LECTURE] Stable ID: D2-B05-S057
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Which criterion is evaluated before administrative distance?; Why might equal routes not visibly split one connection?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Comparing distance across different prefix lengths; Assuming ECMP means per-packet round robin; Ignoring the reverse destination route
Practical handoff: Create two static candidates using instructor-approved lab routes, predict the winner, then validate route-table and traffic state/output. Avoid changing shared default routes without rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Static routing; Routing table; ECMP. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: Which criterion is evaluated before administrative distance?
A: Longest prefix match.
Q: Why might equal routes not visibly split one connection?
A: Path selection is generally session/flow based, so one five-tuple remains pinned.

## Slide 54
DAY 2 • 10:30–12:00
Object Management & Policy Design Best Practices
Foundations • Day 2 of 2
LEARNING OBJECTIVES
• Create clear address, service and group objects
• Apply naming, reuse and ownership conventions
• Review policies for maintainability and operational clarity
PREREQUISITES + PRACTICE RESERVE
• Day 1 policy evaluation
• Agreed naming standard or instructor example
• Read-only review is sufficient for shared labs
Teach ~50 min • reserve ~40 min for guided activity, discussion and debrief
058
Notes: [CORE LECTURE] Stable ID: D2-B06-S058
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Create clear address, service and group objects; Apply naming, reuse and ownership conventions; Review policies for maintainability and operational clarity
Instructor demonstration / expected result: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Discussion prompt: Ask learners to predict the state/output for “Object Management & Policy Design Best Practices” before showing the answer.
[OPTIONAL SUPPLEMENT — IDENTITY/AUTHENTICATION, 10–15 MINUTES IF NEEDED]
LDAP: FortiGate binds/searches a directory using a configured base DN and attributes; connectivity, TLS trust, bind permissions and group lookup are separate failure points. LDAP validates directory credentials/attributes but does not by itself create an IP-to-user mapping for transparent policy.
RADIUS: the FortiGate acts as a network access client and receives Access-Accept, Access-Reject or Access-Challenge. Shared secret, client/NAS identity, source IP, timeout and returned group attributes must agree. Preserve a local break-glass administrator.
FSSO: collector/agent methods learn user logon information and map user/group to workstation IP for identity-aware policy. Shared/NATed devices, stale logoff data, collector reachability and group filters affect accuracy. Validate the live user/IP mapping and matched policy rather than assuming directory success proves FSSO.
Optional demo: test one LDAP/RADIUS server object, then inspect one FSSO user/IP mapping; do not let this supplement displace routing, VPN, EMS, HA or SD-WAN.
Official preparation references: FortiGate/FortiOS 7.6.7 Administration Guide — LDAP servers, RADIUS servers, Firewall authentication and FSSO. Confirm FortiOS 7.6.7 build and authentication architecture.

## Slide 55
55
Objects turn intent into reusable selectors
• Address objects represent hosts, subnets, ranges, FQDNs or interfaces as supported
• Service objects represent protocol and port ranges
• Groups reduce repetition but can hide overly broad membership
• Comments, owners and lifecycle information improve change safety
ILLUSTRATIVE SCENARIO
APP-PROD-10.10.20.10 and SVC-HTTPS-8443 are clearer than “server1” and “custom1”
EXPECTED RESULT
Expand group membership and confirm the concrete match values.
Expected observation
The policy references the intended reusable objects and the test traffic matches that policy ID.
059 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: [CORE LECTURE] Stable ID: D2-B06-S059
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Address objects represent hosts, subnets, ranges, FQDNs or interfaces as supported; Service objects represent protocol and port ranges; Groups reduce repetition but can hide overly broad membership; Comments, owners and lifecycle information improve change safety
Instructor demonstration / expected result: Expand group membership and confirm the concrete match values.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Discussion prompt: Ask learners to predict the state/output for “Objects turn intent into reusable selectors” before showing the answer.

## Slide 56
56
Naming should survive interface and personnel changes
• Name by function, environment and scope rather than transient ticket numbers
• Avoid embedding unverified geography or ownership
• Use consistent prefixes only when they add search value
• Document exceptions and expiration dates for temporary objects
ILLUSTRATIVE SCENARIO
TEMP-VENDOR-HTTPS-EXP-2026-10-31 is auditable if lifecycle is enforced
EXPECTED RESULT
Search for duplicates, unused objects and ambiguous names before adding new ones.
Expected observation
The policy references the intended reusable objects and the test traffic matches that policy ID.
060 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: [CORE LECTURE] Stable ID: D2-B06-S060
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Name by function, environment and scope rather than transient ticket numbers; Avoid embedding unverified geography or ownership; Use consistent prefixes only when they add search value; Document exceptions and expiration dates for temporary objects
Instructor demonstration / expected result: Search for duplicates, unused objects and ambiguous names before adding new ones.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Discussion prompt: Ask learners to predict the state/output for “Naming should survive interface and personnel changes” before showing the answer.

## Slide 57
57
Reusability must not erase policy intent
• Reuse canonical network/service objects
• Create a group when members genuinely share policy treatment
• Do not create mega-groups that make logging and review opaque
• FQDN/dynamic objects add resolution dependencies that must be monitored
ILLUSTRATIVE SCENARIO
A web-services group may be valid; “ALL-SERVERS” usually needs review
EXPECTED RESULT
Trace one object from definition to policy and traffic log.
Expected observation
The policy references the intended reusable objects and the test traffic matches that policy ID.
061 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: [CORE LECTURE] Stable ID: D2-B06-S061
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Reuse canonical network/service objects; Create a group when members genuinely share policy treatment; Do not create mega-groups that make logging and review opaque; FQDN/dynamic objects add resolution dependencies that must be monitored
Instructor demonstration / expected result: Trace one object from definition to policy and traffic log.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Discussion prompt: Ask learners to predict the state/output for “Reusability must not erase policy intent” before showing the answer.

## Slide 58
58
Maintainable policy has a clear purpose and owner
CLEAR
• Specific objects
• Single business purpose
• Expected logging/profile
• Named owner/lifecycle
FRAGILE
• all/all services
• Mixed purposes
• No comment or owner
• Permanent temporary access
KEY DISTINCTION
A policy name should let an operator predict source, destination and service
062 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: [CORE LECTURE] Stable ID: D2-B06-S062
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Place narrow exceptions intentionally; Separate flows with different owners, logging or security profiles; Use comments and change records to explain why a rule exists; Review zero-hit, expired and shadowed policies carefully before removal
Instructor demonstration / expected result: Use hit counters and logs as state/output, not sole justification for deletion.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Discussion prompt: Ask learners to predict the state/output for “Maintainable policy has a readable reason and state/output” before showing the answer.

## Slide 59
059
Policy review
59
01
Expand object groups
02
Compare scope to intent
03
Check rule order
04
Review logs/hits
05
Retain rollback
EXPECTED RESULT
The policy references the intended reusable objects and the test traffic matches that policy ID.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D2-B06-S063
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Resolve all object/group members; Compare scope to the documented flow; Check ordering and overlapping rules; Confirm logs and security profiles support operations
Instructor demonstration / expected result: Export policy/object references before renaming.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Discussion prompt: Ask learners to predict the state/output for “Policy review example” before showing the answer.

## Slide 60
060
Common mistakes—and how to correct them
60
MISTAKE
CORRECTION — AND WHY IT HELPS
Create duplicate objects
Search existing objects first; canonical objects reduce inconsistent policy scope.
Use mega-groups for convenience
Group only members with the same owner and treatment; large mixed groups hide access.
Delete a zero-hit rule immediately
Confirm logging window, seasonality and owner; zero hits alone does not prove obsolescence.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D2-B06-S064
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 61
61
Troubleshooting workflow: narrow the failed decision
01
Start from a failing/desired five-tuple
02
Resolve object membership
03
Check service protocol and port ranges
04
Inspect order, action, NAT and profiles
05
Use traffic logs, hit counters and change history
What to observe
• Check service protocol and port ranges
• Inspect order, action, NAT and profiles
• Use traffic logs, hit counters and change history
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
065 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: [CORE LECTURE] Stable ID: D2-B06-S065
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Start from a failing/desired five-tuple; Resolve object membership; Check service protocol and port ranges; Inspect order, action, NAT and profiles; Use log/hit state/output and change history
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 62
62
Practical handoff: predict, observe, explain
• Prerequisite: Day 1 policy evaluation
• Prerequisite: Agreed naming standard or instructor example
• Goal: Review three policies for naming, reuse, scope and ownership. Propose changes without applying them unless each learner has an isolated configuration and rollback.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Review three policies for naming, reuse, scope and ownership. Propose changes without applying them unless each learner has an isolated configuration and rollback.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The policy references the intended reusable objects and the test traffic matches that policy ID.
066 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: [CORE LECTURE] Stable ID: D2-B06-S066
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Day 1 policy evaluation; Prerequisite: Agreed naming standard or instructor example; Goal: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 63
63
Knowledge check — explain the result
QUESTION 1
• When should objects be grouped?
QUESTION 2
• Why is a zero hit count insufficient to delete a rule?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
067 • DAY 2 • BLOCK 06 • Objects & Policy Design
Notes: [CORE LECTURE] Stable ID: D2-B06-S067
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: When should objects be grouped?; Why is a zero hit count insufficient to delete a rule?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Creating duplicates instead of finding canonical objects; Using groups to conceal unrelated networks; Deleting a zero-hit rule without checking observation period
Practical handoff: Review three policies for naming, reuse, scope and state/output. Propose changes without applying them unless each learner has an isolated configuration and rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Firewall addresses; Services; Object groups; Firewall policy best practices.
Knowledge check answer key:
Q: When should objects be grouped?
A: When all members share the same policy intent and lifecycle.
Q: Why is a zero hit count insufficient to delete a rule?
A: The observation window, logging, seasonality and dependency/change history may be incomplete.

## Slide 64
DAY 2 • 13:00–14:30
Security Services & SSL Inspection
Foundations • Day 2 of 2
LEARNING OBJECTIVES
• Explain AV, IPS, Web Filter and Application Control roles
• Sequence security profiles with inspection prerequisites
• Compare certificate and deep inspection with PKI and operational impacts
PREREQUISITES + PRACTICE RESERVE
• Working outbound policy and logging
• Instructor-managed test content only
• Trusted inspection CA distribution for deep-inspection lab
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
068
Notes: [CORE LECTURE] Stable ID: D2-B07-S068
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain AV, IPS, Web Filter and Application Control roles; Sequence security profiles with inspection prerequisites; Compare certificate and deep inspection with PKI and operational impacts
Instructor demonstration / expected result: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Practical handoff: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Discussion prompt: Ask learners to predict the state/output for “Security Services & SSL Inspection” before showing the answer.

## Slide 65
65
Security profiles answer different detection questions
CONTENT
• Antivirus
• Web content/category
BEHAVIOR
• IPS exploits/protocols
• Application signatures
KEY DISTINCTION
One session may trigger multiple profile decisions; logs must be correlated by time/session
069 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: [CORE LECTURE] Stable ID: D2-B07-S069
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Antivirus scans supported content/files for malware; IPS matches exploit/protocol behavior using signatures and engines; Web Filter classifies and controls web destinations/categories; Application Control identifies applications beyond simple port labels
Instructor demonstration / expected result: Confirm profile mode, policy attachment and inspection mode before interpreting logs.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Practical handoff: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Discussion prompt: Ask learners to predict the state/output for “Security profiles answer different detection questions” before showing the answer.

## Slide 66
66
Inspection mode determines what profiles can see
• Flow mode streams traffic through engines with lower buffering
• Proxy mode terminates/proxies supported protocols for deeper protocol handling
• Feature behavior and availability vary by profile/protocol/release
• Choose mode by required controls and tested compatibility, not habit
ILLUSTRATIVE SCENARIO
Document the required visibility first; then choose inspection/profile combination
EXPECTED RESULT
Check policy inspection mode and profile attachment in the FortiOS 7.6.7 build.
Expected observation
The client trusts the inspection certificate and the relevant security profile records the intended action.
070 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: [CORE LECTURE] Stable ID: D2-B07-S070
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Flow mode streams traffic through engines with lower buffering; Proxy mode terminates/proxies supported protocols for deeper protocol handling; Feature behavior and availability vary by profile/protocol/release; Choose mode by required controls and tested compatibility, not habit
Instructor demonstration / expected result: Check policy inspection mode and profile attachment in the FortiOS 7.6.7 build.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Practical handoff: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Discussion prompt: Ask learners to predict the state/output for “Inspection mode determines what profiles can see” before showing the answer.

## Slide 67
67
Certificate inspection and deep inspection solve different problems
CERTIFICATE
• Handshake metadata
• No payload decryption
• Lower endpoint impact
DEEP
• Payload visible to profiles
• Inspection CA required
• Compatibility/performance impact
KEY DISTINCTION
Certificate inspection can categorize based on visible data; deep inspection enables content scanning
071 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: [CORE LECTURE] Stable ID: D2-B07-S071
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Certificate inspection observes TLS handshake/certificate metadata without decrypting payload; Deep inspection decrypts and re-encrypts TLS traffic to expose content; Deep inspection requires endpoint trust in the inspection CA and policy/privacy approval; Exceptions are often needed for pinning, unsupported protocols or regulated traffic
Instructor demonstration / expected result: Test with a managed endpoint and verify presented certificate chain.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Practical handoff: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Discussion prompt: Ask learners to predict the state/output for “Certificate inspection and deep inspection solve different problems” before showing the answer.

## Slide 68
068
Deep inspection creates two TLS connections
Certificate inspection reads handshake metadata but does not decrypt the application payload
68
CLIENT
trusts Inspection CA
TLS #1
FORTIGATE
decrypt • inspect • re-encrypt
TLS #2
SERVER
original certificate
Certificate presented to client
Replacement certificate for server name signed by the FortiGate Inspection CA
Certificate received from server
Original server certificate validated by FortiGate
CERTIFICATE INSPECTION
• No payload decryption
• Reads visible TLS metadata
• Cannot scan encrypted content
LESSON
The browser trusts the replacement certificate only when the inspection CA is installed and trusted on the endpoint.
Notes: Expected result: under deep inspection, the browser certificate issuer is the configured inspection CA; under certificate inspection, the original server certificate remains end to end. Source: FortiOS 7.6.7 Administration Guide — SSL/SSH inspection and deep inspection.

## Slide 69
069
HTTPS profile interaction
69
01
Policy selects SSL profile
02
TLS visibility is established
03
Security profiles inspect
04
Traffic/security logs record action
05
Client receives allow/block
EXPECTED RESULT
The client trusts the inspection certificate and the relevant security profile records the intended action.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D2-B07-S073
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Policy permits and selects inspection mode; TLS inspection exposes available metadata/content; AV/IPS/Web/App engines apply relevant controls; Traffic and security logs record different state/output
Instructor demonstration / expected result: Correlate logs by source/destination/time/session and verify the final user result.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Practical handoff: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Discussion prompt: Ask learners to predict the state/output for “Profile interaction on HTTPS” before showing the answer.

## Slide 70
070
Common mistakes—and how to correct them
70
MISTAKE
CORRECTION — AND WHY IT HELPS
Enable deep inspection without CA deployment
Install and trust the inspection CA on managed clients; otherwise browsers reject replacement certificates.
Expect certificate inspection to scan payload
Use deep inspection when content scanning is required; certificate inspection does not decrypt payload.
Blame the profile before checking TLS
Check certificate chain, time and pinning first; TLS can fail before a profile scans content.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D2-B07-S074
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Practical handoff: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 71
71
Troubleshooting workflow: narrow the failed decision
01
Prove basic path and policy first
02
Check TLS handshake/certificate errors
03
Confirm inspection mode and client trust
04
Identify which profile blocked or reset the session
05
Test an approved exception without broad bypass
What to observe
• Confirm inspection mode and client trust
• Identify which profile blocked or reset the session
• Test an approved exception without broad bypass
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
075 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: [CORE LECTURE] Stable ID: D2-B07-S075
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prove basic path and policy first; Check TLS handshake/certificate errors; Confirm inspection mode and client trust; Identify which profile blocked or reset the session; Test an approved exception without broad bypass
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Practical handoff: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 72
72
Practical handoff: predict, observe, explain
• Prerequisite: Working outbound policy and logging
• Prerequisite: Instructor-managed test content only
• Goal: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The client trusts the inspection certificate and the relevant security profile records the intended action.
076 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: [CORE LECTURE] Stable ID: D2-B07-S076
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Working outbound policy and logging; Prerequisite: Instructor-managed test content only; Goal: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Practical handoff: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 73
73
Knowledge check — explain the result
QUESTION 1
• What payload does certificate inspection decrypt?
QUESTION 2
• Why can deep inspection break an otherwise reachable site?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
077 • DAY 2 • BLOCK 07 • Security Services & SSL Inspection
Notes: [CORE LECTURE] Stable ID: D2-B07-S077
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What payload does certificate inspection decrypt?; Why can deep inspection break an otherwise reachable site?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Enabling deep inspection without distributing the CA; Assuming every profile can inspect encrypted payload under certificate inspection; Treating a security log as proof of routing or return path
Practical handoff: Compare certificate and deep inspection on an instructor-approved HTTPS target. Prerequisite: isolated managed endpoint and inspection CA. If unavailable, use a conceptual certificate-chain exercise.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Security profiles; Inspection modes; SSL/SSH inspection; Certificates. Confirm FortiGuard package/service prerequisites and 7.6.7 release notes.
Knowledge check answer key:
Q: What payload does certificate inspection decrypt?
A: None; it uses visible TLS handshake and certificate metadata.
Q: Why can deep inspection break an otherwise reachable site?
A: The client may not trust the inspection CA, the application may pin certificates, or protocol/privacy exceptions may apply.

## Slide 74
DAY 2 • 14:30–16:00
FortiGate Hardware Architecture, Monitoring & Operations
Foundations • Day 2 of 2
LEARNING OBJECTIVES
• Distinguish management, control and data planes
• Explain NP/CP acceleration, fast/slow path and VM limitations
• Monitor firmware, sessions, CPU, memory and Conserve Mode
PREREQUISITES + PRACTICE RESERVE
• Read-only operational access
• Lab baseline: FortiOS 7.6.7 Azure FGVM; physical appliance concepts are theoretical
• Maintenance window for upgrades or disruptive tests
Teach ~54 min • reserve ~36 min for guided activity, discussion and debrief
078
Notes: [CORE LECTURE] Stable ID: D2-B08-S078
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Distinguish management, control and data planes; Explain NP/CP acceleration, fast/slow path and VM limitations; Monitor firmware, sessions, CPU, memory and Conserve Mode
Instructor demonstration / expected result: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Practical handoff: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.
Discussion prompt: Ask learners to predict the state/output for “FortiGate Hardware Architecture, Monitoring & Operations” before showing the answer.

## Slide 75
75
Planes separate configuration, decisions and packet work
MANAGEMENT
• GUI/CLI/API
• Admins/config
CONTROL
• Routes/HA/state
• Protocol decisions
DATA
• Sessions/forwarding
• NAT/security engines
KEY DISTINCTION
GUI responsiveness does not prove packet forwarding health; forwarding does not prove routing adjacency health
079 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: [CORE LECTURE] Stable ID: D2-B08-S079
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Management plane serves GUI/CLI/API and administration; Control plane learns routing, HA and system state; Data plane forwards sessions and applies security processing; A plane can be healthy while another is constrained
Instructor demonstration / expected result: Collect plane-specific state/output: admin latency, protocol state, session/packet counters.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Practical handoff: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.
Discussion prompt: Ask learners to predict the state/output for “Planes separate configuration, decisions and packet work” before showing the answer.

## Slide 76
076
Appliance offload and Azure FGVM use different datapaths
First packets and unsupported features remain on the CPU path
76
PHYSICAL FORTIGATE APPLIANCE
CPU
session setup route • policy • NAT
eligible
NP
accelerated forwarding
CP assists supported content / crypto processing on applicable models and features.
TRAFFIC THAT STAYS ON CPU
• First packets and session setup
• Unsupported/offload-ineligible features
• Exceptional traffic and control-plane work
AZURE FORTIGATE-VM LAB
vCPU
FortiOS software path
vNIC
AZURE NETWORK
VM/vNIC/cloud acceleration
• No physical NP/CP ASIC datapath
• Use CPU/session counters for lab learning
• Do not extrapolate FGVM results to appliance capacity
LESSON
Teach appliance NP/CP concepts separately from what learners can actually verify in the Azure FGVM lab.
Notes: Instructor review: use model-specific hardware guides for NP/CP eligibility and counters. The Azure FGVM lab demonstrates software processing and Azure networking, not FortiASIC offload. Source: FortiOS 7.6.7 Administration Guide — Hardware acceleration; FortiGate-VM for Azure documentation.

## Slide 77
77
Fast path and slow path describe processing eligibility
• Session setup and exceptional traffic require CPU decisions
• Established eligible sessions may be offloaded
• Inspection, fragmentation, tunneling or feature choices can affect eligibility
• No-offload is not automatically a fault; compare with documented support
ILLUSTRATIVE SCENARIO
A session can work correctly without offload but consume more CPU
EXPECTED RESULT
Inspect session offload flags/counters only with platform-specific documentation.
Expected observation
CPU, memory and session values are recorded; appliance-only offload counters are not inferred from Azure FGVM.
081 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: [CORE LECTURE] Stable ID: D2-B08-S081
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Session setup and exceptional traffic require CPU decisions; Established eligible sessions may be offloaded; Inspection, fragmentation, tunneling or feature choices can affect eligibility; No-offload is not automatically a fault; compare with documented support
Instructor demonstration / expected result: Inspect session offload flags/counters only with platform-specific documentation.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Practical handoff: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.
Discussion prompt: Ask learners to predict the state/output for “Fast path and slow path describe processing eligibility” before showing the answer.

## Slide 78
078
Operations baseline
78
01
Record build and uptime
02
Count sessions
03
Sample CPU/memory
04
Check Conserve Mode events
05
Compare with normal baseline
EXPECTED RESULT
CPU, memory and session values are recorded; appliance-only offload counters are not inferred from Azure FGVM.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D2-B08-S082
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm firmware build and support policy before change; Back up configuration and document rollback; Track session count, CPU and memory against normal workload; Recognize Conserve Mode as protective behavior under memory pressure
Instructor demonstration / expected result: get system performance status; diagnose sys top; diagnose sys session stat; commands are illustrative.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Practical handoff: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.
Discussion prompt: Ask learners to predict the state/output for “Operations baseline” before showing the answer.

## Slide 79
079
Common mistakes—and how to correct them
79
MISTAKE
CORRECTION — AND WHY IT HELPS
Expect NP/CP counters in Azure FGVM
Use VM CPU/session counters in the lab; ASIC offload requires a physical appliance.
Upgrade without backup and release review
Back up and read 7.6.7 release notes/upgrade path; this preserves rollback.
Treat Conserve Mode as one process fault
Check memory trend, sessions, proxy use and top processes; multiple consumers can trigger it.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D2-B08-S083
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Practical handoff: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 80
80
Troubleshooting workflow: narrow the failed decision
01
Confirm current build/model/VM and recent changes
02
Compare CPU, memory and session counts to baseline
03
Identify top consumers and inspection load
04
Check Conserve Mode thresholds/events and proxy behavior
05
Mitigate safely; preserve evidence before restart/upgrade
What to observe
• Identify top consumers and inspection load
• Check Conserve Mode thresholds/events and proxy behavior
• Mitigate safely; preserve evidence before restart/upgrade
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
084 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: [CORE LECTURE] Stable ID: D2-B08-S084
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm current build/model/VM and recent changes; Compare CPU, memory and session counts to baseline; Identify top consumers and inspection load; Check Conserve Mode thresholds/events and proxy behavior; Mitigate safely; preserve state/output before restart/upgrade
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Practical handoff: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 81
81
Practical handoff: predict, observe, explain
• Prerequisite: Read-only operational access
• Prerequisite: Model/build and deployment type identified
• Goal: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
CPU, memory and session values are recorded; appliance-only offload counters are not inferred from Azure FGVM.
085 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: [CORE LECTURE] Stable ID: D2-B08-S085
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Read-only operational access; Prerequisite: Model/build and deployment type identified; Goal: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Practical handoff: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 82
82
Knowledge check — explain the result
QUESTION 1
• Why can a VM lab not prove NP/CP offload behavior?
QUESTION 2
• What is Conserve Mode?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
086 • DAY 2 • BLOCK 08 • Hardware, Monitoring & Operations
Notes: [CORE LECTURE] Stable ID: D2-B08-S086
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Why can a VM lab not prove NP/CP offload behavior?; What is Conserve Mode?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming appliance ASIC commands apply to FortiGate-VM; Upgrading without configuration backup and release-note review; Treating Conserve Mode as a single process fault
Practical handoff: Collect a read-only baseline: build, uptime, interfaces, sessions, CPU and memory. ASIC/offload validation is an instructor appliance demo; firmware change is demonstration unless a maintenance window and rollback exist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Hardware acceleration; Sessions; System performance; Conserve Mode; Firmware upgrades and release notes. Model-specific hardware guide required.
Knowledge check answer key:
Q: Why can a VM lab not prove NP/CP offload behavior?
A: The VM does not contain the appliance’s ASIC datapath; acceleration depends on virtual platform capabilities.
Q: What is Conserve Mode?
A: A protective FortiOS state triggered by memory pressure that changes/limits processing to preserve system stability; investigate causes and thresholds for the exact build.

## Slide 83
DAY 3 • 09:00–10:30
Route Selection, PBR & OSPF
Advanced • Day 1 of 2
LEARNING OBJECTIVES
• Explain route selection interactions with PBR
• Plan controlled route redistribution
• Establish OSPF neighbors and trace LSA-to-route exchange
PREREQUISITES + PRACTICE RESERVE
• Static routing mastery
• Two routing peers or instructor simulation
• Unique router IDs and non-overlapping lab prefixes
Teach ~56 min • reserve ~34 min for guided activity, discussion and debrief
087
Notes: [CORE LECTURE] Stable ID: D3-B09-S087
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain route selection interactions with PBR; Plan controlled route redistribution; Establish OSPF neighbors and trace LSA-to-route exchange
Instructor demonstration / expected result: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Practical handoff: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Route Selection, PBR & OSPF” before showing the answer.

## Slide 84
84
PBR can override destination-route intent for selected traffic
01
Packet fields
02
PBR match?
03
Next hop valid?
04
Forward
05
Fallback route
What to observe
• If matched and valid, it directs a next hop/interface before normal route selection
• A supporting route and reachable next hop are still required
• PBR increases operational complexity; document scope and fallback
INSTRUCTOR DEMONSTRATION
Inspect policy-route list and debug-flow route decision for the exact test tuple.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
088 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: [CORE LECTURE] Stable ID: D3-B09-S088
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A policy route matches fields such as ingress, source, destination and service as supported; If matched and valid, it directs a next hop/interface before normal route selection; A supporting route and reachable next hop are still required; PBR increases operational complexity; document scope and fallback
Instructor demonstration / expected result: Inspect policy-route list and debug-flow route decision for the exact test tuple.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Practical handoff: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “PBR can override destination-route intent for selected traffic” before showing the answer.

## Slide 85
85
Redistribution moves selected routes between protocols
• Redistribute only intentional prefixes with route maps/prefix filters
• Metrics and tags help prevent loops and control preference
• A route in one database is not automatically advertised into another
• Default-route origination should be conditional and documented
ILLUSTRATIVE SCENARIO
Static branch /24 enters OSPF only if it passes the prefix policy
EXPECTED RESULT
Verify source route, redistribution rule, advertised LSA and remote installation.
Expected observation
The OSPF neighbor reaches Full and the advertised branch prefix is installed with the expected next hop.
089 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: [CORE LECTURE] Stable ID: D3-B09-S089
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Redistribute only intentional prefixes with route maps/prefix filters; Metrics and tags help prevent loops and control preference; A route in one database is not automatically advertised into another; Default-route origination should be conditional and documented
Instructor demonstration / expected result: Verify source route, redistribution rule, advertised LSA and remote installation.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Practical handoff: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Redistribution moves selected routes between protocols” before showing the answer.

## Slide 86
086
OSPF neighbors exchange LSAs; SPF installs the best route
Concrete example: Branch advertises 10.20.10.0/24 into area 0
86
HQ FGT
RID 10.255.0.1
Hello / DBD / LSA
AREA 0
transit network
LSA / ACK
BRANCH FGT
RID 10.255.0.2
BRANCH LAN
10.20.10.0/24
LAN
NEIGHBOR STATE
Down → Init → 2-Way → ExStart → Exchange → Loading → Full
HQ ROUTING TABLE
O 10.20.10.0/24 via <Branch overlay IP> The route appears only after adjacency and LSA processing.
LESSON
Full adjacency is necessary, but the learned prefix must also appear in the LSDB and active routing table.
Notes: Expected result: the neighbor reaches Full; the LSDB contains the branch prefix; HQ installs 10.20.10.0/24 with the intended OSPF next hop. Source: FortiOS 7.6.7 Administration Guide — OSPF neighbors, LSDB and routing table.

## Slide 87
87
LSAs build a shared topology; SPF installs best paths
R1 AREA 0
LSA FLOOD
R2 LSDB
SPF → ROUTE
A connected /24 is advertised, appears in LSDB, then installs as OSPF route
• Routers flood link-state information within defined scope
• Area design limits flooding and supports hierarchy
• The LSDB is not the routing table; SPF derives candidate paths
• Route type and metric influence the installed result
Compare the OSPF database, installed route and one forwarded test flow.
091 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: [CORE LECTURE] Stable ID: D3-B09-S091
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Routers flood link-state information within defined scope; Area design limits flooding and supports hierarchy; The LSDB is not the routing table; SPF derives candidate paths; Route type and metric influence the installed result
Instructor demonstration / expected result: Compare OSPF database, routing table and packet forwarding state/output.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Practical handoff: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “LSAs build a shared topology; SPF installs best paths” before showing the answer.

## Slide 88
088
OSPF route exchange
88
01
Reach Full neighbor
02
Receive/flood LSA
03
Run SPF
04
Install route
05
Forward test traffic
EXPECTED RESULT
The OSPF neighbor reaches Full and the advertised branch prefix is installed with the expected next hop.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D3-B09-S092
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm interface and router ID; Reach Full neighbor state where expected; Verify prefix exists in LSDB with intended LSA/type; Verify active route and return route; Test traffic and preserve packet/session state/output
Instructor demonstration / expected result: Use neighbor, database and routing-table commands together.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Practical handoff: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “OSPF exchange state/output” before showing the answer.

## Slide 89
089
Common mistakes—and how to correct them
89
MISTAKE
CORRECTION — AND WHY IT HELPS
Troubleshoot only the routing table
Check neighbor state and LSDB first; no route installs until adjacency and LSA exchange succeed.
Redistribute every route
Apply prefix/route-map filters; controlled redistribution prevents leaks and loops.
Use PBR to hide a return-path problem
Correct both route directions; PBR only changes selected matching traffic.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D3-B09-S093
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Practical handoff: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 90
90
Troubleshooting workflow: narrow the failed decision
01
Check physical/IP reachability and PBR scope
02
Verify OSPF interface/area/timers/authentication/MTU
03
Inspect neighbor state transition
04
Inspect LSDB and redistribution filter
05
Confirm active route, policy and return path
What to observe
• Inspect neighbor state transition
• Inspect LSDB and redistribution filter
• Confirm active route, policy and return path
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
094 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: [CORE LECTURE] Stable ID: D3-B09-S094
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check physical/IP reachability and PBR scope; Verify OSPF interface/area/timers/authentication/MTU; Inspect neighbor state transition; Inspect LSDB and redistribution filter; Confirm active route, policy and return path
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Practical handoff: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 91
91
Practical handoff: predict, observe, explain
• Prerequisite: Static routing mastery
• Prerequisite: Two routing peers or instructor simulation
• Goal: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The OSPF neighbor reaches Full and the advertised branch prefix is installed with the expected next hop.
095 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: [CORE LECTURE] Stable ID: D3-B09-S095
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Static routing mastery; Prerequisite: Two routing peers or instructor simulation; Goal: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Practical handoff: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 92
92
Knowledge check — explain the result
QUESTION 1
• Which command output shows route exchange beyond adjacency?
QUESTION 2
• Why filter redistribution?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
096 • DAY 3 • BLOCK 09 • Route Selection, PBR & OSPF
Notes: [CORE LECTURE] Stable ID: D3-B09-S096
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Which state/output proves route exchange beyond adjacency?; Why filter redistribution?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Troubleshooting only the routing table when adjacency is down; Redistributing everything without filters/tags; Using PBR to mask an addressing or return-path problem
Practical handoff: Form one OSPF adjacency or inspect an instructor capture, advertise a lab prefix, and prove neighbor → LSA → route → traffic. PBR change is isolated and includes rollback.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Policy routes; OSPF; Route maps and prefix lists; Route redistribution. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: Which state/output proves route exchange beyond adjacency?
A: The expected LSA/prefix in the database and installed route on the peer.
Q: Why filter redistribution?
A: To limit scope, prevent loops/leaks and preserve predictable path selection.

## Slide 93
DAY 3 • 10:30–12:00
BGP exchanges policy-controlled reachability between autonomous systems
BGP Fundamentals & Practical Use • Advanced Day 1
BGP IN ONE MINUTE
• An autonomous system (AS) applies one routing policy under an AS number
• eBGP peers use different ASes; iBGP peers share an AS
• TCP/179 and OPEN/KEEPALIVE must succeed before UPDATE messages
• Filters control which prefixes are accepted and advertised
PEERING STATE
• Route to neighbor and TCP reachability
• State progresses to Established
• Intended prefix is advertised/received
• Best path installs with reachable next hop
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
097
Notes: [CORE LECTURE] Stable ID: D3-B10-S097
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain autonomous systems, eBGP/iBGP and neighbor establishment; Advertise only intended prefixes; Use attributes and filters to predict path selection
Instructor demonstration / expected result: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “BGP Fundamentals & Practical Use” before showing the answer.

## Slide 94
094
BGP policy controls which reachable prefixes cross an AS boundary
Received does not automatically mean selected or installed
94
HQ • AS 65010
advertises 10.10.10.0/24
eBGP TCP/179
EDGE • AS 65020
filter policy
accepted prefix
BRANCH • AS 65100
receives UPDATE
OUTBOUND FILTER AT AS 65010
permit 10.10.10.0/24 deny 0.0.0.0/0 le 32
CONTROL → FORWARDING
1 Prefix received
2 Policy permits
3 Best path selected
4 Next hop reachable
5 Route installed
INSTALLED ROUTE
B 10.10.10.0/24 via <eBGP next hop>
LESSON
Troubleshoot BGP in order: peer Established → prefix permitted → best path selected → next hop resolved → route installed.
Notes: Expected result: only 10.10.10.0/24 is advertised; the peer receives it, marks one path best, resolves the next hop and installs the route. Source: FortiOS 7.6.7 Administration Guide — BGP, route maps and prefix lists.

## Slide 95
95
BGP neighbor state reveals the failed stage
01
Idle
02
Connect
03
OpenSent
04
OpenConfirm
05
Established
What to observe
• OpenSent/OpenConfirm indicate BGP capability/parameter exchange
• Established permits UPDATE messages
• Timers, source address, multihop, password and AS configuration must agree
INSTRUCTOR DEMONSTRATION
get router info bgp summary; inspect peer state, uptime and received/advertised counts.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
099 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: [CORE LECTURE] Stable ID: D3-B10-S099
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Idle/Connect/Active indicate transport or retry state; OpenSent/OpenConfirm indicate BGP capability/parameter exchange; Established permits UPDATE messages; Timers, source address, multihop, password and AS configuration must agree
Instructor demonstration / expected result: get router info bgp summary; inspect peer state, uptime and received/advertised counts.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “BGP neighbor state reveals the failed stage” before showing the answer.

## Slide 96
96
eBGP and iBGP serve different propagation roles
eBGP
• Different AS
• External policy boundary
• AS_PATH changes
iBGP
• Same AS
• Internal distribution
• Full mesh or RR design
KEY DISTINCTION
Route reflector design is optional deep dive; do not infer full-mesh scalability
100 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: [CORE LECTURE] Stable ID: D3-B10-S100
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: eBGP exchanges routes across AS boundaries and commonly changes next-hop behavior; iBGP distributes external/internal reachability within one AS; iBGP split-horizon requires full mesh or route reflectors at scale; IGP reachability to BGP next hops remains essential
Instructor demonstration / expected result: Trace next hop and AS_PATH after each advertisement.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “eBGP and iBGP serve different propagation roles” before showing the answer.

## Slide 97
97
Prefix advertisement requires route presence and policy permission
• A network statement/redistribution mechanism does not create reachability by itself
• The prefix must meet the platform’s origination conditions
• Outbound filters prevent accidental leaks
• Inbound filters and maximum-prefix controls limit accepted scope
ILLUSTRATIVE SCENARIO
Advertise 10.20.10.0/24 only; reject documentation default and unrelated internal routes
EXPECTED RESULT
Compare local route, advertised-routes, peer received-routes and active table.
Expected observation
The peer reaches Established, the permitted prefix is received, and the selected BGP path is installed.
101 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: [CORE LECTURE] Stable ID: D3-B10-S101
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A network statement/redistribution mechanism does not create reachability by itself; The prefix must meet the platform’s origination conditions; Outbound filters prevent accidental leaks; Inbound filters and maximum-prefix controls limit accepted scope
Instructor demonstration / expected result: Compare local route, advertised-routes, peer received-routes and active table.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Prefix advertisement requires route presence and policy permission” before showing the answer.

## Slide 98
98
BGP path selection is ordered, not a vote
PATH A
• local-pref 200
• AS_PATH 65020 65100
• next hop reachable
PATH B
• local-pref 100
• AS_PATH 65200
• next hop reachable
RESULT
• A wins at local preference
• Later criteria not evaluated
• Validate best-path marker
KEY DISTINCTION
Two /24 paths: higher local preference can win before shorter AS_PATH
102 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: [CORE LECTURE] Stable ID: D3-B10-S102
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Policy can set weight/local preference and other attributes depending on scope; AS_PATH length, origin, MED, eBGP/iBGP and IGP cost are evaluated in an implementation-defined order; Only compare attributes when earlier criteria tie; Document which attributes are locally significant and confirm exact FortiOS order
Instructor demonstration / expected result: Inspect all paths and identify the first decision point that differs.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “BGP path selection is ordered, not a vote” before showing the answer.

## Slide 99
99
Route maps and prefix lists implement routing policy
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
get router info bgp summary get router info bgp network get router info bgp neighbors <peer> advertised-routes get router info bgp neighbors <peer> received-routes
READ THE OUTPUT
• Prefix lists match address and prefix-length ranges
• Route maps match and permit/deny or set attributes
• Direction matters: inbound changes acceptance; outbound changes advertisement
• Always include an explicit policy for default/unmatched routes
Safe operation
Outbound permit for 10.20.10.0/24; deny everything else
103 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: [CORE LECTURE] Stable ID: D3-B10-S103
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prefix lists match address and prefix-length ranges; Route maps match and permit/deny or set attributes; Direction matters: inbound changes acceptance; outbound changes advertisement; Always include an explicit policy for default/unmatched routes
Instructor demonstration / expected result: Review policy counters/advertised routes before and after change.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Route maps and prefix lists implement routing policy” before showing the answer.

## Slide 100
100
BGP state connects peer, prefix selection and forwarding
• Peer state: Established with stable uptime
• Control plane: expected prefix received/advertised and best path selected
• Routing table: BGP route installed with intended next hop
• Data plane: policy/session/packet behavior follows that next hop
ILLUSTRATIVE SCENARIO
A received route can lose selection or fail installation; never stop at prefix count
EXPECTED RESULT
Capture summary, detailed prefix, route table and one test flow.
Expected observation
The peer reaches Established, the permitted prefix is received, and the selected BGP path is installed.
104 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: [CORE LECTURE] Stable ID: D3-B10-S104
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Peer state: Established with stable uptime; Control plane: expected prefix received/advertised and best path selected; Routing table: BGP route installed with intended next hop; Data plane: policy/session/packet state/output follows that next hop
Instructor demonstration / expected result: Capture summary, detailed prefix, route table and one test flow.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “BGP state/output connects peer, prefix and forwarding” before showing the answer.

## Slide 101
101
Controlled BGP advertisement
101
01
Peer reaches Established
02
Prefix list permits /24
03
UPDATE advertises prefix
04
Peer selects best path
05
Route installs
EXPECTED RESULT
The peer reaches Established, the permitted prefix is received, and the selected BGP path is installed.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D3-B10-S105
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Establish one eBGP peer; Originate one exact lab prefix; Apply outbound prefix filter; Confirm remote receipt and best path; Withdraw or deny and observe controlled change
Instructor demonstration / expected result: No production ASN or public prefix is implied.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “BGP controlled advertisement” before showing the answer.

## Slide 102
102
Common mistakes—and how to correct them
102
MISTAKE
CORRECTION — AND WHY IT HELPS
Call Active state healthy
Check TCP/179 and peer parameters; BGP Active means the session is not Established.
Advertise a broad default accidentally
Use an explicit outbound prefix list and review advertised-routes before activation.
Tune attributes before next-hop reachability
Resolve the next hop first; an unusable path cannot enter forwarding.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D3-B10-S106
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 103
103
Troubleshooting workflow: narrow the failed decision
01
Verify route and TCP/179 reachability to peer
02
Check local/remote AS, update source, password and timers
03
Reach Established; inspect notifications if not
04
Verify origination and inbound/outbound filters
05
Confirm best path, active route and return path
What to observe
• Reach Established; inspect notifications if not
• Verify origination and inbound/outbound filters
• Confirm best path, active route and return path
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
107 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: [CORE LECTURE] Stable ID: D3-B10-S107
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Verify route and TCP/179 reachability to peer; Check local/remote AS, update source, password and timers; Reach Established; inspect notifications if not; Verify origination and inbound/outbound filters; Confirm best path, active route and return path
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 104
104
Practical handoff: predict, observe, explain
• Prerequisite: IP reachability between peers
• Prerequisite: Unique AS and router-ID plan
• Goal: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The peer reaches Established, the permitted prefix is received, and the selected BGP path is installed.
108 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: [CORE LECTURE] Stable ID: D3-B10-S108
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: IP reachability between peers; Prerequisite: Unique AS and router-ID plan; Goal: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 105
105
Knowledge check — explain the result
QUESTION 1
• What does Established prove?
QUESTION 2
• Which path wins if local preference differs?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
109 • DAY 3 • BLOCK 10 • BGP Fundamentals
Notes: [CORE LECTURE] Stable ID: D3-B10-S109
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What does Established prove?; Which path wins if local preference differs?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Calling Active state established; Advertising a broad aggregate/default unintentionally; Changing AS_PATH/MED before checking next-hop reachability
Practical handoff: Build or inspect one eBGP peering, advertise a single lab /24 through an explicit prefix list, then prove advertised, received, selected and forwarded state/output.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: BGP; BGP neighbors; Route maps and prefix lists; BGP path selection. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: What does Established prove?
A: The BGP session exchanged OPEN/KEEPALIVE successfully; it does not prove any particular prefix is permitted or installed.
Q: Which path wins if local preference differs?
A: The higher local preference wins before later criteria such as AS_PATH, subject to the exact FortiOS selection order.

## Slide 106
DAY 3 • 13:00–14:30
IPsec VPN Architecture & ADVPN
Advanced • Day 1 of 2
LEARNING OBJECTIVES
• Relate IKEv2 Phase 1, Phase 2 and route-based forwarding
• Design selectors, routes and policies as one system
• Explain ADVPN underlay/overlay, hub/spoke and shortcut behavior
PREREQUISITES + PRACTICE RESERVE
• Working underlay IP reachability
• Defined protected prefixes and crypto policy
• ADVPN feature/version support confirmed before lab
Teach ~60 min • reserve ~30 min for guided activity, discussion and debrief
110
Notes: [CORE LECTURE] Stable ID: D3-B11-S110
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Relate IKEv2 Phase 1, Phase 2 and route-based forwarding; Design selectors, routes and policies as one system; Explain ADVPN underlay/overlay, hub/spoke and shortcut behavior
Instructor demonstration / expected result: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “IPsec VPN Architecture & ADVPN” before showing the answer.

## Slide 107
107
Route-based IPsec connects protected subnets over an underlay
Negotiation creates SAs; application traffic follows routes and firewall policies
107
HQ LAN
10.10.10.0/24
HQ FGVM
peer 203.0.113.2
AZURE / INTERNET
underlay reachability
BRANCH FGVM
peer 198.51.100.2
BRANCH LAN
10.20.10.0/24
UDP 500/4500
IKEv2
IPsec overlay / CHILD SA selectors: 10.10.10.0/24 ↔ 10.20.10.0/24
CONTROL
IKE_SA_INIT → IKE_AUTH → CHILD SA
DATA
route → tunnel interface → policy → encrypted packets
LESSON
A tunnel can be “up” while application traffic fails because route, policy, selectors or return path are wrong.
Notes: Expected result: IKE and IPsec SAs are established, the branch route points to the tunnel interface, matching policies allow the flow, and encaps/decaps counters increase. Source: FortiOS 7.6.7 Administration Guide — IKEv2 and route-based IPsec VPN.

## Slide 108
108
IKEv2 negotiation produces authenticated secure state
01
IKE_SA_INIT
02
IKE_AUTH
03
CHILD SA
04
Route/policy
05
Protected traffic
What to observe
• Proposal, authentication method, IDs and reachability must be compatible
• NAT traversal and fragmentation behavior depend on path/design
• Logs/debug should be filtered by peer and stopped after capture
INSTRUCTOR DEMONSTRATION
Use tunnel summary and filtered IKE diagnostics; do not paste invented output.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
112 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [CORE LECTURE] Stable ID: D3-B11-S112
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Peers exchange proposals, identities, authentication and key material; Proposal, authentication method, IDs and reachability must be compatible; NAT traversal and fragmentation behavior depend on path/design; Logs/debug should be filtered by peer and stopped after capture
Instructor demonstration / expected result: Use tunnel summary and filtered IKE diagnostics; do not paste invented output.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “IKEv2 negotiation produces authenticated secure state” before showing the answer.

## Slide 109
109
Phase 2 selectors define permitted protected traffic
• Route-based designs may use broad selectors but still require routing/policy boundaries
• Mismatched local/remote selectors prevent or limit SA establishment
• Overlapping prefixes complicate route and identity decisions
• Rekey/lifetime mismatches can appear as intermittent failures
ILLUSTRATIVE SCENARIO
HQ local 10.10.10.0/24 must match Branch remote 10.10.10.0/24 reciprocally
EXPECTED RESULT
Compare selectors on both peers and active SA packet counters.
Expected observation
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
113 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [CORE LECTURE] Stable ID: D3-B11-S113
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Route-based designs may use broad selectors but still require routing/policy boundaries; Mismatched local/remote selectors prevent or limit SA establishment; Overlapping prefixes complicate route and identity decisions; Rekey/lifetime mismatches can appear as intermittent failures
Instructor demonstration / expected result: Compare selectors on both peers and active SA packet counters.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “Phase 2 selectors define permitted protected traffic” before showing the answer.

## Slide 110
110
VPN design begins with failure domains and scale
• Define underlay resilience, addressing, routing ownership and crypto standards
• Choose static mesh, hub-spoke or dynamic overlay based on scale and traffic patterns
• Account for MTU/MSS, NAT, asymmetric paths and overlapping networks
• Document monitoring, certificate/PSK lifecycle and change coordination
ILLUSTRATIVE SCENARIO
A tunnel “up” with no traffic can still be a routing, policy or return-path failure
EXPECTED RESULT
Design review must include data-plane test cases, not only IKE settings.
Expected observation
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
114 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [CORE LECTURE] Stable ID: D3-B11-S114
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Define underlay resilience, addressing, routing ownership and crypto standards; Choose static mesh, hub-spoke or dynamic overlay based on scale and traffic patterns; Account for MTU/MSS, NAT, asymmetric paths and overlapping networks; Document monitoring, certificate/PSK lifecycle and change coordination
Instructor demonstration / expected result: Design review must include data-plane test cases, not only IKE settings.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “VPN design begins with failure domains and scale” before showing the answer.

## Slide 111
111
ADVPN starts through the hub, then builds a spoke shortcut
Underlay reaches tunnel endpoints; overlay routes select protected destinations
111
SPOKE A
LAN 10.20.10.0/24
HUB
control / discovery
SPOKE B
LAN 10.30.10.0/24
1 initial data → hub
1 hub → spoke B
2 Dynamic shortcut tunnel: subsequent spoke-to-spoke application traffic
UNDERLAY
Public/private transport routes reach hub and spoke tunnel endpoints.
OVERLAY
Protected prefixes and dynamic routing choose the logical tunnel path.
LESSON
Shortcut formation changes the data path; hub discovery/control activity and underlay reachability remain essential.
Notes: Instructor review: ADVPN generation and OSPF-over-ADVPN behavior are release/design dependent. Confirm the supported FortiOS 7.6.7 Azure topology before lab use. Source: FortiOS 7.6.7 Administration Guide — ADVPN and dynamic routing over IPsec.

## Slide 112
112
OSPF over ADVPN requires intentional network behavior
• Neighbor model, network type and area design must fit the overlay
• Shortcut routing must not break next-hop resolution
• Hub route reflection/advertisement choices affect spoke reachability
• Scale testing must include neighbors, LSAs, routes, tunnels and CPU/memory
ILLUSTRATIVE SCENARIO
Do not present one OSPF-over-ADVPN recipe as universal
EXPECTED RESULT
Confirm FortiOS 7.6.7 ADVPN guidance and the supported Azure FGVM topology before implementation.
Expected observation
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
116 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [OPTIONAL DEEP DIVE] Stable ID: D3-B11-S116
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Neighbor model, network type and area design must fit the overlay; Shortcut routing must not break next-hop resolution; Hub route reflection/advertisement choices affect spoke reachability; Scale testing must include neighbors, LSAs, routes, tunnels and CPU/memory
Instructor demonstration / expected result: Confirm FortiOS 7.6.7 ADVPN guidance and the supported Azure FGVM topology before implementation.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “OSPF over ADVPN requires intentional network behavior” before showing the answer.

## Slide 113
113
ADVPN sizing tracks spokes, tunnels, routes and sessions
• Estimate concurrent hub-spoke and shortcut tunnels
• Account for route scale, neighbor scale, session count, crypto throughput and inspection
• Use platform data sheets and validated design guides, not slide estimates
• Failure/rekey storms can be more demanding than steady state
ILLUSTRATIVE SCENARIO
Sizing remains an instructor design exercise without a declared appliance/model and traffic profile
EXPECTED RESULT
Record assumptions and validate against current Fortinet sizing guidance.
Expected observation
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
117 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [OPTIONAL DEEP DIVE] Stable ID: D3-B11-S117
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Estimate concurrent hub-spoke and shortcut tunnels; Account for route scale, neighbor scale, session count, crypto throughput and inspection; Use platform data sheets and validated design guides, not slide estimates; Failure/rekey storms can be more demanding than steady state
Instructor demonstration / expected result: Record assumptions and validate against current Fortinet sizing guidance.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “ADVPN sizing tracks spokes, tunnels, routes and sessions” before showing the answer.

## Slide 114
114
Route-based VPN
114
01
Reach peer over underlay
02
Create IKE SA
03
Create CHILD SA
04
Route points to tunnel
05
Policy permits protected flow
EXPECTED RESULT
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D3-B11-S118
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Underlay reaches peer address; IKEv2 authenticates peers and creates IKE SA; CHILD SA selectors protect intended prefixes; Routes send traffic to tunnel; policies permit both directions; Return route and session counters prove bidirectional flow
Instructor demonstration / expected result: Validate one layer at a time.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “End-to-end route-based VPN design” before showing the answer.

## Slide 115
115
Common mistakes—and how to correct them
115
MISTAKE
CORRECTION — AND WHY IT HELPS
Check only tunnel-up status
Verify selectors, route, policy and bidirectional counters; IKE state alone does not carry traffic.
Confuse underlay and overlay routes
Check peer reachability separately from protected-prefix routes; they solve different paths.
Copy one ADVPN recipe everywhere
Confirm the supported 7.6.7 ADVPN generation and routing design before configuration.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D3-B11-S119
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 116
116
Troubleshooting workflow: narrow the failed decision
01
Prove underlay route and UDP/500/4500 reachability
02
Validate Phase 1 identity/proposal/authentication
03
Validate Phase 2 selectors/proposals and counters
04
Check overlay route, policies and return path
05
Capture filtered packets/IKE diagnostics; reset debug
What to observe
• Validate Phase 2 selectors/proposals and counters
• Check overlay route, policies and return path
• Capture filtered packets/IKE diagnostics; reset debug
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
120 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [CORE LECTURE] Stable ID: D3-B11-S120
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prove underlay route and UDP/500/4500 reachability; Validate Phase 1 identity/proposal/authentication; Validate Phase 2 selectors/proposals and counters; Check overlay route, policies and return path; Capture filtered packets/IKE diagnostics; reset debug
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 117
117
Practical handoff: predict, observe, explain
• Prerequisite: Working underlay IP reachability
• Prerequisite: Defined protected prefixes and crypto policy
• Goal: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
IKE and IPsec SAs are up, the protected route points to the tunnel, and both tunnel counters increase.
121 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [CORE LECTURE] Stable ID: D3-B11-S121
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Working underlay IP reachability; Prerequisite: Defined protected prefixes and crypto policy; Goal: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 118
118
Knowledge check — explain the result
QUESTION 1
• What does a route-based tunnel still need after SAs are up?
QUESTION 2
• What is the ADVPN shortcut for?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
122 • DAY 3 • BLOCK 11 • IPsec & ADVPN
Notes: [CORE LECTURE] Stable ID: D3-B11-S122
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What does a route-based tunnel still need after SAs are up?; What is the ADVPN shortcut for?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Checking only tunnel-up status; Confusing underlay peer reachability with overlay protected routing; Assuming an ADVPN/OSPF example applies to every 7.6.7 deployment variant
Practical handoff: Configure or inspect one route-based IKEv2 tunnel. ADVPN and OSPF-over-ADVPN are instructor demo/conceptual unless matching licenses, topology and exact release support are confirmed.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec VPN; IKEv2; Route-based VPN; ADVPN; Dynamic routing over IPsec. FortiOS 7.6.7 CLI Reference and release notes.
Knowledge check answer key:
Q: What does a route-based tunnel still need after SAs are up?
A: Routes, firewall policies, matching selectors and a valid return path.
Q: What is the ADVPN shortcut for?
A: To let eligible spoke-to-spoke data bypass the hub after dynamic discovery, while the underlay still reaches tunnel endpoints.

## Slide 119
DAY 3 • 14:30–16:00
VPN Troubleshooting & Operational Validation
Advanced • Day 1 of 2
LEARNING OBJECTIVES
• Localize failure across underlay, IKE, IPsec, routing, policy and return path
• Interpret Phase 1/2 state and selectors
• Use packet capture and CLI diagnostics without uncontrolled debug
PREREQUISITES + PRACTICE RESERVE
• Known-good test endpoints
• Authorization for VPN diagnostics
• Peer-side state or an instructor-provided capture
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
123
Notes: [CORE LECTURE] Stable ID: D3-B12-S123
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Localize failure across underlay, IKE, IPsec, routing, policy and return path; Interpret Phase 1/2 state and selectors; Use packet capture and CLI diagnostics without uncontrolled debug
Instructor demonstration / expected result: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “VPN Troubleshooting & Operational Validation” before showing the answer.

## Slide 120
120
Tunnel establishment is a layered dependency chain
01
Underlay
02
IKE SA
03
IPsec SA
04
Route
05
Policy/session
06
Return path
What to observe
• IKE SA precedes CHILD/IPsec SA
• Selectors and traffic triggers affect Phase 2
• Routes, policies and return path determine usable data flow
INSTRUCTOR DEMONSTRATION
Record state and timestamps before remediation.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
124 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S124
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Underlay route and peer reachability precede IKE; IKE SA precedes CHILD/IPsec SA; Selectors and traffic triggers affect Phase 2; Routes, policies and return path determine usable data flow
Instructor demonstration / expected result: Record state and timestamps before remediation.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Tunnel establishment is a layered dependency chain” before showing the answer.

## Slide 121
121
Phase 1 state isolates reachability, identity and proposal faults
• No response suggests path, NAT or peer availability
• Proposal mismatch prevents cryptographic agreement
• Authentication/ID mismatch fails after initial exchange
• Certificate failures require time, chain and identity checks
ILLUSTRATIVE SCENARIO
Filter IKE diagnostics to the peer; avoid broad debug on production
EXPECTED RESULT
Compare both peers’ timestamps and stated failure reason.
Expected observation
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
125 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S125
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: No response suggests path, NAT or peer availability; Proposal mismatch prevents cryptographic agreement; Authentication/ID mismatch fails after initial exchange; Certificate failures require time, chain and identity checks
Instructor demonstration / expected result: Compare both peers’ timestamps and stated failure reason.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Phase 1 state/output isolates identity and proposal faults” before showing the answer.

## Slide 122
122
Phase 2 state links selectors to directional packet counters
• An IKE SA can be healthy while no CHILD SA exists
• Selector mismatch or proposal mismatch prevents data SA
• Encaps/decaps counters show directionality
• Rekey failures may preserve old state briefly, causing intermittent symptoms
ILLUSTRATIVE SCENARIO
Encaps increasing with zero decaps points toward the remote policy, path or return route
EXPECTED RESULT
Compare both endpoints’ SA and packet counters.
Expected observation
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
126 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S126
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: An IKE SA can be healthy while no CHILD SA exists; Selector mismatch or proposal mismatch prevents data SA; Encaps/decaps counters show directionality; Rekey failures may preserve old state briefly, causing intermittent symptoms
Instructor demonstration / expected result: Compare both endpoints’ SA and packet counters.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Phase 2 state/output links selectors to packet counters” before showing the answer.

## Slide 123
123
Routing chooses the tunnel; policy permits the chosen path
• Route lookup must select the tunnel for the protected destination
• Policy ingress/egress pair must match actual interfaces
• A broader WAN route can steal traffic if overlay route is absent
• Return path must choose the reciprocal tunnel or valid symmetric design
ILLUSTRATIVE SCENARIO
Tunnel-up does not override a more-specific route to another interface
EXPECTED RESULT
Run route lookup for both destination directions.
Expected observation
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
127 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S127
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Route lookup must select the tunnel for the protected destination; Policy ingress/egress pair must match actual interfaces; A broader WAN route can steal traffic if overlay route is absent; Return path must choose the reciprocal tunnel or valid symmetric design
Instructor demonstration / expected result: Run route lookup for both destination directions.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Routing chooses the tunnel; policy permits the chosen path” before showing the answer.

## Slide 124
124
Sessions preserve the chosen VPN and NAT state
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
get vpn ipsec tunnel summary diagnose vpn tunnel list get router info routing-table details <protected-ip> diagnose sys session filter dst <protected-ip> diagnose sys session list
READ THE OUTPUT
• Existing sessions can continue using old routing/policy decisions
• A configuration fix may require a new test tuple or authorized session clear
• NAT is usually unintended for site-to-site protected traffic unless designed
• Asymmetric return creates one-sided counters and incomplete sessions
Safe operation
Use a new source port before disruptive session clearing
128 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S128
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Existing sessions can continue using old routing/policy decisions; A configuration fix may require a new test tuple or authorized session clear; NAT is usually unintended for site-to-site protected traffic unless designed; Asymmetric return creates one-sided counters and incomplete sessions
Instructor demonstration / expected result: If clearing, filter narrowly and warn learners about impact.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Sessions preserve the chosen VPN and NAT state” before showing the answer.

## Slide 125
125
Packet capture shows where protected traffic stops
• Capture IKE on the underlay and protected traffic on LAN/tunnel-relevant interfaces
• One-sided protected packets reveal where forwarding stops
• ESP versus UDP/4500 depends on NAT traversal/path
• Schematic output must be labelled illustrative unless captured in the declared lab
ILLUSTRATIVE SCENARIO
Use host/port filters and bounded packet counts
EXPECTED RESULT
Stop capture/debug and sanitize addresses before sharing.
Expected observation
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
129 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S129
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Capture IKE on the underlay and protected traffic on LAN/tunnel-relevant interfaces; One-sided protected packets reveal where forwarding stops; ESP versus UDP/4500 depends on NAT traversal/path; Schematic output must be labelled illustrative unless captured in the declared lab
Instructor demonstration / expected result: Stop capture/debug and sanitize addresses before sharing.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Packet capture bridges control state and actual traffic” before showing the answer.

## Slide 126
126
Certificate inspection versus deep inspection
OPTION A
• Certificate inspection reads TLS handshake/certificate metadata without decrypting application payload
• Deep inspection proxies TLS and exposes payload to security profiles
OPTION B
• Deep inspection requires endpoint trust in the FortiGate inspection CA
• Pinning, privacy policy and performance may require scoped exceptions
KEY DISTINCTION
This is a cross-course diagnostic reminder: IPsec protects packets between gateways; SSL inspection acts on application TLS flows according to policy
130 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S130
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Certificate inspection reads TLS handshake/certificate metadata without decrypting application payload; Deep inspection proxies TLS and exposes payload to security profiles; Deep inspection requires endpoint trust in the FortiGate inspection CA; Pinning, privacy policy and performance may require scoped exceptions
Instructor demonstration / expected result: Validate client certificate chain and matched SSL/SSH profile.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Certificate inspection versus deep inspection” before showing the answer.

## Slide 127
127
VPN fault isolation
127
01
Underlay reachability
02
Phase 1 state
03
Phase 2 selectors/counters
04
Overlay route/policy
05
Return traffic
EXPECTED RESULT
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D3-B12-S131
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Symptom: Branch cannot reach HQ server; Check underlay and IKE state; Check CHILD SA selectors/counters; Check route and policy on both peers; Check session and captures; remediate only the failed layer
Instructor demonstration / expected result: Resolution criterion: bidirectional packets plus expected SA/session counters.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Single VPN fault tree” before showing the answer.

## Slide 128
128
Common mistakes—and how to correct them
128
MISTAKE
CORRECTION — AND WHY IT HELPS
Restart IKE before collecting state
Record peer/SA error and counters first; restart removes the failing condition.
Clear every session
Use a fresh test flow or narrow filter; broad clearing hides scope and disrupts service.
Declare success from Phase 1
Require route, policy and increasing encap/decap counters; Phase 1 authenticates only the peers.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D3-B12-S132
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 129
129
Troubleshooting workflow: narrow the failed decision
01
Underlay route/capture
02
Phase 1 peer/proposal/identity
03
Phase 2 selectors/proposal/counters
04
Overlay route and policies
05
Session, NAT and return-path capture
What to observe
• Phase 2 selectors/proposal/counters
• Overlay route and policies
• Session, NAT and return-path capture
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
133 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S133
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Underlay route/capture; Phase 1 peer/proposal/identity; Phase 2 selectors/proposal/counters; Overlay route and policies; Session, NAT and return-path capture
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 130
130
Practical handoff: predict, observe, explain
• Prerequisite: Known-good test endpoints
• Prerequisite: Authorization for VPN diagnostics
• Goal: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; the captured state must identify the failed layer and the retest must show restoration.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; the captured state must identify the failed layer and the retest must show restoration.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The failed VPN layer is identified by peer state, selectors, route, policy and directional counters.
134 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S134
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Known-good test endpoints; Prerequisite: Authorization for VPN diagnostics; Goal: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 131
131
Knowledge check — explain the result
QUESTION 1
• If encaps increases but decaps stays zero, what does it suggest?
QUESTION 2
• Why use a new five-tuple after a route change?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
135 • DAY 3 • BLOCK 12 • VPN Troubleshooting
Notes: [CORE LECTURE] Stable ID: D3-B12-S135
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: If encaps increases but decaps stays zero, what does it suggest?; Why use a new five-tuple after a route change?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Restarting IKE before preserving failure state/output; Clearing all sessions instead of using a fresh tuple/filter; Declaring success from Phase 1 only
Practical handoff: Instructor injects one safe fault (missing lab route, selector mismatch or disabled test policy). Teams diagnose without broad debug; state/output must identify the failed layer and prove restoration.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: IPsec monitoring and troubleshooting; Debugging IPsec VPN; Packet sniffer; Sessions. FortiOS 7.6.7 CLI Reference.
Knowledge check answer key:
Q: If encaps increases but decaps stays zero, what does it suggest?
A: Local traffic enters encryption but return protected traffic is not arriving; inspect remote routing/policy/peer path.
Q: Why use a new five-tuple after a route change?
A: Existing session state may retain the previous egress/policy decision.

## Slide 132
DAY 4 • 09:00–10:30
FortiClient Architecture & EMS Awareness
Advanced • Day 2 of 2
LEARNING OBJECTIVES
• Describe FortiClient components, VPN profiles and endpoint integration
• Explain EMS telemetry and centralized profile management
• Compare EMS and Intune by use case without claiming equivalence
PREREQUISITES + PRACTICE RESERVE
• Managed test endpoint for live demo
• FortiClient/EMS versions and licensing declared
• No assumption that EMS is deployed
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
136
Notes: [CORE LECTURE] Stable ID: D4-B13-S136
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Describe FortiClient components, VPN profiles and endpoint integration; Explain EMS telemetry and centralized profile management; Compare EMS and Intune by use case without claiming equivalence
Instructor demonstration / expected result: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “FortiClient Architecture & EMS Awareness” before showing the answer.

## Slide 133
133
FortiClient is an endpoint platform with modular capabilities
ENDPOINT
FORTICLIENT MODULES
FORTIGATE / EMS
Treat “FortiClient installed” as insufficient scope; state the module and management mode
• Available modules depend on edition, platform, license and EMS policy
• VPN, endpoint telemetry, ZTNA and security features have separate prerequisites
• FortiGate remote-access settings and FortiClient profile must align
• Client logs show failures that the status icon does not explain
Record client version, OS, enabled features and profile source.
137 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: [CORE LECTURE] Stable ID: D4-B13-S137
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Available modules depend on edition, platform, license and EMS policy; VPN, endpoint telemetry, ZTNA and security features have separate prerequisites; FortiGate remote-access settings and FortiClient profile must align; Client logs are essential state/output when GUI status is insufficient
Instructor demonstration / expected result: Record client version, OS, enabled features and profile source.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “FortiClient is an endpoint platform with modular capabilities” before showing the answer.

## Slide 134
134
VPN profiles encode gateway and authentication intent
• Profile defines gateway, tunnel type and user/certificate parameters as supported
• Split/full tunnel and DNS behavior affect traffic path
• MFA/SSO/certificate methods require matching FortiGate identity design
• Remote-access option support must be checked for exact FortiOS/FortiClient release
ILLUSTRATIVE SCENARIO
Use placeholders <vpn-gateway> and <auth-method>; do not invent tenant values
EXPECTED RESULT
Check client log, assigned address/routes/DNS and the FortiGate session.
Expected observation
The endpoint shows its assigned FortiClient profile and EMS connection; FortiGate logs the resulting access session.
138 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: [CORE LECTURE] Stable ID: D4-B13-S138
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Profile defines gateway, tunnel type and user/certificate parameters as supported; Split/full tunnel and DNS behavior affect traffic path; MFA/SSO/certificate methods require matching FortiGate identity design; Remote-access option support must be checked for exact FortiOS/FortiClient release
Instructor demonstration / expected result: Validate client log, assigned address/routes/DNS and FortiGate session state/output.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “VPN profiles encode gateway and authentication intent” before showing the answer.

## Slide 135
135
EMS distributes FortiClient policy and receives endpoint telemetry
FortiGate still makes network/VPN access decisions from its configured policy
135
EMS
profiles • inventory telemetry • endpoint tags
policy / telemetry
FORTICLIENT
VPN • certificates posture / logs
VPN / ZTNA
FORTIGATE
auth • policy • session
application
PRIVATE APP
10.20.10.50
MANAGEMENT PLANE
EMS → assigned profile; endpoint → telemetry/status
ACCESS PATH
Endpoint traffic → FortiGate VPN/policy → application
EMS is not implied by installing FortiClient. Check the endpoint’s EMS connection and assigned profile.
LESSON
Correlate endpoint profile, client logs, EMS status and the FortiGate session rather than treating one console as the whole path.
Notes: Expected result: the endpoint is registered to the intended EMS, receives the assigned profile, and its VPN/access session appears on FortiGate. FortiClient/EMS exact release and licensing remain instructor review items. Source: official FortiClient EMS Administration Guide and FortiOS 7.6.7 Administration Guide — endpoint integration.

## Slide 136
136
Endpoint integration connects identity, posture and network policy
• Endpoint tags/posture can inform access policy where supported
• Certificate deployment and trust stores can enable deep inspection or VPN authentication
• Client upgrades/profile changes need staged rollout and rollback
• Privacy and endpoint-ownership boundaries must be documented
ILLUSTRATIVE SCENARIO
A managed device may receive VPN profile and inspection CA through different management systems
EXPECTED RESULT
Prove which system owns each control.
Expected observation
The endpoint shows its assigned FortiClient profile and EMS connection; FortiGate logs the resulting access session.
140 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: [CORE LECTURE] Stable ID: D4-B13-S140
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Endpoint tags/posture can inform access policy where supported; Certificate deployment and trust stores can enable deep inspection or VPN authentication; Client upgrades/profile changes need staged rollout and rollback; Privacy and endpoint-ownership boundaries must be documented
Instructor demonstration / expected result: Prove which system owns each control.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “Endpoint integration connects identity, posture and network policy” before showing the answer.

## Slide 137
137
Inspection profiles on managed endpoints: certificate vs deep inspection
CERTIFICATE INSPECTION
• Reads TLS handshake and certificate metadata
• Does not decrypt application payload
• Lower privacy and endpoint-trust impact
• Cannot scan encrypted content or URLs beyond visible metadata
DEEP INSPECTION
• Terminates and re-signs TLS sessions
• Requires clients to trust the inspection CA
• Enables content/security profile inspection
• Creates compatibility, privacy and performance considerations
KEY DISTINCTION
EMS or another endpoint-management system can distribute the inspection CA; this does not make EMS and Intune equivalent products.
141 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: [CORE LECTURE] Stable ID: D4-B13-S141
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Certificate inspection uses visible TLS metadata and does not decrypt payload; Deep inspection requires endpoint trust in the inspection CA and exposes payload to profiles; EMS can help distribute relevant FortiClient/endpoint policy in supported designs; Intune may distribute certificates/configuration, but it does not become EMS or replace FortiGate inspection policy
Instructor demonstration / expected result: Validate trust chain on endpoint and the policy’s SSL/SSH profile.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “Inspection profiles on managed endpoints: certificate vs deep inspection” before showing the answer.

## Slide 138
138
EMS and Intune overlap only in selected endpoint-management tasks
EMS FIT
• FortiClient profiles
• FortiClient telemetry
• ZTNA/network integration
INTUNE FIT
• Device enrollment
• Broad configuration/app policy
• Microsoft compliance ecosystem
COEXISTENCE
• Clear ownership
• Avoid duplicate settings
• Test precedence/rollback
KEY DISTINCTION
Map each requirement—VPN profile, CA, app compliance, FortiClient telemetry—to an accountable system
142 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: [CORE LECTURE] Stable ID: D4-B13-S142
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: EMS is FortiClient-centric: profiles, telemetry and network-access integrations; Intune manages broader device/app/compliance configuration in Microsoft ecosystems; They can coexist: Intune enrolls/configures device; EMS manages FortiClient-specific posture/profile; Replacement is use-case specific; never claim blanket feature equivalence
Instructor demonstration / expected result: Instructor confirms current product licensing and integration documentation.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “EMS and Intune overlap only in selected endpoint-management tasks” before showing the answer.

## Slide 139
139
Client troubleshooting correlates endpoint, EMS and FortiGate state
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
Endpoint: record FortiClient version/profile, route table and DNS EMS: confirm endpoint registration and assigned profile (if deployed) FortiGate: correlate auth/VPN/traffic session logs Use exact product documentation for log locations
READ THE OUTPUT
• Endpoint network state and routes/DNS
• FortiClient event/VPN logs
• EMS profile/telemetry status if used
• FortiGate authentication, VPN, policy and session logs
Safe operation
A client-side “connected” icon does not prove protected application reachability
143 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: [CORE LECTURE] Stable ID: D4-B13-S143
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Endpoint network state and routes/DNS; FortiClient event/VPN logs; EMS profile/telemetry status if used; FortiGate authentication, VPN, policy and session logs
Instructor demonstration / expected result: Use one timestamped five-tuple across endpoint, EMS and FortiGate state/output.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “Client troubleshooting correlates four command or log fields” before showing the answer.

## Slide 140
140
Managed VPN profile
140
01
Endpoint registers to EMS
02
EMS assigns profile
03
FortiClient applies gateway/auth
04
FortiGate authenticates
05
Session reaches application
EXPECTED RESULT
The endpoint shows its assigned FortiClient profile and EMS connection; FortiGate logs the resulting access session.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D4-B13-S144
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Requirement: consistent VPN gateway and certificate trust; Choose EMS, Intune or coexistence based on ownership and supported controls; Deploy to a pilot group; Validate client and FortiGate state/output; Define rollback and help-desk signals
Instructor demonstration / expected result: No tenant, credential or working deployment is implied.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “Managed VPN profile decision” before showing the answer.

## Slide 141
141
Common mistakes—and how to correct them
141
MISTAKE
CORRECTION — AND WHY IT HELPS
Assume installed FortiClient is EMS-managed
Check the EMS connection and assigned profile; installation alone is not centralized management.
Treat EMS and Intune as equivalent
Assign each requirement to the product that supports it; they overlap only for selected endpoint tasks.
Troubleshoot only FortiGate
Correlate client logs, endpoint routes/DNS, EMS profile and FortiGate session state.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D4-B13-S145
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 142
142
Troubleshooting workflow: narrow the failed decision
01
Confirm endpoint OS/client/version/license
02
Verify assigned profile and gateway reachability
03
Check authentication/certificate trust
04
Inspect client and EMS logs
05
Correlate FortiGate VPN, policy and session state
What to observe
• Check authentication/certificate trust
• Inspect client and EMS logs
• Correlate FortiGate VPN, policy and session state
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
146 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: [CORE LECTURE] Stable ID: D4-B13-S146
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Confirm endpoint OS/client/version/license; Verify assigned profile and gateway reachability; Check authentication/certificate trust; Inspect client and EMS logs; Correlate FortiGate VPN/policy/session state/output
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 143
143
Practical handoff: predict, observe, explain
• Prerequisite: Managed test endpoint for live demo
• Prerequisite: FortiClient/EMS versions and licensing declared
• Goal: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The endpoint shows its assigned FortiClient profile and EMS connection; FortiGate logs the resulting access session.
147 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: [CORE LECTURE] Stable ID: D4-B13-S147
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Managed test endpoint for live demo; Prerequisite: FortiClient/EMS versions and licensing declared; Goal: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 144
144
Knowledge check — explain the result
QUESTION 1
• When can EMS and Intune coexist?
QUESTION 2
• What does FortiClient “connected” fail to prove?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
148 • DAY 4 • BLOCK 13 • FortiClient & EMS
Notes: [CORE LECTURE] Stable ID: D4-B13-S148
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: When can EMS and Intune coexist?; What does FortiClient “connected” fail to prove?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Assuming every FortiClient installation is EMS-managed; Claiming EMS and Intune are interchangeable; Troubleshooting only on the gateway
Practical handoff: Compare two endpoint-management designs and inspect one VPN profile. Live EMS activity requires a supplied tenant, license and supported versions; otherwise use screenshots/documentation supplied by the instructor.
Official reference for instructor preparation: Official FortiClient and FortiClient EMS Administration Guides for the deployed FortiClient/EMS release; FortiGate/FortiOS 7.6.7 Administration Guide: Remote access and endpoint/ZTNA integration. Confirm licensing and support matrix.
Knowledge check answer key:
Q: When can EMS and Intune coexist?
A: When ownership is explicit—for example, Intune manages broad device configuration while EMS manages FortiClient-specific profiles and telemetry.
Q: What does FortiClient “connected” fail to prove?
A: That routes, DNS, FortiGate policy and the target application path are working end to end.

## Slide 145
DAY 4 • 10:30–12:00
FortiGate High Availability Fundamentals
Advanced • Day 2 of 2
LEARNING OBJECTIVES
• Explain FGCP prerequisites, heartbeat, election and synchronization
• Trace Active-Passive failover and session impact
• Separate appliance HA demonstration from cloud HA designs
PREREQUISITES + PRACTICE RESERVE
• Azure FGVM: FGCP only with a provisioned HA pair
• Match heartbeat and configuration prerequisites
• Physical-appliance HA: theory or separate demo
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
149
Notes: [CORE LECTURE] Stable ID: D4-B14-S149
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Explain FGCP prerequisites, heartbeat, election and synchronization; Trace Active-Passive failover and session impact; Separate appliance HA demonstration from cloud HA designs
Instructor demonstration / expected result: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “FortiGate High Availability Fundamentals” before showing the answer.
Azure lab emphasis: use an Azure-supported HA design only if the required pair and Azure networking components are provisioned. The heartbeat, election and session-synchronization explanation also covers physical appliances, but cable/link demonstrations require separate hardware.

## Slide 146
146
Active/passive HA synchronizes state before a controlled failover
Physical appliance concepts shown; Azure deployment mechanics require the Fortinet Azure design
146
PRIMARY
forwarding traffic
SECONDARY
standby / synchronized
HEARTBEAT
health • election config/session sync
before
UPSTREAM / DOWNSTREAM
traffic via primary
after
UPSTREAM / DOWNSTREAM
traffic via new primary
FAILOVER TRIGGER
monitored failure → election → role change → adjacent-network convergence
LESSON
Session continuity depends on synchronized eligible state; role change alone does not guarantee zero application interruption.
Notes: Expected result: before failover, members are synchronized and one unit is primary; after the approved trigger, the secondary becomes primary and eligible sessions recover as designed. Azure HA requires the current Fortinet Azure architecture. Source: FortiOS 7.6.7 Administration Guide — FGCP HA, session pickup and failover; FortiGate-VM for Azure HA guide.

## Slide 147
147
Election selects the current primary using ordered criteria
• Priority, override behavior, monitored interfaces and uptime/state influence election according to configuration
• Preemption/override choices affect whether the preferred unit reclaims primary
• A stable cluster is more important than repeatedly forcing preferred ownership
• Document expected primary and the exact trigger for change
ILLUSTRATIVE SCENARIO
Predict election before disconnecting anything
EXPECTED RESULT
Show member state and election-relevant values on both units.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
151 • DAY 4 • BLOCK 14 • High Availability
Notes: [CORE LECTURE] Stable ID: D4-B14-S151
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Priority, override behavior, monitored interfaces and uptime/state influence election according to configuration; Preemption/override choices affect whether the preferred unit reclaims primary; A stable cluster is more important than repeatedly forcing preferred ownership; Document expected primary and the exact trigger for change
Instructor demonstration / expected result: Show member state and election-relevant values on both units.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Election selects the current primary using ordered criteria” before showing the answer.

## Slide 148
148
Synchronization preserves cluster configuration and selected runtime state
• Most configuration is synchronized; some member-specific settings remain local
• Session pickup/session synchronization must be configured and supported for desired protocols/features
• Security engine and dynamic state behavior may vary during failover
• Checksum mismatch requires investigation before relying on redundancy
ILLUSTRATIVE SCENARIO
Configuration sync does not guarantee every session survives
EXPECTED RESULT
Compare cluster checksums and one test session before/after controlled failover.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
152 • DAY 4 • BLOCK 14 • High Availability
Notes: [CORE LECTURE] Stable ID: D4-B14-S152
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Most configuration is synchronized; some member-specific settings remain local; Session pickup/session synchronization must be configured and supported for desired protocols/features; Security engine and dynamic state behavior may vary during failover; Checksum mismatch requires investigation before relying on redundancy
Instructor demonstration / expected result: Compare cluster checksums and one test session before/after controlled failover.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Synchronization preserves cluster configuration and selected runtime state” before showing the answer.

## Slide 149
149
Monitored failures trigger role change only when configured
01
Failure detected
02
Heartbeat/election
03
New primary
04
L2/L3 convergence
05
Session recovery
What to observe
• Link-monitor/path health mechanisms may be needed beyond physical interface state
• Failover time includes detection, election, forwarding convergence and upstream learning
• Flapping monitored links can cause repeated disruption
INSTRUCTOR DEMONSTRATION
Declare the trigger, expected timer and convergence checkpoints before the test.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
153 • DAY 4 • BLOCK 14 • High Availability
Notes: [CORE LECTURE] Stable ID: D4-B14-S153
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Heartbeat loss, monitored interface failure and device failure are distinct events; Link-monitor/path health mechanisms may be needed beyond physical interface state; Failover time includes detection, election, forwarding convergence and upstream learning; Flapping monitored links can cause repeated disruption
Instructor demonstration / expected result: Declare expected trigger, timer and convergence state/output before test.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Monitored failures trigger role change only when configured” before showing the answer.

## Slide 150
150
Session behavior depends on synchronization and traffic type
• Synced eligible sessions can continue with limited interruption
• Unsynchronized or unsupported sessions must be re-established
• NAT, IPsec, routing and authentication state have specific HA considerations
• Measure user impact, not only role change
ILLUSTRATIVE SCENARIO
A long-lived TCP stream and a new connection reveal different effects
EXPECTED RESULT
Track session on both members and packet loss during failover.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
154 • DAY 4 • BLOCK 14 • High Availability
Notes: [CORE LECTURE] Stable ID: D4-B14-S154
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Synced eligible sessions can continue with limited interruption; Unsynchronized or unsupported sessions must be re-established; NAT, IPsec, routing and authentication state have specific HA considerations; Measure user impact, not only role change
Instructor demonstration / expected result: Track session on both members and packet loss during failover.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Session behavior depends on synchronization and traffic type” before showing the answer.

## Slide 151
151
Common HA faults cluster around prerequisites and Layer 2
• Firmware/model mismatch prevents expected formation
• Heartbeat VLAN/switch behavior can introduce loss or loops
• Duplicate management/IP design can make a healthy cluster appear unreachable
• Upstream/downstream MAC/ARP convergence can dominate outage time
ILLUSTRATIVE SCENARIO
Separate cluster health from surrounding-network convergence
EXPECTED RESULT
Capture heartbeat/role events plus adjacent switch/router state.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
155 • DAY 4 • BLOCK 14 • High Availability
Notes: [CORE LECTURE] Stable ID: D4-B14-S155
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Firmware/model mismatch prevents expected formation; Heartbeat VLAN/switch behavior can introduce loss or loops; Duplicate management/IP design can make a healthy cluster appear unreachable; Upstream/downstream MAC/ARP convergence can dominate outage time
Instructor demonstration / expected result: Capture heartbeat/role events plus adjacent switch/router state/output.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Common HA faults cluster around prerequisites and Layer 2” before showing the answer.

## Slide 152
152
Cloud HA is a provider-integrated design, not an appliance clone
• Cloud instances lack physical heartbeat/transparent L2 assumptions in many designs
• Routing, load balancers, APIs and provider failover mechanisms may be required
• Licensing and bootstrap/state synchronization depend on marketplace/deployment model
• Use the exact Fortinet cloud deployment guide for the platform
ILLUSTRATIVE SCENARIO
A physical-appliance cable-pull does not validate Azure FGVM failover
EXPECTED RESULT
Keep cloud HA conceptual unless the cloud architecture and permissions are supplied.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
156 • DAY 4 • BLOCK 14 • High Availability
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B14-S156
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Cloud instances lack physical heartbeat/transparent L2 assumptions in many designs; Routing, load balancers, APIs and provider failover mechanisms may be required; Licensing and bootstrap/state synchronization depend on marketplace/deployment model; Use the exact Fortinet cloud deployment guide for the platform
Instructor demonstration / expected result: Keep cloud HA conceptual unless the cloud architecture and permissions are supplied.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Cloud HA is a provider-integrated design, not an appliance clone” before showing the answer.

## Slide 153
153
Controlled HA failover
153
01
Confirm sync/primary
02
Start eligible test session
03
Trigger monitored failure
04
Secondary becomes primary
05
Measure application recovery
EXPECTED RESULT
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D4-B14-S157
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Record primary/secondary and sync state; Generate an eligible test session; Trigger one approved monitored failure; Measure role, packet loss and session result; Restore and confirm stable resynchronization
Instructor demonstration / expected result: Success includes expected service behavior and clean recovery.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Controlled Active-Passive failover” before showing the answer.

## Slide 154
154
Common mistakes—and how to correct them
154
MISTAKE
CORRECTION — AND WHY IT HELPS
Build HA from mismatched members
Match supported model/build/mode and HA settings before joining; compatibility is prerequisite.
Assume config sync means every session survives
Enable/verify supported session pickup and test the traffic type; runtime state varies.
Use appliance failover assumptions in Azure
Follow the Fortinet Azure HA architecture; cloud routing/load-balancing changes the mechanism.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D4-B14-S158
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 155
155
Troubleshooting workflow: narrow the failed decision
01
Check member compatibility and heartbeat
02
Confirm role/election and sync checksums
03
Inspect monitored failure event
04
Separate role change from network convergence
05
Validate session/application recovery and resync
What to observe
• Inspect monitored failure event
• Separate role change from network convergence
• Validate session/application recovery and resync
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
159 • DAY 4 • BLOCK 14 • High Availability
Notes: [CORE LECTURE] Stable ID: D4-B14-S159
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check member compatibility and heartbeat; Confirm role/election and sync checksums; Inspect monitored failure event; Separate role change from network convergence; Validate session/application recovery and resync
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 156
156
Practical handoff: predict, observe, explain
• Prerequisite: Two compatible appliances or instructor demonstration
• Prerequisite: Dedicated heartbeat links and matching configuration prerequisites
• Goal: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The secondary is synchronized before failover; after failover, the new primary forwards eligible test sessions.
160 • DAY 4 • BLOCK 14 • High Availability
Notes: [CORE LECTURE] Stable ID: D4-B14-S160
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Two compatible appliances or instructor demonstration; Prerequisite: Dedicated heartbeat links and matching configuration prerequisites; Goal: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 157
157
Knowledge check — explain the result
QUESTION 1
• What is the heartbeat used for?
QUESTION 2
• Why can traffic remain interrupted after the secondary becomes primary?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
161 • DAY 4 • BLOCK 14 • High Availability
Notes: [CORE LECTURE] Stable ID: D4-B14-S161
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What is the heartbeat used for?; Why can traffic remain interrupted after the secondary becomes primary?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Building HA with mismatched firmware or modes; Assuming configuration sync means all sessions survive; Testing cloud HA with appliance assumptions
Practical handoff: Instructor demonstrates a controlled failover on a dedicated pair; learners predict election and session outcome. If no pair exists, analyze an event timeline and configuration checklist.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: FGCP HA; Primary election; Session pickup; HA troubleshooting. Model-specific and cloud-provider deployment guides required.
Knowledge check answer key:
Q: What is the heartbeat used for?
A: Member health, election and synchronization/control exchange between cluster units.
Q: Why can traffic remain interrupted after the secondary becomes primary?
A: Adjacent network convergence, unsynchronized sessions or dependent routing/security state may still be recovering.

## Slide 158
DAY 4 • 13:00–14:30
Fortinet SD-WAN & Design Considerations
Advanced • Day 2 of 2
LEARNING OBJECTIVES
• Build SD-WAN from members, zones, health checks and rules
• Predict SLA-based application path selection and failover
• Place FortiAnalyzer, FortiManager and security services without inventing entitlements
PREREQUISITES + PRACTICE RESERVE
• Two WAN paths or instructor simulation
• Defined performance targets and test applications
• Licensing/subscription details confirmed by instructor
Teach ~60 min • reserve ~30 min for guided activity, discussion and debrief
162
Notes: [CORE LECTURE] Stable ID: D4-B15-S162
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Build SD-WAN from members, zones, health checks and rules; Predict SLA-based application path selection and failover; Place FortiAnalyzer, FortiManager and security services without inventing entitlements
Instructor demonstration / expected result: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “Fortinet SD-WAN & Design Considerations” before showing the answer.

## Slide 159
159
SD-WAN selects a member from rule intent and measured SLA
Illustrative voice rule: latency <25 ms, jitter <10 ms, loss <1%
159
VOICE SESSION
10.10.10.25 → SaaS
SD-WAN RULE
voice → best-quality member
BEFORE DEGRADATION
ISP-A 18 ms / 4 ms / 0.2% ✓ ISP-B 35 ms / 8 ms / 0.4% ✕ latency
select A
ISP-A
selected egress
AFTER ISP-A DEGRADES
ISP-A 42 ms / 15 ms / 2.0% ✕ ISP-B 20 ms / 6 ms / 0.3% ✓
new → B
ISP-B
selected for new session
LESSON
Link-up is insufficient: the rule considers measured SLA, and existing sessions may behave differently from new sessions.
Notes: Illustrative values only. Expected result: before degradation, the new voice session uses ISP-A; after ISP-A fails the stated SLA, a new session uses ISP-B. Confirm actual egress in SD-WAN service state and session output. Source: FortiOS 7.6.7 Administration Guide — SD-WAN performance SLA and rules.

## Slide 160
160
Health checks must measure the service you care about
• Target should represent the path/service dependency, not only the next-hop router
• Latency, jitter and packet loss thresholds define SLA state as supported
• Probe interval/fail/recovery settings trade responsiveness against instability
• Multiple targets can reduce false positives but complicate interpretation
ILLUSTRATIVE SCENARIO
An ISP gateway can respond while SaaS path is impaired
EXPECTED RESULT
Compare raw measurements, SLA state and application experience.
Expected observation
The SD-WAN rule selects the member that meets the stated SLA, and the session egress matches that member.
164 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [CORE LECTURE] Stable ID: D4-B15-S164
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Target should represent the path/service dependency, not only the next-hop router; Latency, jitter and packet loss thresholds define SLA state as supported; Probe interval/fail/recovery settings trade responsiveness against instability; Multiple targets can reduce false positives but complicate interpretation
Instructor demonstration / expected result: Compare raw measurements, SLA state and application experience.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “Health checks must measure the service you care about” before showing the answer.

## Slide 161
161
SLA criteria turn measurements into path eligibility
ISP-A
• 35 ms latency
• 0.5% loss
• SLA: fail for voice
ISP-B
• 18 ms latency
• 0.1% loss
• SLA: pass
RESULT
• Voice → ISP-B
• New session path
• Verify actual egress
KEY DISTINCTION
ISP-A latency 35 ms/loss 0.5%; ISP-B 18 ms/loss 0.1%—voice rule chooses B if thresholds demand it
165 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [CORE LECTURE] Stable ID: D4-B15-S165
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: A member can be up but out of SLA; Rules can prefer, balance or choose based on quality/cost strategies as supported; Hysteresis/recovery behavior prevents oscillation; Existing sessions may remain pinned while new sessions choose differently
Instructor demonstration / expected result: Record rule, threshold, member SLA state and selected session interface.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “SLA criteria turn measurements into path eligibility” before showing the answer.

## Slide 162
162
Application steering depends on identification timing
• Rules can use address/service/application constructs depending on design
• Application identity may be learned after initial packets
• Fallback/default rule must be intentional
• Security profiles and SSL visibility affect application identification
ILLUSTRATIVE SCENARIO
A first packet can use a provisional path before application is identified
EXPECTED RESULT
Use session details and logs to confirm the final matched rule/member.
Expected observation
The SD-WAN rule selects the member that meets the stated SLA, and the session egress matches that member.
166 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [CORE LECTURE] Stable ID: D4-B15-S166
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Rules can use address/service/application constructs depending on design; Application identity may be learned after initial packets; Fallback/default rule must be intentional; Security profiles and SSL visibility affect application identification
Instructor demonstration / expected result: Use session details and logs to confirm the final matched rule/member.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “Application steering depends on identification timing” before showing the answer.

## Slide 163
163
Failover is detection plus session/application recovery
01
SLA breach
02
Member ineligible
03
Rule recalculates
04
New egress
05
Application recovery
What to observe
• Rule removes or de-prioritizes member
• New sessions select another eligible path
• Existing session continuity depends on NAT, remote state and design
INSTRUCTOR DEMONSTRATION
Test new and long-lived flows separately.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
167 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [CORE LECTURE] Stable ID: D4-B15-S167
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Probe detects threshold breach; Rule removes or de-prioritizes member; New sessions select another eligible path; Existing session continuity depends on NAT, remote state and design
Instructor demonstration / expected result: Test new and long-lived flows separately.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “Failover is detection plus session/application recovery” before showing the answer.

## Slide 164
164
Verify the actual egress path, not the intended diagram
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
diagnose sys sdwan health-check diagnose sys sdwan service get router info routing-table details <destination> diagnose sys session filter dst <destination> diagnose sys session list
READ THE OUTPUT
• Check member/health-check state
• Confirm rule match and priority/strategy
• Inspect route/policy/session chosen interface
• Capture packets at candidate egresses
Safe operation
Use unique test tuple and timestamp to avoid stale session confusion
168 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [CORE LECTURE] Stable ID: D4-B15-S168
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check member/health-check state; Confirm rule match and priority/strategy; Inspect route/policy/session chosen interface; Capture packets at candidate egresses; Correlate traffic logs with SLA events
Instructor demonstration / expected result: A clean proof names rule, member, NAT address and return packets.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “Verify the actual egress path, not the intended diagram” before showing the answer.

## Slide 165
165
FortiAnalyzer and FortiManager solve different operational problems
FORTIOS
• Local config/GUI/CLI
• Routing, policy, SD-WAN
• Local logs within capacity
FORTIANALYZER
• Central logs/analytics
• Reports/incidents
• Retention architecture
FORTIMANAGER
• Central config/policy
• Templates/ADOM workflow
• Controlled deployment
KEY DISTINCTION
Use product roles, not invented bundle claims
169 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [CORE LECTURE] Stable ID: D4-B15-S169
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: FortiAnalyzer centralizes logs, analytics and reporting workflows; FortiManager centralizes configuration, policy packages and controlled deployment; FortiOS includes local management, routing, SD-WAN and security capabilities subject to platform/build; Security services and cloud subscriptions add update/intelligence/management value; exact entitlement must be verified
Instructor demonstration / expected result: Instructor reviews current order/contract and Fortinet product documentation.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “FortiAnalyzer and FortiManager solve different operational problems” before showing the answer.

## Slide 166
166
Licensing boundaries are a validation task, not a memory test
• Base FortiOS feature availability varies by model/release
• FortiGuard services require relevant subscriptions and connectivity
• Manager/analyzer cloud/on-prem offerings have separate sizing and licensing
• Avoid promising retention, device counts or service entitlement without current documentation
ILLUSTRATIVE SCENARIO
Mark every design dependency as built-in, subscription, external platform or instructor-confirmed
EXPECTED RESULT
Create a validation checklist rather than a price/entitlement claim.
Expected observation
The SD-WAN rule selects the member that meets the stated SLA, and the session egress matches that member.
170 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B15-S170
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Base FortiOS feature availability varies by model/release; FortiGuard services require relevant subscriptions and connectivity; Manager/analyzer cloud/on-prem offerings have separate sizing and licensing; Avoid promising retention, device counts or service entitlement without current documentation
Instructor demonstration / expected result: Create a validation checklist rather than a price/entitlement claim.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “Licensing boundaries are a validation task, not a memory test” before showing the answer.

## Slide 167
167
Confirm SD-WAN selection in SLA state, rule match and session egress
Before/after scenario continued
167
1 HEALTH CHECK
Probe the service-relevant target. Record latency, jitter and loss.
2 SLA STATE
ISP-A: out of SLA ISP-B: in SLA
3 RULE MATCH
Voice rule removes A and chooses B
4 SESSION
Egress: ISP-B NAT: ISP-B address
BEFORE
voice session → ISP-A
AFTER
new voice session → ISP-B
Existing-session behavior depends on application/NAT/remote state; test long-lived and new flows separately.
LESSON
Do not stop at the intent diagram—confirm the matched SD-WAN rule and the actual session egress member.
Notes: Expected result: ISP-A reports out-of-SLA values, the voice rule selects ISP-B, and a new session shows ISP-B as egress with the expected source NAT. Source: FortiOS 7.6.7 Administration Guide — SD-WAN diagnostics and session verification.

## Slide 168
168
Common mistakes—and how to correct them
168
MISTAKE
CORRECTION — AND WHY IT HELPS
Probe only the ISP gateway
Probe a service-relevant target; a local gateway can stay up while the application path fails.
Expect an existing session to move seamlessly
Test both new and long-lived flows; NAT and remote state can require reconnection.
Assume managers are bundled
Check current licensing and architecture; FortiManager and FortiAnalyzer have distinct roles.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D4-B15-S172
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 169
169
Troubleshooting workflow: narrow the failed decision
01
Check member/link and probe reachability
02
Review SLA raw values and threshold state
03
Confirm matched SD-WAN rule
04
Inspect route, policy, session and NAT egress
05
Capture both links; test new session and recovery
What to observe
• Confirm matched SD-WAN rule
• Inspect route, policy, session and NAT egress
• Capture both links; test new session and recovery
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
173 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [CORE LECTURE] Stable ID: D4-B15-S173
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check member/link and probe reachability; Review SLA raw values and threshold state; Confirm matched SD-WAN rule; Inspect route, policy, session and NAT egress; Capture both links; test new session and recovery
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 170
170
Practical handoff: predict, observe, explain
• Prerequisite: Two WAN paths or instructor simulation
• Prerequisite: Defined performance targets and test applications
• Goal: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The SD-WAN rule selects the member that meets the stated SLA, and the session egress matches that member.
174 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [CORE LECTURE] Stable ID: D4-B15-S174
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Two WAN paths or instructor simulation; Prerequisite: Defined performance targets and test applications; Goal: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 171
171
Knowledge check — explain the result
QUESTION 1
• What is the difference between a member being up and in SLA?
QUESTION 2
• What proves the selected path?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
175 • DAY 4 • BLOCK 15 • SD-WAN & Design
Notes: [CORE LECTURE] Stable ID: D4-B15-S175
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What is the difference between a member being up and in SLA?; What proves the selected path?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Probing only the local gateway; Expecting an existing session to move seamlessly; Assuming FortiAnalyzer or FortiManager is included/licensed
Practical handoff: Create or analyze one health check and two rules, predict path under normal/degraded conditions, then verify selected member. If two links are unavailable, use an instructor-provided state table.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: SD-WAN members/zones; Performance SLA; SD-WAN rules; Diagnostics. Official FortiManager, FortiAnalyzer and FortiGuard service documentation for current licensing.
Knowledge check answer key:
Q: What is the difference between a member being up and in SLA?
A: Up indicates basic availability; in-SLA means measured criteria meet the rule’s thresholds.
Q: What proves the selected path?
A: Rule/service state plus session egress/NAT and packet or traffic-log state/output on the chosen member.

## Slide 172
DAY 4 • 14:30–16:00
Performance Optimization, Advanced Troubleshooting & Capstone
Advanced • Day 2 of 2
LEARNING OBJECTIVES
• Relate session scale, offload, inspection and resource use
• Troubleshoot CPU, memory and Conserve Mode from measured state
• Complete an integrated policy/routing/VPN/SD-WAN capstone
PREREQUISITES + PRACTICE RESERVE
• Read-only performance access
• Baseline or instructor-provided metrics
• Safe fault injection in an isolated lab only
Teach ~58 min • reserve ~32 min for guided activity, discussion and debrief
176
Notes: [CORE LECTURE] Stable ID: D4-B16-S176
Approximate timing: 3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Relate session scale, offload, inspection and resource use; Troubleshoot CPU, memory and Conserve Mode from state/output; Complete an integrated policy/routing/VPN/SD-WAN capstone
Instructor demonstration / expected result: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Performance Optimization, Advanced Troubleshooting & Capstone” before showing the answer.

## Slide 173
173
Session-table sizing begins with traffic behavior
• Concurrent sessions differ from new sessions per second
• Long-lived, idle and half-open sessions consume different operational attention
• NAT, inspection and logging add state/resources
• Use model datasheet and measured baseline; never copy a generic maximum into design
ILLUSTRATIVE SCENARIO
A branch with many short web sessions stresses setup rate differently from persistent VPN flows
EXPECTED RESULT
Compare session count/rate, timeout distribution and peak trend.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
177 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S177
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Concurrent sessions differ from new sessions per second; Long-lived, idle and half-open sessions consume different operational attention; NAT, inspection and logging add state/resources; Use model datasheet and measured baseline; never copy a generic maximum into design
Instructor demonstration / expected result: Compare session count/rate, timeout distribution and peak trend.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Session-table sizing begins with traffic behavior” before showing the answer.

## Slide 174
174
Hardware offload validation must be platform specific
• Check whether the session and enabled features are eligible
• First packets and exception traffic can remain on CPU
• Azure FGVM performance uses VM/vNIC/cloud acceleration—not a physical NP/CP ASIC datapath
• A no-offload flag requires investigation; it is not automatically a misconfiguration
ILLUSTRATIVE SCENARIO
Compare an eligible simple flow and an inspected/tunneled flow on a declared appliance
EXPECTED RESULT
Use model-specific documentation and session diagnostics.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
178 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S178
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Check whether the session and enabled features are eligible; First packets and exception traffic can remain on CPU; VM acceleration uses hypervisor/cloud mechanisms rather than appliance NP/CP; A no-offload flag is state/output to investigate, not automatic misconfiguration
Instructor demonstration / expected result: Use model-specific documentation and session diagnostics.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Hardware offload validation must be platform specific” before showing the answer.

## Slide 175
175
CPU troubleshooting starts with time and workload correlation
ILLUSTRATIVE CLI — validate on FortiOS 7.6.7 / Azure FortiGate-VM
get system performance status diagnose sys top 1 20 diagnose sys session stat # Stop interactive top with the documented key sequence
READ THE OUTPUT
• Identify whether load is sustained or bursty
• Locate responsible processes/cores and traffic changes
• Correlate policy/profile, routing events, logging and session setup
• Record process, session and memory state before restarting or changing load
Safe operation
High CPU during an IPS update differs from sustained packet-processing saturation
179 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S179
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Identify whether load is sustained or bursty; Locate responsible processes/cores and traffic changes; Correlate policy/profile, routing events, logging and session setup; Avoid restarting before preserving state/output and understanding impact
Instructor demonstration / expected result: Capture performance status/top samples and event timeline.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “CPU troubleshooting starts with time and workload correlation” before showing the answer.

## Slide 176
176
Memory management requires trend, consumers and thresholds
• Track used memory, proxy buffers, sessions and process growth
• Conserve Mode is triggered by system memory thresholds and protects stability
• Entry/exit thresholds and behavior must be confirmed for exact build/model
• A reboot removes transient state and may only postpone recurrence
ILLUSTRATIVE SCENARIO
Collect event log, process and session state before mitigation
EXPECTED RESULT
Use release-specific Conserve Mode documentation and support guidance.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
180 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S180
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Track used memory, proxy buffers, sessions and process growth; Conserve Mode is triggered by system memory thresholds and protects stability; Entry/exit thresholds and behavior must be confirmed for exact build/model; A reboot removes state/output and may only postpone recurrence
Instructor demonstration / expected result: Use release-specific Conserve Mode documentation and support guidance.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Memory management requires trend, consumers and thresholds” before showing the answer.

## Slide 177
177
Conserve Mode changes the troubleshooting priority
01
Threshold crossed
02
Protective behavior
03
Identify consumer
04
Scoped mitigation
05
Stable recovery
What to observe
• Identify whether sessions, proxy inspection or a process dominates
• Apply scoped mitigation and monitor exit/re-entry
• Escalate with timestamps, process samples and memory trends when a defect is suspected
INSTRUCTOR DEMONSTRATION
Resolution includes stable memory below recovery threshold and no recurring event.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
181 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S181
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: First protect stability and reduce unsafe load; Identify whether sessions, proxy inspection or a process dominates; Apply scoped mitigation and monitor exit/re-entry; Escalate with state/output when leak/defect is suspected
Instructor demonstration / expected result: Resolution includes stable memory below recovery threshold and no recurring event.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Conserve Mode changes the troubleshooting priority” before showing the answer.

## Slide 178
178
SSL inspection has measurable compute and compatibility cost
• Deep inspection adds TLS termination, certificate generation and content scanning
• Cipher suites, key sizes, session resumption and traffic mix affect cost
• Certificate inspection has lower visibility and generally lower processing cost
• Capacity planning must use representative encrypted traffic and enabled profiles
ILLUSTRATIVE SCENARIO
Measure throughput/latency/CPU with and without the intended profile in a controlled test
EXPECTED RESULT
Do not extrapolate one lab VM result to appliance capacity.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
182 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S182
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Deep inspection adds TLS termination, certificate generation and content scanning; Cipher suites, key sizes, session resumption and traffic mix affect cost; Certificate inspection has lower visibility and generally lower processing cost; Capacity planning must use representative encrypted traffic and enabled profiles
Instructor demonstration / expected result: Do not extrapolate one lab VM result to appliance capacity.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “SSL inspection has measurable compute and compatibility cost” before showing the answer.

## Slide 179
179
Security profiles consume resources according to traffic mix
• AV, IPS, Web and App Control engage different engines and update packages
• Encrypted traffic requires sufficient inspection visibility before content scanning
• Logging volume and disk/remote transport can become bottlenecks
• Profile tuning should preserve security requirements and use representative measurements
ILLUSTRATIVE SCENARIO
Optimize exclusions/signatures only with risk owner approval and rollback
EXPECTED RESULT
Compare security events, CPU/memory and user impact.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
183 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S183
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: AV, IPS, Web and App Control engage different engines and update packages; Encrypted traffic requires sufficient inspection visibility before content scanning; Logging volume and disk/remote transport can become bottlenecks; Profile tuning should preserve security requirements and use measured state/output
Instructor demonstration / expected result: Compare security events, CPU/memory and user impact.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Security profiles consume resources according to traffic mix” before showing the answer.

## Slide 180
180
A layered workflow prevents random configuration changes
01
Symptom
02
Route
03
Policy/NAT
04
Overlay/SD-WAN
05
Profiles
06
Resources
What to observe
• Check policy/NAT/session
• Check VPN/SD-WAN/security-profile layers as applicable
• Check resource pressure and recent changes last/throughout
INSTRUCTOR DEMONSTRATION
Stop, reset and document debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
184 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S184
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Start with symptom and exact five-tuple/time; Check physical/interface and routing; Check policy/NAT/session; Check VPN/SD-WAN/security-profile layers as applicable; Check resource pressure and recent changes last/throughout
Instructor demonstration / expected result: Stop, reset and document debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “An state/output ladder prevents random configuration changes” before showing the answer.

## Slide 181
181
Capstone topology uses one consistent illustrative design
HQ CLIENT
HQ FGT
WAN / VPN / SD-WAN
BRANCH FGT
BRANCH SERVER
Instructor replaces interface names and chooses only faults supported by the lab
• Client 10.10.10.25 in HQ user LAN
• Branch server 10.20.10.50 reached through IPsec/ADVPN or SD-WAN member
• HQ DMZ server 10.10.20.10 published by VIP where applicable
• ISP-A 203.0.113.0/30 and ISP-B 198.51.100.0/30 are documentation ranges
Azure FGVM is confirmed; VNet, subnet, NSG, UDR, load-balancer, credentials and student ranges remain unspecified.
185 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S185
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Client 10.10.10.25 in HQ user LAN; Branch server 10.20.10.50 reached through IPsec/ADVPN or SD-WAN member; HQ DMZ server 10.10.20.10 published by VIP where applicable; ISP-A 203.0.113.0/30 and ISP-B 198.51.100.0/30 are documentation ranges
Instructor demonstration / expected result: No Azure design, credentials or student ranges are implied.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Capstone topology uses one consistent illustrative design” before showing the answer.

## Slide 182
182
Capstone symptom: application is intermittently unreachable
• User reports HTTPS timeout to branch application
• DNS answer is correct and must be recorded
• Traffic may fail at policy, overlay route, SD-WAN rule or resource pressure
• Teams must avoid changing more than one variable at a time
ILLUSTRATIVE SCENARIO
Timebox triage; assign a diagnostic owner and change recorder
EXPECTED RESULT
Success is identifying the failed decision from actual device state—not fastest guessing.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
186 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S186
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: User reports HTTPS timeout to branch application; DNS answer is correct and must be recorded; Traffic may fail at policy, overlay route, SD-WAN rule or resource pressure; Teams must avoid changing more than one variable at a time
Instructor demonstration / expected result: Success is localization with state/output, not fastest guessing.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Capstone symptom: application is intermittently unreachable” before showing the answer.

## Slide 183
183
Capstone fault set is chosen from achievable prerequisites
• Fault A: disabled/narrowed lab policy or wrong service object
• Fault B: missing/more-specific route or mismatched VPN selector
• Fault C: SD-WAN SLA target/rule steers to failed lab path
• Optional observation: elevated memory metric from instructor-provided snapshot—no synthetic Conserve Mode on shared equipment
ILLUSTRATIVE SCENARIO
Inject only one or two faults in isolated lab; state them in instructor notes
EXPECTED RESULT
Never claim hardware/EMS/HA faults are live if resources are absent.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
187 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S187
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Fault A: disabled/narrowed lab policy or wrong service object; Fault B: missing/more-specific route or mismatched VPN selector; Fault C: SD-WAN SLA target/rule steers to failed lab path; Optional observation: elevated memory metric from instructor-provided snapshot—no synthetic Conserve Mode on shared equipment
Instructor demonstration / expected result: Never claim hardware/EMS/HA faults are live if resources are absent.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Capstone fault set is chosen from achievable prerequisites” before showing the answer.

## Slide 184
184
Capstone record connects every relevant layer
• Exact test tuple, timestamp and expected path
• Route/PBR/SD-WAN decision
• Matched policy, NAT and session state
• VPN SA/selectors/counters when used
• Relevant packet/log output and CPU/memory status
ILLUSTRATIVE SCENARIO
Screenshots alone need labels and context; CLI output must be captured from the actual lab
EXPECTED RESULT
Teams submit a concise before/after state table.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
188 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S188
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Exact test tuple, timestamp and expected path; Route/PBR/SD-WAN decision; Matched policy, NAT and session state; VPN SA/selectors/counters when used; Packet/log state/output and CPU/memory status
Instructor demonstration / expected result: Teams submit a concise before/after state/output table.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Capstone troubleshooting record connects every layer” before showing the answer.

## Slide 185
185
Capstone workflow: localize before remediation
• Reproduce once and freeze the test definition
• Predict path using route, policy and overlay state
• Collect minimally invasive diagnostics
• Name the failed decision and proposed change
• Apply approved change; retest; restore injected fault baseline
ILLUSTRATIVE SCENARIO
Use fresh five-tuple after route/policy changes to avoid stale session state
EXPECTED RESULT
Document every disruptive command.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
189 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S189
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Reproduce once and freeze the test definition; Predict path using route, policy and overlay state; Collect minimally invasive state/output; Name the failed decision and proposed change; Apply approved change; retest; restore injected fault baseline
Instructor demonstration / expected result: Document every disruptive command.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Capstone workflow: localize before remediation” before showing the answer.

## Slide 186
186
Capstone resolution criteria are observable
• Expected route/member/tunnel selected
• Correct policy/VIP/NAT and security profile applied
• Bidirectional packets and session byte counters increase
• Application succeeds without Conserve Mode or abnormal resource trend
• Rollback remains available and intentional faults are removed
ILLUSTRATIVE SCENARIO
“Ping works” is not sufficient for HTTPS success
EXPECTED RESULT
Debrief explains why each misleading clue did not prove the path.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
190 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S190
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Expected route/member/tunnel selected; Correct policy/VIP/NAT and security profile applied; Bidirectional packets and session byte counters increase; Application succeeds without Conserve Mode or abnormal resource trend; Rollback remains available and intentional faults are removed
Instructor demonstration / expected result: Debrief explains why each misleading clue did not prove the path.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Capstone resolution criteria are observable” before showing the answer.

## Slide 187
187
Capstone checkpoint: policy and NAT
Student exercise—record the command or log field that answers each question
187
01
Which policy ID should match the test tuple?
02
Is NAT required, and what should the translated tuple be?
03
Which traffic-log fields distinguish deny, accept and security-profile action?
LESSON
Do not reveal the injected fault; require the team to connect each conclusion to the actual lab state.
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S191
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Expected result: route and tunnel are healthy; debug/log shows deny or wrong policy/service; Fix: restore intended lab object/policy order/action; Retest: new HTTPS tuple matches intended policy and logs accept; Debrief: route reachability did not imply policy permission
Instructor demonstration / expected result: Answer key belongs in notes; visible slide shows state/output structure.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Instructor answer key: policy fault” before showing the answer.

## Slide 188
188
Capstone checkpoint: route and VPN
Student exercise—record the command or log field that answers each question
188
01
Which route should win for the protected destination?
02
Are Phase 2 selectors reciprocal?
03
Which encap/decap pattern identifies the failing direction?
LESSON
Do not reveal the injected fault; require the team to connect each conclusion to the actual lab state.
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S192
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Expected result: policy is plausible but route selects wrong interface or Phase 2 counters are one-sided; Fix: restore exact lab route or reciprocal selector/return route; Retest: tunnel counters increase both directions and session uses tunnel; Debrief: Phase 1 up did not prove the protected subnet path
Instructor demonstration / expected result: No production route manipulation.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Instructor answer key: route/VPN fault” before showing the answer.

## Slide 189
189
Capstone checkpoint: SD-WAN and resources
Student exercise—record the command or log field that answers each question
189
01
Which rule and SLA should select the egress member?
02
Does a new session use the expected member/NAT address?
03
Are CPU, memory or Conserve Mode affecting the result?
LESSON
Do not reveal the injected fault; require the team to connect each conclusion to the actual lab state.
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S193
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Expected result: rule/SLA selects degraded member, or instructor snapshot shows memory protection event; Fix: correct lab SLA target/rule or apply scoped resource mitigation per runbook; Retest: new session uses healthy member; memory remains stable below recovery threshold; Debrief: link-up and role state were incomplete state/output
Instructor demonstration / expected result: Do not intentionally drive a shared unit into Conserve Mode.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Instructor answer key: SD-WAN/resource fault” before showing the answer.

## Slide 190
190
Operational escalation package makes support efficient
• State model, exact FortiOS build and topology
• Give timestamps, timezone, symptom and reproduction
• Include filtered diagnostics and before/after change record
• Remove credentials/private data and identify business impact
ILLUSTRATIVE SCENARIO
A timestamped, reproducible diagnostic bundle is more useful than a long unfiltered debug
EXPECTED RESULT
Follow organizational and Fortinet support data-collection guidance.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
194 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [OPTIONAL DEEP DIVE] Stable ID: D4-B16-S194
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: State model, exact FortiOS build and topology; Give timestamps, timezone, symptom and reproduction; Include filtered diagnostics and before/after change record; Remove credentials/private data and identify business impact
Instructor demonstration / expected result: Follow organizational and Fortinet support data-collection guidance.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Operational escalation package makes support efficient” before showing the answer.

## Slide 191
191
Integrated capstone
191
01
Define tuple and symptom
02
Check route/overlay
03
Check policy/NAT/session
04
Check profiles/resources
05
Apply one reversible fix
EXPECTED RESULT
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
LESSON
Each step names a FortiGate state or packet change that can be checked directly; stop when the failed step is identified.
Notes: [CORE LECTURE] Stable ID: D4-B16-S195
Approximate timing: 7–9 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Teams receive symptom plus one or two declared achievable faults; They predict expected path and collect route/policy/session/overlay/resource state/output; They propose one reversible change; They prove restoration and remove intentional faults; Class compares state/output quality and false leads
Instructor demonstration / expected result: Instructor selects fault set based on actual lab resources.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Integrated triage rehearsal” before showing the answer.

## Slide 192
192
Common mistakes—and how to correct them
192
MISTAKE
CORRECTION — AND WHY IT HELPS
Change policy, route and tunnel together
Change one layer at a time with rollback; otherwise the causal fix is unknown.
Restart before recording the failure
Capture route/session/protocol/resource state first; restart destroys transient clues.
Use FGVM results as appliance capacity data
Use model data sheets and representative appliance testing; VM results do not prove ASIC capacity.
LESSON
A correction changes a concrete configuration, test or interpretation—not merely the wording used to describe it.
Notes: [CORE LECTURE] Stable ID: D4-B16-S196
Approximate timing: 4 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Instructor demonstration / expected result: Record the smallest safe test that separates the competing explanations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Common mistakes change the state/output pattern” before showing the answer.

## Slide 193
193
Troubleshooting workflow: narrow the failed decision
01
Define tuple/time/symptom
02
Check route/PBR/SD-WAN/VPN state
03
Check policy/NAT/session/logs
04
Check packet direction and security profile
05
Check CPU/memory/Conserve events and validate one reversible fix
What to observe
• Check policy/NAT/session/logs
• Check packet direction and security profile
• Check CPU/memory/Conserve events and validate one reversible fix
INSTRUCTOR DEMONSTRATION
Preserve timestamps and before/after state; stop/reset debug operations.
If debug is used, filter by the test tuple and disable/reset it immediately after capture.
197 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S197
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Define tuple/time/symptom; Check route/PBR/SD-WAN/VPN state; Check policy/NAT/session/logs; Check packet direction and security profile; Check CPU/memory/Conserve events and validate one reversible fix
Instructor demonstration / expected result: Preserve timestamps and before/after state; stop/reset debug operations.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Troubleshooting workflow: narrow the failed decision” before showing the answer.

## Slide 194
194
Practical handoff: predict, observe, explain
• Prerequisite: Read-only performance access
• Prerequisite: Baseline or instructor-provided metrics
• Goal: Run the integrated capstone with one or two achievable lab faults. Required evidence: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
• EXPECTED RESULT:
• Debrief: compare the prediction with the actual command/log result; restore intentional changes
ILLUSTRATIVE SCENARIO
Run the integrated capstone with one or two achievable lab faults. Required evidence: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
EXPECTED RESULT
Instructor confirms resources and environment-specific placeholders before the exercise.
Expected observation
The team identifies the failed decision, applies one reversible fix, and the application succeeds with stable resources.
198 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S198
Approximate timing: 2–3 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Prerequisite: Read-only performance access; Prerequisite: Baseline or instructor-provided metrics; Goal: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.; Expected state/output: configuration/state plus traffic or log proof; Debrief: compare prediction with state/output; restore intentional changes
Instructor demonstration / expected result: Instructor confirms resources and environment-specific placeholders before the exercise.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Discussion prompt: Ask learners to predict the state/output for “Practical handoff: predict, observe, explain” before showing the answer.

## Slide 195
195
Knowledge check — explain the result
QUESTION 1
• What is the first deliverable in the capstone?
QUESTION 2
• When is the incident resolved?
KEY DISTINCTION
Answers and teaching rationale are in speaker notes.
199 • DAY 4 • BLOCK 16 • Performance, Troubleshooting & Capstone
Notes: [CORE LECTURE] Stable ID: D4-B16-S199
Approximate timing: 5–7 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: What is the first deliverable in the capstone?; When is the incident resolved?
Instructor demonstration / expected result: Require a reason or command or log field, not only a one-word answer.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Knowledge check answer key:
Q: What is the first deliverable in the capstone?
A: A precise symptom/test definition: timestamp, five-tuple, expected path and success criterion.
Q: When is the incident resolved?
A: When the intended path/policy/overlay is proven, bidirectional application traffic succeeds, resources are stable and injected faults are removed with rollback retained.

## Slide 196
COURSE WRAP-UP
Operate from packet state, logs and protocol state
A complete diagnosis connects packet fields to route, policy, session, overlay, inspection and resource state.
01
Every block includes theory, a worked mechanism, mistakes, troubleshooting, practical handoff and knowledge check
02
Advanced coverage completes BGP, IPsec/ADVPN, VPN validation, FortiClient/EMS, HA, SD-WAN and performance
03
Optional deep dives are marked in notes; practice time is protected
04
Instructor validates FortiOS 7.6.7 build, platform, licensing and lab topology before delivery
Final Q&A • capstone debrief • remove intentional faults • retain diagnostics and rollback
Notes: [CORE LECTURE] Stable ID: D4-B16-S200
Approximate timing: 5–10 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Every block includes theory, worked state/output, mistakes, troubleshooting, practical handoff and knowledge check; Advanced coverage completes BGP, IPsec/ADVPN, VPN validation, FortiClient/EMS, HA, SD-WAN and performance; Optional deep dives are marked in notes; practice time is protected; Instructor validates FortiOS 7.6.7 build, platform, licensing and lab topology before delivery
Instructor demonstration / expected result: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Changing policy, route and tunnel simultaneously; Clearing sessions or restarting before preserving state/output; Using a VM result to claim appliance offload/capacity
Practical handoff: Run the integrated capstone with one or two achievable lab faults. Required state/output: symptom, expected path, failed decision, reversible fix, bidirectional proof and resource sanity check. Debrief removes every intentional fault.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: System performance; Sessions; Hardware acceleration; Conserve Mode; SSL inspection; Troubleshooting. Exact model hardware guide, CLI Reference and release notes required.
Knowledge check answer key:
Q: What state/output chain should a FortiGate administrator build?
A: Tuple/time → route/PBR/SD-WAN/VPN → policy/NAT/session → packet/log/profile → CPU/memory state.
Q: What remains to be confirmed before delivery?
A: Exact FortiOS 7.6.x build, platform/model, feature support, licensing and actual lab resources.

## Slide 197
FortiGate Foundations + Advanced | Lab: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
197
Instructor preparation: what changed in version 1.3
RESEQUENCED
Two Foundations days followed by two Advanced days; basic routing precedes policy/NAT dependencies and dynamic routing.
REWRITTEN
Generic objectives replaced by topic facts, worked traffic, corrections and troubleshooting.
ADDED
FortiLink, hardware planes/offload, Conserve Mode, expanded OSPF/BGP, IPsec/ADVPN, EMS, HA, SD-WAN and capstone.
PRESERVED
Editable PowerPoint, existing red/navy visual language, widescreen aspect ratio and proportionate optional authentication context in notes.
CHANGE SUMMARY
INSTRUCTOR APPENDIX
Notes: [CORE LECTURE] Stable ID: D1-B01-S004
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Two Foundations days followed by two Advanced days; basic routing precedes policy/NAT dependencies and dynamic routing.; Generic objectives replaced by topic facts, worked traffic, decision state/output, mistakes and troubleshooting.; FortiLink, hardware planes/offload, Conserve Mode, expanded OSPF/BGP, IPsec/ADVPN, EMS, HA, SD-WAN and capstone.; Editable PowerPoint, existing red/navy visual language, widescreen aspect ratio and proportionate optional authentication context in notes.
Instructor demonstration / expected result: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Change summary” before showing the answer.
Instructor-only production information. Do not present during student delivery.

## Slide 198
FortiGate Foundations + Advanced | Lab: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
198
Use the declared Azure lab baseline—and distinguish physical-appliance theory
DECLARED LAB BASELINE
• FortiOS 7.6.7
• Azure FortiGate-VM for all hands-on labs
• Physical appliance NP/CP and FGCP remain theory/demo
• Instructor still confirms optional HA, FortiSwitch, EMS and dual-WAN resources
SAFE LAB BOUNDARIES
• Use placeholders until mappings are supplied
• Filter and stop/reset all debug
• Treat session clearing, restore and firmware changes as disruptive
• Do not drive shared equipment into Conserve Mode
OPTIONAL CONTEXT
• LDAP/RADIUS/FSSO details retained as optional discussion in identity/policy notes
• Appliance ASIC and FGCP tasks are theory/demo unless separate hardware exists
• Licensing claims require current contract/product documents
KEY DISTINCTION
No deployed resource, entitlement, credential, interface mapping or successful result is assumed.
ASSUMPTIONS + VALIDATION
INSTRUCTOR APPENDIX
Notes: [CORE LECTURE] Stable ID: D1-B01-S005
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: FortiOS 7.6.7; Azure FortiGate-VM lab platform; FortiClient/EMS versions and licensing; Available HA, FortiSwitch, dual-WAN and VPN resources; Use placeholders until mappings are supplied; Filter and stop/reset all debug; Treat session clearing, restore and firmware changes as disruptive; Do not drive shared equipment into Conserve Mode; LDAP/RADIUS/FSSO details retained as optional discussion in identity/policy notes; ASIC, cloud HA and EMS live tasks are demonstrations unless prerequisites exist; Licensing claims require current contract/product documents
Instructor demonstration / expected result: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Assumptions and validation” before showing the answer.
Instructor-only production information. Do not present during student delivery.

## Slide 199
FortiGate Foundations + Advanced | Lab: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
199
Coverage matrix — blocks 1–8
Final slide ranges are stable in this revised 200-slide deck
# | DAY | SLIDES | BLOCK
1 | 1 | 4–13 | Network Foundations & FortiGate Packet Flow
2 | 1 | 14–23 | FortiGate Introduction & Initial Configuration
3 | 1 | 24–33 | Segmentation, Zones & Firewall Policy Design
4 | 1 | 34–43 | NAT, Logging & CLI Troubleshooting
5 | 2 | 44–53 | Routing Fundamentals & Route Selection
6 | 2 | 54–63 | Object Management & Policy Design Best Practices
7 | 2 | 64–73 | Security Services & SSL Inspection
8 | 2 | 74–82 | FortiGate Hardware Architecture, Monitoring & Operations
COVERAGE MATRIX • BLOCKS 1–8
INSTRUCTOR APPENDIX
Notes: [CORE LECTURE] Stable ID: D1-B01-S006
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Block 1: slides 8–17; Block 2: slides 18–27; Block 3: slides 28–37; Block 4: slides 38–47; Block 5: slides 48–57; Block 6: slides 58–67; Block 7: slides 68–77; Block 8: slides 78–86
Instructor demonstration / expected result: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Coverage matrix 1-8” before showing the answer.
Instructor-only production information. Do not present during student delivery.

## Slide 200
FortiGate Foundations + Advanced | Lab: FortiOS 7.6.7 on Azure FortiGate-VM • physical appliance theory included
200
Coverage matrix — blocks 9–16
Final slide ranges are stable in this revised 200-slide deck
# | DAY | SLIDES | BLOCK
9 | 3 | 83–92 | Route Selection, PBR & OSPF
10 | 3 | 93–105 | BGP Fundamentals & Practical Use
11 | 3 | 106–118 | IPsec VPN Architecture & ADVPN
12 | 3 | 119–131 | VPN Troubleshooting & Operational Validation
13 | 4 | 132–144 | FortiClient Architecture & EMS Awareness
14 | 4 | 145–157 | FortiGate High Availability Fundamentals
15 | 4 | 158–171 | Fortinet SD-WAN & Design Considerations
16 | 4 | 172–195 | Performance Optimization, Advanced Troubleshooting & Capstone
COVERAGE MATRIX • BLOCKS 9–16
INSTRUCTOR APPENDIX
Notes: [CORE LECTURE] Stable ID: D1-B01-S007
Approximate timing: 4–6 minutes. Protect the block’s practical/discussion reserve; skip optional slides when time is short.
Explanation: Block 9: slides 87–96; Block 10: slides 97–109; Block 11: slides 110–122; Block 12: slides 123–135; Block 13: slides 136–148; Block 14: slides 149–161; Block 15: slides 162–175; Block 16: slides 176–199
Instructor demonstration / expected result: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Illustrative topology note: addresses and interface names are documentation examples only. Replace <port>, <peer>, <policy-id>, <VDOM> and lab-specific values before class.
Typical mistakes to surface: Treating DNS success as proof of end-to-end reachability; Assuming destination port proves the application; Looking at policy without checking route/return path
Practical handoff: Learners predict and then trace one illustrative TCP flow. Prerequisite: reachable lab FortiGate or instructor demonstration; state/output: route, policy ID, session tuple and bidirectional packets.
Official reference for instructor preparation: FortiGate/FortiOS 7.6.7 Administration Guide: Life of a packet; Sessions; Debugging the packet flow. CLI syntax cross-check: FortiOS 7.6.7 CLI Reference.
Discussion prompt: Ask learners to predict the state/output for “Coverage matrix 9-16” before showing the answer.
Instructor-only production information. Do not present during student delivery.